## Slide 1: Volte Drive Test Report

## Slide 2: DT Scénario
Short Call (10s)
Long call (2min)
Scanner

## Slide 3: Voice Call

## Slide 4
RAT distribution
Long call
Short call

## Slide 5
EARFCN distribution
Long call
Short call

## Slide 6
LTE - RSRP
Long call
Short call
Average [dBm]
-79,53
Average [dBm]
-80,67

## Slide 7
LTE- RSRQ
Long call
Short call

## Slide 8
LTE-SINR
Long call
Short call

## Slide 9: MO Call Setup Time (call setup time in VoLTE)
Call Setup Time IMS Voice |  | 
Average (Sec) | Maximum (Sec) | Minimum (Sec)
2,55 | 4,07 | 1,84
Short call

## Slide 10: MO Handover Type
Long call
HO Type | Percentage [%]
LTE Inter-Frequency handover | 3,38%
LTE Intra-Frequency handover | 96,62%
Handover KPI’s | 
Handover Attemps | 266
Handover Success | 265
Handover succès Rate | 99,62%
Étiquettes de lignes | LTE FDD_1800 | LTE FDD_2100 | LTE FDD_800 | Total général
LTE FDD_1800 | 83 | 1 | 2 | 86
LTE FDD_2100 | 2 | 113 | 2 | 117
LTE FDD_800 | 1 | 1 | 61 | 63
Total général | 86 | 115 | 65 | 266

## Slide 11: MO Voice Stats (VoLTE call stats)
Long call
Voice KPIs | 
Number Call Attempts | 51
Number Dropped Calls | 0
Call Drop Rate (%) | 0%
HO success rate | 99,62%

## Slide 12: MO Voice Stats (VoLTE call stats)
Voice KPIs | 
Number Call Attempts | 293
Number Call Setup | 292
Number Blocked Calls | 1
Setup Succes Rate (%) | 99,66%
Call Block Rate (%) | 0,34%
Call Setup Time IMS Voice Average (Sec) | 2,55
Short call

## Slide 13: MO Voice Stats (VoLTE call stats)
KPIs | 
VoLTE Call Setup SR | 99,66%
Call Setup Time | 2,55
VoLTE Drop Call Rate | 0%
Speech Quality - MOS (% of the samples >3,5) | 93,43
Average MOS | 4,18
VoLTE Handover SR | 99,62%
VoLTE SRVCC SR | -

## Slide 14: MO Voice Call - Blocked call
Short call

## Slide 15: MO Voice Quality Metrics
long Call

## Slide 16: Scanner_RSRP
L2100

## Slide 17: Scanner_RSRP
L800

## Slide 18: Scanner_RSRP
L1800

## Slide 19: Scanner_RSCP
U2100

## Slide 20: Scanner_RSCP
900