## Slide 1
Network QoS
ALLADA Intermediate report
November 22nd, 2023

## Slide 2: Summary
Drive tests Activity, Current Status & Progress | 12
Executive Summary | 15
Benchmarking Key Results | 21
Benchmarking Coverage | 26
Benchmarking Voice Service | 33
Benchmarking Data Service | 48
Next Steps | 63

## Slide 3
Introduction: Scope of Intermediate Report
01

## Slide 4: Intermediate report
Scope of this report
  1. Network benchmarking results for the ALLADA area between MTN, MOOV, and CELTISS from September 9th to September 13th, 2023..

## Slide 5
Benchmarking Executive Summary
02

## Slide 6: Executive Summary – Benchmarking coverage 2G/3G/4G
Coverage 2G/3G/4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
MTN, MOOV, and CELTISS have similar 2G coverage, All of them satisfy the ARCEP requirements
MTN and MOOV failed to satisfy the ARCEP 3G Coverage requirements
Only MOOV reach the ARCEP 4G coverage thresholds. MTN and CELTISS failed in Incar &Indoor 4G coverage
Tune and align power settings mainly in 3G/4G. Actual setting may impact the coverage strength specially at Indoor locations
Review the design at the coverage and quality blackspots
We highlight that 4G ARCEP coverage Thresholds are aggressive

## Slide 7: Executive Summary – Benchmarking voice service 2G/3G
Voice service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
MTN is ranked first in voice accessibility and It’s the only operator that satisfied the blocking rate ARCEP requirement
All operators satisfy the retainability ARCEP thresholds
All operators met the MOS ARCEP thresholds however MOOV and CELTISS have better average MOS
Voice quality is always better in 3G due to its better codec rate , we recommend to push as much as possible the voice traffic to 3G.
Actual selection/reselection/Irat parameters need to be reviewed and aligned.
2G Full Rate/Half Rate settings need to be tuned in order to improve Full rate penetration

## Slide 8: Executive Summary – Benchmarking SMS service
SMS service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
MTN and MOOV fail in SMS service due to the delivery time exceeding 6s
There is no issue in radio accessibility that could be correlated to the SMS high delivery time.
End to End investigation need to be performed to analyses the high delivery time including mainly Core/SMS parts: SM Sserver...

## Slide 9: Executive Summary – Benchmarking 4G Data service
Data service 4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 4G data service, and all operators met ARCEP's requirements.
MTN is ranked first in Both DL and UL of 4G ftp tests, with 46.17/16.42Mbps DL/UL Throughput compared to 24.82/13.85 Mbps and 13/11.9 Mbps for MOOV and CELTISS.
MTN spectrum need to be used with a better efficiency, Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles

## Slide 10: Executive Summary – Benchmarking 3G Data service
Data service 3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 3G data service, and all operators met ARCEP's requirements except MOOV in Web failure Rate
MTN is in 2nd position for 3G DL throughput with 3.5Mbps, compared to 9.46Mbps for CELTISS and 4Mbps for MOOV.
MTN is ranked first in term of 3G UL throughput with 1.78 Mbps against 1.16 Mbps for MOOV and 2.18Mbps for CELTISS,
Its recommended to push as much as possible the data traffic to 4G in order to:
- Improve end user perception, Both DT and stats are showing that users in average are served with up to 700% better throughput in 4G than in 3G
- Offload the 3G network which will improve the 3G throughput and the 3G radio quality
Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles

## Slide 11
Benchmarking Key Results
03

## Slide 12: Benchmarking Key Results – Coverage MTN, MOOV, and CELTISS have similar2G coverage, All of them satisfy the ARCEP requirements MTN and MOOV failed to satisfy the ARCEP 3G Coverage requirements Only MOOV reach the ARCEP 4G coverage thresholds. MTN and CELTISS failed in Incar &Indoor 4G coverage
KPI |  | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
2G Coverage Rate | Incar | More than 90% with Incar: Rxlev >-87 dBm | 99,16% | OK | 99,77% | OK | 99,95% | OK | 3
 | Outdoor | More than 90% with Outdoor: Rxlev >-92 dBm | 99,84% | OK | 100% | OK | 100% | OK | 3
 | Indoor | More than 90% with Outdoor: Rxlev >-74 dBm | 90,80% | OK | 90,02% | OK | 91,41% | OK | 2
3G Coverage Rate | Incar,Indoor,Outdoor | More than 90% with RSCP <-85 dBm | 86,47% | NOK | 84,84% | NOK | 94,74% | OK | 2
4G Coverage Rate | Incar | More than 90% with RSRP <-90 dBm* | 84,48% | NOK | 97,4% | OK | 77,24% | NOK | 2
 | Outdoor | More than 90% with RSRP <-95 dBm* | 96,68% | OK | 99,92% | OK | 92,55% | OK | 2
 | Indoor | More than 90% with RSRP <-78 dBm* | 24,54% | NOK | 81,40% | OK | 44,23% | NOK | 3

## Slide 13: Benchmarking Key Results – 2G/3G voice and SMS Summary MTN is ranked first in voice accessibility and It’s the only operator that satisfied the blocking rate ARCEP requirement All operators satisfy the retainability ARCEP thresholds All operators met the MOS ARCEP thresholds however MOOV and CELTISS have better average MOS MTN and MOOV fail in SMS service due to the delivery time exceeding 6s
KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  | Value | Conformity | Value | Conformity | Value | Conformity | 
Accesibility: Blocking rate | <1% | 0,61% | OK | 1,29% | NOK | 1,17 | NOK | 1
Retainability: Call drop rate | <1% | 0,71% | OK | 0,84% | OK | 0,41% | OK | 2
Call Completetion Rate (%) | =<99% | 98,87% | NOK | 98,03% | NOK | 98,94% | NOK | 1
Integrity: Voice quality | Note requise> 2,8 | 3,79 | OK | 3,95 | OK | 3,91 | OK | 3
SMS sending success rate % (E2E delivery Time<6 sec) | >99% | 96,34% | NOK | 93,73% | NOK | 99,67% | OK | 2
SMS receving success rate % | >99% | 96,14% | NOK | 91,10% | NOK | 99,36% | OK | 2

## Slide 14: Benchmarking Key Results – 3G Data Summary All operators met the 3G Data ARCEP requirements except MOOV in Web failure Rate
Services | KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
3G HTTP | Successful internet connexion rate | >96% | 97,44% | OK | 98,59% | OK | 97,10% | OK | 2
 | Connexion setup time | <=10sec | 5,35 | OK | 7,01 | OK | 6,49 | OK | 1
 | Web service failure rate | <3% | 0,69% | OK | 3,56% | NOK | 0% | OK | 2
3G FTP | FTP failure rate UL/DL | <3 % | 0%/0,45% | OK | 0,47%/0% | OK | 0,48%/0,5% | OK | 1
 | FTP Data transmission average (DL) | >= 2Mbps | 5,344 | OK | 4,071 | OK | 9,461 | OK | 2
 | FTP Data transmission average (UL) | >= 1Mbps | 2,002 | OK | 1,159 | OK | 2,186 | OK | 2

## Slide 15: Benchmarking Key Results – 4G Data Summary All operators met the 4G Data ARCEP requirements. MTN is ranked first in 4G FTP DL and UL tests
Services | KPI | Threshorlds* | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
4G HTTP Browsing | Web service failure rate (%) | <3% | 0% | OK | 0% | OK | 0% | OK | 1
 | Connexion setup time | <=3sec | 1,15 | OK | 0,83 | OK | 1,23 | OK | 2
4G FTP | FTP failure rate UL/DL | <3 % | 0%/0,43% | OK | 0%/0% | OK | 0%/0% | OK | 3
 | FTP Data transmission average (DL) | 4G >= 5 Mbps | 46,172 | OK | 24,826 | OK | 12,997 | OK | 1
 | FTP Data transmission average (UL) | 4G: >= 2Mbps | 16,624 | OK | 13,955 | OK | 11,903 | OK | 1

## Slide 16
Benchmarking 2G/3G/4G coverage
04

## Slide 17: Benchmarking: 2G coverage MTN, MOOV and CELTISS’s 2G coverage met the ARCEP RxLev thresholds.
Chart: RxLev Distribution (%)
| Indoor>-74 | Incar >-87 | Outdoor >-92
MTN | 0.908 | 0.9916 | 0.9984
MOOV | 0.9002 | 0.9977 | 1
CELTISS | 0.9141 | 0.9995 | 1

## Slide 18: Benchmarking: 2G coverage - Maps 2G coverage plots are quite similar for the 3 operators

## Slide 19: Benchmarking: 3G coverage MTN and MOOV failed to satisfy the ARCEP 3G Coverage requirements
Chart: RSCP Distribution (%)
| Indoor,Incar,Outdoor >-85
MTN | 0.8647
MOOV | 0.8484
CELTISS | 0.9474

## Slide 20: Benchmarking: 3G coverage-Maps CELLTIS have the best 3G coverage distribution

## Slide 21: Benchmarking: 4G coverage Only MOOV reach the ARCEP 4G coverage thresholds. MTN and CELTISS failed in Incar &Indoor 4G coverage
Chart: RSRP Distribution (%)
| Indoor > -78 | Incar > -90 | Outdoor > -95
MTN | 0.2454 | 0.8448 | 0.9668
MOOV | 0.814 | 0.974 | 0.9992
CELTISS | 0.4423 | 0.7722 | 0.9255

## Slide 22: Benchmarking – 4G coverage - Maps MOOV have the best 4G coverage distribution

## Slide 23
Benchmarking voice service
05

## Slide 24: Benchmarking: CS Accessibility 2G/3G BLOCKED CALLS MTN is ranked first in voice accessibility and It’s the only operator that satisfied the blocking rate ARCEP requirement
Chart: Call Blocked Rate (%)
| CBR (%)
MTN | 0.0061
MOOV | 0.0129
CELTISS | 0.0117
Chart: Call Blocked Rate per Technology (%)
| CBR (%)
MTN 2G | 0
MTN 3G | 0.0078
MOOV 2G | 0
MOOV 3G | 0.0148
CELTISS 2G | 0.0284
CELTISS 3G | 0.0094

## Slide 25: Benchmarking: CS Integrity Voice quality Mean Opinion Score MTN have the best ratio of excellent and good Voice Quality samples
Chart: Average MOS
| Avrege MOS
MTN | 3.79
MOOV | 3.95
CELTISS | 3.91
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Excel+Goog
MTN | 0.1385 | 0.8384 | 0.0136 | 0.0094 | 0.9769
MOOV | 0.5488 | 0.4059 | 0.0215 | 0.0238 | 0.9547
CELTISS | 0.5763 | 0.411 | 0.0095 | 0.0032 | 0.0017

## Slide 26: Benchmarking: CS Retainability 2G/3G DROPPED CALLS All operators satisfy the retainability ARCEP thresholds
Chart: Call Drop Rate (%)
| CDR (%)
MTN | 0.0071
MOOV | 0.0084
CELTISS | 0.0041

## Slide 27: Benchmarking Voice service Band usage(%) Voice calls are mainly carried by 3G for all operators. MTN's 2G band usage: 87,69% GSM 900 and 12,31% DCS 1800 Mhz, 30,1 % of MTN 3G CS traffic is carried on U900 compared to 81,38% and 12,15% for MOOV and CELTISS.
Chart: System Technology usage(%)
| GSM | UMTS
MTN | 0.0168 | 0.9832
MOOV | 0.0012 | 0.9988
CELTISS | 0.0208 | 0.9792
Chart: 2G band usage(%)
| GSM 900 | GSM 1800
MTN | 0.8769 | 0.1231
MOOV | 0.75 | 0.25
CELTISS | 0.7759 | 0.2241
Chart: 3G band usage(%)
| UMTS 900 | UMTS 2100
MTN | 0.301 | 0.699
MOOV | 0.8138 | 0.1862
CELTISS | 0.12149 | 0.8785

## Slide 28: Benchmarking – CS Integrity Voice quality maps (MOS) MTN have less than 1% of MOS samples lower than 2.2, Values lower than 2,2 pose risk of bad users perceived voice quality 3d

## Slide 29: Benchmarking: Radio parameters EC/NO comparison CELLTIS have the best 3G EcNo samples within acceptable range
Chart: Ec/No Distribution (%)
| -8 to 0 | -12 to -8 | -16 to -12 | -34 to -16 | ACCEPTABLE EC/N0
MTN | 0.2285 | 0.3202 | 0.3897 | 0.0616 | 0.5487
MOOV | 0.1384 | 0.3213 | 0.4809 | 0.0595 | 0.4597
CELTISS | 0.7463 | 0.1762 | 0.0506 | 0.0269 | 0.9225

## Slide 30: Benchmarking: Radio parameters EC/NO CELLTIS have the best 3G EcNo samples distribution

## Slide 31: Benchmarking – SINR comparison Drive tests are showing that MTN have the best acceptable level range of SINR
Chart: SINR Comparison
| (Min,-4) | (-4,0) | (0,7) | (7,15 <) | ACCEPTABLE SINR
MTN | 0.005 | 0.0152 | 0.0676 | 0.9122 | 0.9798
MOOV | 0.0065 | 0.034 | 0.1487 | 0.8108 | 0.9595
CELTISS | 0.0141 | 0.0228 | 0.1119 | 0.8512 | 0.9631

## Slide 32: Benchmarking – SNIR comparison map 4G MTN have a better quality of signal compared to CELTISS and MOOV

## Slide 33: Benchmarking – 2G/3G CALL SETUP TIME MTN have the best Call setup time.
Chart: Call Setup Time (s)
| Call Setup Time
MTN | 5.7
MOOV | 7.38
CELTISS | 7.65

## Slide 34: Benchmarking – CALL SETUP TIME/Call Mode MTN have the best 4G CSBF Call setup Time, Call setup time 2G is higher than in 3G/4G.
Chart: CS Call setup Time by technology (s)
| 4G CSFB CST | 3G CST | 2G CST
MTN | 5.4 | 5.75 | 6.09
MOOV | 6.97 | 7.62 | 7.55
CELTISS | 7.07 | 8.35 | 8.13

## Slide 35: Benchmarking – SMS SENDING FAILURE
Chart: SMS
| SMS Sending message success rate (%) | SMS Receving message success rate (%)
MTN | 0.9634 | 0.9514
MOOV | 0.9373 | 0.911
CELTISS | 0.9967 | 0.9936
Chart: SMS Send Time(%)
| (0,3) | (3,6) | >6
MTN | 0.4439 | 0.5225 | 0.0336
MOOV | 0.4054 | 0.532 | 0.0626
CELTISS | 0.4751 | 0.5216 | 0.0033
MTN and MOOV fail in SMS service due to the delivery time exceeding 6s

## Slide 36
Benchmarking Data service
06

## Slide 37: Benchmarking – DATA 3G All operators have a acceptable rate of successful Internet connection
Chart: PS Attach & PDP Contex Act(%)
| PS Attach success(%) | PDP Context Act Success (%)
MTN | 0.9744 | 0.9901
MOOV | 0.9859 | 0.9887
CELTISS | 0.971 | 0.9877
Chart: Attach & PDP Activation Time (s)
| PS Attach Setup Time | PDP Context Act Time
MTN | 1.66 | 1.88
MOOV | 1.9 | 1.97
CELTISS | 1.64 | 1.91

## Slide 38: Benchmarking – DATA 3G MOOV failed in http browsing SR
Chart: PS Connection setup time
| PS Connection setup time
MTN | 5.35
MOOV | 7.01
CELTISS | 6.49
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9931
MOOV | 0.9644
CELTISS | 1

## Slide 39: Benchmarking – DATA 3G All operators have good downlink and uplink FTP success rate
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 1 | 0.9955
MOOV | 0.9953 | 1
CELTISS | 0.9952 | 0.995

## Slide 40: Benchmarking – 3G FTP MEAN THROUGHPUT All operators met the ARCEP downlink and uplink FTP success rate thresholds
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 5344.28 | 2002.72 | 14313.8 | 12478.99
MOOV | 4071.6 | 1159.53 | 10514.01 | 0
CELTISS | 9464.71 | 2186.94 | 14187.27 | 9458.83
MTN FTP DL AVERAGE Throughout is ranked second
MTN FTP UL AVERAGE Throughout isranked second

## Slide 41: Benchmarking – 3G FTP MEAN THROUGHPUT comparison map All samples exceed 2Mbps

## Slide 42: Benchmarking – 4G HTTP Browsing All operators have a very good HTTP Browsing success rate.
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 1
MOOV | 1
CELTISS | 1

## Slide 43: Benchmarking – 4G FTP THROUGHPUT comparison All operators have a very good FTP success rate.
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 1 | 0.9957
MOOV | 1 | 1
CELTISS | 1 | 1

## Slide 44: Benchmarking – 4G FTP THROUGHPUT comparison MTN have the best average FTP throuhjpun in both DL and UL.
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 46172.72 | 16624.74 | 177456.54 | 31484.63
MOOV | 24826.97 | 13955.81 | 198254.08 | 42328.41
CELTISS | 12997.57 | 11903.43 | 28803.17 | 14455.73

## Slide 45: Benchmarking – 4G FTP THROUGHPUT comparison map MTN Shows the best 4G FTP throughput samples distribution.

## Slide 46: Benchmarking – BAND and TECHNOLOGY UTILISATION Most of MTN LTE samples are in 2600 band. Most of CELTIS LTE samples are in 1800 band. Most of MOOV LTE samples are in 800 and 2600 band Usage of 3G U900 is lower for CELTISS
Chart: 3G band Distribution (%)
| UMTS 900 | UMTS 2100
MTN | 0.0955 | 0.9045
MOOV | 0.3474 | 0.6526
CELTISS | 0.0433 | 0.9567
Chart: 4G Band Distribution (%)
| LTE 800 | LTE 700 | LTE 1800 | LTE 2100 | LTE 2600
MTN | 0.0878 | 0.0077 | 0.0659 | 0 | 0.8387
MOOV | 0.5036 | 0 | 0 | 0 | 0.4964
CELTISS | 0.2883 | 0 | 0.7117 | 0 | 0

## Slide 47: Benchmarking – Data TECHNOLOGY Usage(%) MTN have the highest LTE CA Carrier Aggregation usage.
Chart: 3G Packet Technology usage (%)
| DC-HSPA | HSPA | HSDPA | UMTS
MTN | 0.5255 | 0.0278 | 0 | 0.4467
MOOV | 0.2212 | 0.3475 | 0 | 0.4313
CELTISS | 0.3795 | 0.0648 | 0.0121 | 0.5436
Chart: 4G Packet Technology usage (%)
| LTE | LTE CA
MTN | 0.1386 | 0.8614
MOOV | 0.5109 | 0.4891
CELTISS | 0.4535 | 0.5465

## Slide 48
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2023 Deloitte Bénin SARL. Société du réseau Deloitte