## Slide 1
Network QoS
BOHICON Intermediate report
November 21st, 2023

## Slide 2: Summary
Scope of Intermediate Report | 3
Executive Summary | 5
Benchmarking Key Results | 11
Benchmarking Coverage | 16
Benchmarking Voice Service | 23
Benchmarking Data Service | 36

## Slide 3
Introduction: Scope of Intermediate Report
01

## Slide 4: Intermediate report
Scope of this report
  1. Network benchmarking results for the BOHICON area between MTN, MOOV, and CELTISS from September 9th to September 13th, 2023..

## Slide 5
Benchmarking Executive Summary
02

## Slide 6: Executive Summary – Benchmarking coverage 2G/3G/4G
Coverage 2G/3G/4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
All operators met ARCEP 2G coverage obligations and have comparable results.
All operators met ARCEP 3G coverage obligation
MTN is ranked first in 3G coverage
All operators failed to satisfy the ARCEP requirements in terms of Indoor 4G coverage. CELTISS fails in Incar 4G coverage as well
Tune and align power settings mainly in 3G/4G. Actual setting may impact the coverage strength specially at Indoor locations
Review the design at the coverage and quality blackspots
We highlight that 4G ARCEP coverage Thresholds are aggressive

## Slide 7: Executive Summary – Benchmarking voice service 2G/3G
Voice service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
MTN is ranked second in both in voice accessibility and retainability
Only CELTISS satisfies the retainability ARCEP thresholds
All operators met the MOS ARCEP thresholds
MOOV and CELTISS have better average MOS than MTN
Voice quality is always better in 3G due to its better codec rate , we recommend to push as much as possible the voice traffic to 3G.
Actual selection/reselection/Irat parameters need to be reviewed and aligned.
2G Full Rate/Half Rate settings need to be tuned in order to improve Full rate penetration

## Slide 8: Executive Summary – Benchmarking SMS service
SMS service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
All operators failed to meet ARCEP for SMS Send Success with End To End Delivery Time < 6 sec,
MTN have the best SMS results,
There is no issue in radio accessibility that could be correlated to the SMS high delivery time.
End to End investigation need to be performed to analyses the high delivery time including mainly Core/SMS parts: SM Sserver...

## Slide 9: Executive Summary – Benchmarking 4G Data service
Data service 4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 4G data service, and all operators met ARCEP's requirements.
MTN is ranked first in all kinds of 4G data tests, with 37/15,5Mbps DL/UL Throughput compared to 16/9.5 Mbps and 13/14.5 Mbps for MOOV and MTN.
MTN spectrum need to be used with a better efficiency, Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles

## Slide 10: Executive Summary – Benchmarking 3G Data service
Data service 3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 3G data service, and all operators met ARCEP's requirements.
MTN is in 2nd position for 3G DL throughput with 3.5Mbps, compared to 6.5Mbps for CELTISS and 3Mbps for MOOV.
MTN is ranked first in term of 3G UL throughput with 1.78 Mbps against 1.16 Mbps for MOOV and 1.75Mbps for CELTISS,
Its recommended to push as much as possible the data traffic to 4G in order to:
- Improve end user perception, Both DT and stats are showing that users in average are served with up to 700% better throughput in 4G than in 3G
- Offload the 3G network which will improve the 3G throughput and the 3G radio quality
Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles

## Slide 11
Benchmarking Key Results
03

## Slide 12: Benchmarking Key Results – Coverage MTN, MOOV, and CELTISS have similar2G coverage, All of them satisfy the ARCEP requirements MTN is ranked first in 3G coverage where all operators satisfy the ARCEP requirements All operators failed to satisfy the ARCEP requirements in terms of Indoor 4G coverage. CELTISS fails in Incar 4G coverage as well
KPI |  | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
2G Coverage Rate | Incar | More than 90% with Incar: Rxlev >-87 dBm | 99,06% | OK | 99,97% | OK | 99,99% | OK | 3
 | Outdoor | More than 90% with Outdoor: Rxlev >-92 dBm | 99,87% | OK | 100% | OK | 99,99% | OK | 3
 | Indoor | More than 90% with Outdoor: Rxlev >-74 dBm | 95,62% | OK | 94,35% | OK | 93,70% | OK | 1
3G Coverage Rate | Incar,Indoor,Outdoor | More than 90% with RSCP <-85 dBm | 94,35% | OK | 92,33% | OK | 93,62% | OK | 1
4G Coverage Rate | Incar | More than 90% with RSRP <-90 dBm* | 90,42% | OK | 92,55% | OK | 76,75% | NOK | 2
 | Outdoor | More than 90% with RSRP <-95 dBm* | 97,25% | OK | 99,13% | OK | 93,26% | OK | 2
 | Indoor | More than 90% with RSRP <-78 dBm* | 54,17% | NOK | 71,04% | NOK | 24,53% | NOK | 2

## Slide 13: Benchmarking Key Results – 2G/3G voice and SMS Summary MTN is ranked second in both in voice accessibility and retainability Only CELTISS satisfies the retainability ARCEP thresholds All operators met the MOS ARCEP thresholds however MOOV and CELTISS have better average MOS All operators failed in SMS service due to the delivery time exceeding 6s however MTN have the best SMS results
KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  | Value | Conformity | Value | Conformity | Value | Conformity | 
Accesibility: Blocking rate | <1% | 0,53% | OK | 2,11% | NOK | 0,36 | OK | 2
Retainability: Call drop rate | <1% | 1,37% | NOK | 1,57% | NOK | 0% | OK | 2
Call Completetion Rate (%) | =<99% | 98,1% | NOK | 96,32% | NOK | 99,64% | OK | 1
Integrity: Voice quality | Note requise> 2,8 | 3,78 | OK | 4,02 | OK | 3,86 | OK | 3
SMS sending success rate % (E2E delivery Time<6 sec) | >99% | 95,89% | NOK | 85,50% | NOK | 89,60% | NOK | 1
SMS receving success rate % | >99% | 94,12% | NOK | 83,98% | NOK | 87,65% | NOK | 1

## Slide 14: Benchmarking Key Results – 3G Data Summary All operators met the 3G Data ARCEP requirements.
Services | KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
3G HTTP | Successful internet connexion rate | >96% | 100,00% | OK | 99,55% | OK | 98,90% | OK | 1
 | Connexion setup time | <=10sec | 5,91 | OK | 6,07 | OK | 6,10 | OK | 1
 | Web service failure rate | <3% | 1,12% | OK | 0,23% | OK | 1,74% | OK | 2
3G FTP | FTP failure rate UL/DL | <3 % | 1,42%/2,87% | OK | 1,31%/2,74% | OK | 0,42%/0,87% | OK | 3
 | FTP Data transmission average (DL) | >= 2Mbps | 3,506 | OK | 3,089 | OK | 6,459 | OK | 2
 | FTP Data transmission average (UL) | >= 1Mbps | 1,982 | OK | 1,162 | OK | 1,755 | OK | 1

## Slide 15: Benchmarking Key Results – 4G Data Summary All operators met the 4G Data ARCEP requirements. MTN is ranked first in all kinds of 4G data tests
Services | KPI | Threshorlds* | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
4G HTTP Browsing | Web service failure rate (%) | <3% | 1,04% | OK | 1,83% | OK | 2,12% | OK | 1
 | Connexion setup time | <=3sec | 0,97 | OK | 1,09 | OK | 1,33 | OK | 1
4G FTP | FTP failure rate UL/DL | <3 % | 0%/0% | OK | 0%/0,23% | OK | 0,68%/0% | OK | 1
 | FTP Data transmission average (DL) | 4G >= 5 Mbps | 36,956 | OK | 15882 | OK | 12,999 | OK | 1
 | FTP Data transmission average (UL) | 4G: >= 2Mbps | 15,436 | OK | 9,549 | OK | 14,439 | OK | 1

## Slide 16
Benchmarking 2G/3G/4G coverage
04

## Slide 17: Benchmarking: 2G coverage MTN, MOOV and CELTISS 2G coverage met the ARCEP RxLev thresholds.
Chart: RxLev Distribution (%)
| Indoor>-74 | Incar >-87 | Outdoor >-92
MTN | 0.9562 | 0.9906 | 0.9987
MOOV | 0.9435 | 0.9997 | 1
CELTISS | 0.937 | 0.9999 | 0.9999

## Slide 18: Benchmarking: 2G coverage - Maps 2G coverage plots are quite similar for the 3 operators

## Slide 19: Benchmarking: 3G coverage MTN is ranked first in 3G coverage where all operators satisfy the ARCEP requirements
Chart: RSCP Distribution (%)
| Indoor,Incar,Outdoor >-85
MTN | 0.9435
MOOV | 0.9233
CELTISS | 0.9362

## Slide 20: Benchmarking: 3G coverage-Maps 3G coverage plots are quite similar for the 3 operators

## Slide 21: Benchmarking: 4G coverage All operators failed to satisfy the ARCEP requirements in terms of Indoor 4G coverage. CELTISS fails in Incar 4G coverage as well
Chart: RSRP Distribution (%)
| Indoor > -78 | Incar > -90 | Outdoor > -95
MTN | 0.5417 | 0.9042 | 0.9725
MOOV | 0.7104 | 0.9255 | 0.9913
CELTISS | 0.2453 | 0.7675 | 0.9326

## Slide 22: Benchmarking – 4G coverage - Maps MOOV have a better 4G coverage plot distribution MTN and CELTISS.

## Slide 23
Benchmarking voice service
04

## Slide 24: Benchmarking: CS Accessibility 2G/3G BLOCKED CALLS MTN is ranked second in voice accessibility. MOOV failed to satisfy the ARCEP thresholds
Chart: Call Blocked Rate (%)
| CBR (%)
MTN | 0.0053
MOOV | 0.0211
CELTISS | 0.0036
Chart: Call Blocked Rate per Technology (%)
| CBR (%)
MTN 2G | 0.019
MTN 3G | 0.0201
MOOV 2G | 0
MOOV 3G | 0.0211
CELTISS 2G | 0
CELTISS 3G | 0.0036

## Slide 25: Benchmarking: CS Integrity Voice quality Mean Opinion Score MOOV have the best ratio of excellent and good Voice Quality samples MTN needs to improve its voice quality MOS by pushing CS traffic to 3G and increase 2G full rate penetration.
Chart: Average MOS
| Avrege MOS
MTN | 3.78
MOOV | 4.02
CELTISS | 3.86
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Excel+Goog
MTN | 0.4488 | 0.4606 | 0.0663 | 0.0243 | 0.9094
MOOV | 0.8546 | 0.1312 | 0.0067 | 0.0076 | 0.9858
CELTISS | 0.3843 | 0.5997 | 0.0102 | 0.0058 | 0.984

## Slide 26: Benchmarking: CS Retainability 2G/3G DROPPED CALLS Only CELTISS satisfies the retainability ARCEP thresholds
Chart: Call Drop Rate (%)
| CDR (%)
MTN | 0.0137
MOOV | 0.0157
CELTISS | 0

## Slide 27: Benchmarking Voice service Band usage(%) 12% of MTN voice calls is carried by 2G while all voice traffic is carried by 3G for competitors Its recommended for MTN to reduce 2G utilization and increase 3G penetration for better audio quality. MTN's 2G band usage: 76,06% GSM 900 and 23,94% GSM 1800 Mhz, 27,2 % of MTN 3G CS traffic is carried on U900 compared to 12% and 24,5% for MOOV and CELTISS.
Chart: System Technology usage(%)
| GSM | UMTS
MTN | 0.1208 | 0.8792
MOOV | 0 | 1
CELTISS | 0 | 1
Chart: 2G band usage(%)
| GSM 900 | GSM 1800
MTN | 0.7606 | 0.2394
MOOV
CELTISS
Chart: 3G band usage(%)
| UMTS 900 | UMTS 2100
MTN | 0.2719 | 0.7281
MOOV | 0.1196 | 0.8804
CELTISS | 0.2449 | 0.7551

## Slide 28: Benchmarking – CS Integrity Voice quality maps (MOS) MTN has around 2.43% of MOS samples lower than 2.2 Values lower than 2.2 pose risk of bad users perceived voice quality 3d

## Slide 29: Benchmarking: Radio parameters EC/NO comparison CELLTIS have the best 3G EcNo samples within acceptable range
Chart: Ec/No Distribution (%)
| -8 to 0 | -12 to -8 | -16 to -12 | -34 to -16 | ACCEPTABLE EC/N0
MTN | 0.0839 | 0.2337 | 0.5741 | 0.1083 | 0.3176
MOOV | 0.1033 | 0.1765 | 0.4945 | 0.2257 | 0.2798
CELTISS | 0.5467 | 0.2873 | 0.1199 | 0.0461 | 0.834

## Slide 30: Benchmarking: Radio parameters EC/NO CELLTIS have the best 3G EcNo samples distribution

## Slide 31: Benchmarking – SINR comparison Drive tests are showing that MTN have the best acceptable level range of SINR.
Chart: SINR Comparison
| (Min,-4) | (-4,0) | (0,7) | (7,15 <) | ACCEPTABLE SINR
MTN | 0.0112 | 0.0502 | 0.3522 | 0.5864 | 0.9386
MOOV | 0.0167 | 0.0594 | 0.4131 | 0.5108 | 0.9239
CELTISS | 0.0306 | 0.0921 | 0.2958 | 0.5815 | 0.8773

## Slide 32: Benchmarking – SNIR comparison map 4G MTN have a better quality of signal compared to CELTISS and MOOV.

## Slide 33: Benchmarking – 2G/3G CALL SETUP TIME MTN have the best Call setup time.
Chart: Call Setup Time (s)
| Call Setup Time
MTN | 6.25
MOOV | 7.41
CELTISS | 7.69

## Slide 34: Benchmarking – CALL SETUP TIME/Call Mode MTN have the best 4G CSBF Call setup Time, Call setup time 2G is higher than in 3G/4G.
Chart: CS Call setup Time by technology (s)
| 4G CSFB CST | 3G CST | 2G CST
MTN | 6.22 | 6.47 | 6.81
MOOV | 7.77 | 7.01
CELTISS | 7.91 | 7.51

## Slide 35: Benchmarking – SMS SENDING FAILURE All operators failed in SMS service due to the delivery time exceeding 6s however MTN have the best SMS results
Chart: SMS SR(%)
| SMS Sending message success rate (%) | SMS Receving message success rate (%)
MTN | 0.9589 | 0.9412
MOOV | 0.855 | 0.8398
CELTISS | 0.896 | 0.8765
Chart: SMS Send Time(%)
| (0,3) | (3,6) | >6
MTN | 0.6445 | 0.3144 | 0.0411
MOOV | 0.598 | 0.298 | 0.104
CELTISS | 0.6171 | 0.2689 | 0.114

## Slide 36
Benchmarking Data service
04

## Slide 37: Benchmarking – DATA 3G All operators have a good rate of successful Internet connection
Chart: PS Attach & PDP Contex Act(%)
| PS Attach success(%) | PDP Context Act Success (%)
MTN | 1 | 0.9943
MOOV | 0.9955 | 0.983
CELTISS | 0.989 | 0.9946
Chart: Attach & PDP Activation Time (s)
| PS Attach Setup Time | PDP Context Act Time
MTN | 1.11 | 1.77
MOOV | 1.19 | 1.55
CELTISS | 1.32 | 2.01

## Slide 38: Benchmarking – DATA 3G All operators have good web service success rate. MTN have the best PS connection setup time
Chart: PS Connection setup time
| PS Connection setup time
MTN | 5.91
MOOV | 6.07
CELTISS | 6.1
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9888
MOOV | 0.9977
CELTISS | 0.9826

## Slide 39: Benchmarking – DATA 3G All operators met the ARCEP downlink and uplink FTP success rate thresholds.
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9858 | 0.9713
MOOV | 0.9869 | 0.9726
CELTISS | 0.9958 | 0.9913

## Slide 40: Benchmarking – 3G FTP MEAN THROUGHPUT All operators met the ARCEP downlink and uplink FTP success rate thresholds.
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 3506.88 | 1982.95 | 19541.22 | 17350.35
MOOV | 3089.84 | 1168.93 | 18690.66 | 14960.63
CELTISS | 6459.46 | 1755.94 | 15344.54 | 10101.01
MTN FTP DL AVERAGE Throughout is ranked second
MTN FTP UL AVERAGE Throughout is ranked first

## Slide 41: Benchmarking – 3G FTP MEAN THROUGHPUT comparison map All samples exceed 2Mbps

## Slide 42: Benchmarking – 4G HTTP Browsing MTN Have the best HTTP Browsing success rate.
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9896
MOOV | 0.9817
CELTISS | 0.9788

## Slide 43: Benchmarking – 4G FTP THROUGHPUT comparison All operators have a good FTP success rate.
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 1 | 1
MOOV | 1 | 0.9977
CELTISS | 0.9932 | 1

## Slide 44: Benchmarking – 4G FTP THROUGHPUT comparison MTN is ranked first in all kinds of 4G data tests
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 36956.67 | 15436.67 | 187904.99 | 35302.45
MOOV | 15662.65 | 9549.01 | 179845.12 | 25508.51
CELTISS | 12999.143 | 14439.78 | 22466.23 | 14439.78

## Slide 45: Benchmarking – 4G FTP THROUGHPUT comparison map MTN Shows the best 4G FTP throughput samples distribution.

## Slide 46: Benchmarking – BAND and TECHNOLOGY UTILISATION Most of MTN LTE samples are in 2600 band. Most of CELTIS LTE samples are in 1800 band. Most of MOOV LTE samples are in 2600 band Usage of 3G U900 is lower for CELTISS
Chart: 3G band Distribution(%)
| UMTS 900 | UMTS 2100
MTN | 0.1768 | 0.8232
MOOV | 0.197 | 0.803
CELTISS | 0.0715 | 0.9285
Chart: 4G Band Distribution (%)
| LTE 800 | LTE 700 | LTE 1800 | LTE 2100 | LTE 2600
MTN | 0.1405 | 0.0876 | 0.057 | 0 | 0.7149
MOOV | 0.3131 | 0 | 0.0324 | 0 | 0.6545
CELTISS | 0.2037 | 0 | 0.5051 | 0 | 0.2912

## Slide 47: Benchmarking – Data TECHNOLOGY Usage(%) MTN have the highest LTE CA Carrier Aggregation usage.
Chart: 3G Packet Technology usage (%)
| DC-HSPA | HSPA | HSDPA | UMTS
MTN | 0.5135 | 0.0887 | 0 | 0.3978
MOOV | 0.4506 | 0.1462 | 0.0017 | 0.4017
CELTISS | 0.4475 | 0.0583 | 0.0261 | 0.4681
Chart: 4G Packet Technology usage (%)
| LTE | LTE CA
MTN | 0.1071 | 0.8929
MOOV | 0.422 | 0.578
CELTISS | 0.495 | 0.505

## Slide 48
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2023 Deloitte Bénin SARL. Société du réseau Deloitte