## Slide 1
Network QoS
OUIDAH Intermediate report
November 21st, 2023

## Slide 2: Summary
Scope of Intermediate Report | 3
Executive Summary | 5
Benchmarking Key Results | 11
Benchmarking Coverage | 16
Benchmarking Voice Service | 23
Benchmarking Data Service | 36

## Slide 3
Introduction: Scope of Intermediate Report
01

## Slide 4: Intermediate report
Scope of this report
  1. Network benchmarking results for the Ouidah area between MTN, MOOV, and CELTISS from September 9th to September 13th, 2023..
  Comments and recommendations may be enriched on final report using CM audit findings

## Slide 5
Benchmarking Executive Summary
02

## Slide 6: Executive Summary – Benchmarking coverage 2G/3G/4G
Coverage 2G/3G/4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
2G MTN is ranked 2nd in indoor and incar and coverage rate
All operators met ARCEP 2G coverage obligation except CELTISS Indoor.
3G MTN coverage rate is ranked second
All operators met ARCEP 3G coverage obligation
4G MTN coverage rate is ranked second
All operators satisfy the 4G Coverage thresholds only for outdoor measurement .
Tune and align power settings mainly in 3G/4G. Actual setting may impact the coverage strength specially at Indoor locations
Review the design at the coverage and quality blackspots
We highlight that 4G ARCEP coverage Thresholds are aggressive

## Slide 7: Executive Summary – Benchmarking voice service 2G/3G
Voice service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Accessibility: MTN is ranked first for the accessibility to voice service , better than CELTISS and MOOV
All operators satisfy the ARCEP accessibility thresholds,
Retainability: MTN is ranked second in term of retainability
Only CELTISS satisfies the retainability ARCEP thresholds
Integrity: MTN is in third position in term of voice quality lower than MOOV and CELTISS with average Mean Opinion Score of 3.85 as opposed to 3.94 for CELTISS and 4.01 for MOOV.
Voice quality is always better in 3G due to its better codec rate , we recommend to push as much as possible the voice traffic to 3G.
Actual selection/reselection/Irat parameters need to be reviewed and aligned.
2G Full Rate/Half Rate settings need to be tuned in order to improve Full rate penetration

## Slide 8: Executive Summary – Benchmarking SMS service
SMS service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
All operators failed to meet ARCEP for SMS Send Success with End To End Delivery Time < 6 sec,
MTN is ranked first in SMS service tests.
There is no issue in radio accessibility that could be correlated to the SMS high delivery time.
End to End investigation need to be performed to analyses the high delivery time including mainly Core/SMS parts: SM Sserver...

## Slide 9: Executive Summary – Benchmarking 4G Data service
Data service 4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 4G data service, and all operators meet ARCEP's requirements.
MTN is ranked first in terms of 4G DL and UL average throughput with 53.33/19.15Mbps, which is better than MOOV 36.33/13.02 Mbps and CELTISS 13.94/11.94Mbps.
MTN spectrum need to be used with a better efficiency, Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles

## Slide 10: Executive Summary – Benchmarking 3G Data service
Data service 3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 3G data service, and all operators met ARCEP's requirements.
MTN is in third position for 3G DL throughput with 3.3Mbps, compared to 5.85Mbps for MOOV and 7.93Mbps for CELTISS.
MTN is ranked third in term of 3G UL throughput with 1.15 Mbps compared yo 1.46 Mbps for MOOV and 2.16Mbps for CELTISS,
All operators met ARCEP’s 3G User Throughput obligation for download and upload.
All operators met ARCEP’s web browsing service accessibility thresholds.
Its recommended to push as much as possible the data traffic to 4G in order to:
- Improve end user perception, Both DT and stats are showing that users in average are served with up to 700% better throughput in 4G than in 3G
- Offload the 3G network which will improve the 3G throughput and the 3G radio quality
Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles

## Slide 11
Benchmarking Key Results
03

## Slide 12: Benchmarking Key Results – Coverage All operators met the different coverage thresholds except 4G Incar and Indoor and CELTISS 2G Indoor CELTISS have the best 2G and the worst 4G Incar coverage. All remaining coverage results are within the same ranges MTN is ranked 2nd in almost all kind of coverage except 2G outdoor where results are very similar for all operators
KPI |  | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
2G Coverage Rate | Incar | More than 90% with Incar: Rxlev >-87 dBm | 96,41% | OK | 92,22% | OK | 99,91% | OK | 2
 | Outdoor | More than 90% with Outdoor: Rxlev >-92 dBm | 99,40% | OK | 99,63% | OK | 99,97% | OK | 3
 | Indoor | More than 90% with Outdoor: Rxlev >-74 dBm | 90,22% | OK | 90,46% | OK | 89,28% | NOK | 2
3G Coverage Rate | Incar,Indoor,Outdoor | More than 90% with RSCP <-85 dBm | 92,15% | OK | 91,56% | OK | 95,68% | OK | 2
4G Coverage Rate | Incar | More than 90% with RSRP <-90 dBm* | 88,02% | NOK | 88,33% | NOK | 60,95% | NOK | 2
 | Outdoor | More than 90% with RSRP <-95 dBm* | 96,42% | OK | 95,99% | OK | 97,94% | OK | 2
 | Indoor | More than 90% with RSRP <-78 dBm* | 24,06% | NOK | 26,88% | NOK | 23,03% | NOK | 2

## Slide 13: Benchmarking Key Results – 2G/3G voice and SMS Summary MTN is ranked first in voice accessibility Only CELTISS satisfies the retainability ARCEP thresholds All operators met the MOS ARCEP thresholds however MOOV and CELTISS have better average MOS All operators fail in SMS service due to the delivery time exceeding 6s.
KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  | Value | Conformity | Value | Conformity | Value | Conformity | 
Accesibility: Blocking rate | <1% | 0,24% | OK | 0,27% | OK | 0,32 | OK | 1
Retainability: Call drop rate | <1% | 1,15% | NOK | 2,44% | NOK | 0% | OK | 2
Call Completetion Rate (%) | =<99% | 98,61% | NOK | 97,29% | NOK | 99,68% | OK | 2
Integrity: Voice quality | Note requise> 2,8 | 3,85 | OK | 4,01 | OK | 3,94 | OK | 3
SMS sending success rate % (E2E delivery Time<6 sec) | >99% | 98,71% | NOK | 96,57% | NOK | 93,81% | NOK | 1
SMS receving success rate % | >99% | 97,33% | NOK | 94,51% | NOK | 91,89% | NOK | 1

## Slide 14: Benchmarking Key Results – 3G Data Summary All operators met the 3G Data ARCEP requirements. MTN is the best in 3G HTTP service MTN is ranked 3rd in 3G FTP service
Services | KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
3G HTTP | Successful internet connexion rate | >96% | 99,86% | OK | 98,00% | OK | 98,35% | OK | 1
 | Connexion setup time | <=10sec | 5,09 | OK | 6,31 | OK | 5,98 | OK | 1
 | Web service failure rate | <3% | 0,96% | OK | 0,28% | OK | 1,22% | OK | 2
3G FTP | FTP failure rate UL/DL | <3 % | 1,34%/0% | OK | 0,12%/0% | OK | 0,49%/0,51% | OK | 3
 | FTP Data transmission average (DL) | >= 2Mbps | 3,259 | OK | 5,853 | OK | 7,928 | OK | 3
 | FTP Data transmission average (UL) | >= 1Mbps | 1,147 | OK | 1,458 | OK | 2,163 | OK | 3

## Slide 15: Benchmarking Key Results – 4G Data Summary All operators met the 3G Data ARCEP requirements. MTN is the best in 4G data for both HTTP and FTP
Services | KPI | Threshorlds* | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
4G HTTP Browsing | Web service failure rate (%) | <3% | 0,00% | OK | 0,00% | OK | 0,00% | OK | 1
 | Connexion setup time | <=3sec | 0,39 | OK | 0,77 | OK | 0,29 | OK | 2
4G FTP | FTP failure rate UL/DL | <3 % | 0%/0% | OK | 0,9%/0,56% | OK | 0%/0% | OK | 1
 | FTP Data transmission average (DL) | 4G >= 5 Mbps | 53,331 | OK | 36,338 | OK | 13,943 | OK | 1
 | FTP Data transmission average (UL) | 4G: >= 2Mbps | 19,146 | OK | 13,019 | OK | 11,937 | OK | 1

## Slide 16
Benchmarking 2G/3G/4G coverage
04

## Slide 17: Benchmarking: 2G coverage CELTISS’s 2G indoor coverage failed to reach the ARCEP requirement.
Chart: RxLev Distribution (%)
| Indoor>-74 | Incar >-87 | Outdoor >-92
MTN | 0.9022 | 0.9641 | 0.994
MOOV | 0.9046 | 0.9222 | 0.9963
CELTISS | 0.8928 | 0.9991 | 0.9997

## Slide 18: Benchmarking: 2G coverage - Maps 2G coverage plots are quite similar for the 3 operators except in few roads

## Slide 19: Benchmarking: 3G coverage All operators 3G coverage met ARCEP requirements with better average values for CELTISS.
Chart: RSCP Distribution (%)
| Indoor,Incar,Outdoor >-85
MTN | 0.9215
MOOV | 0.9156
CELTISS | 0.9568

## Slide 20: Benchmarking: 3G coverage-Maps 2G coverage plots are quite similar for the 3 operators except in few roads.

## Slide 21: Benchmarking: 4G coverage All operators failed to satisfy the 4G Indoor coverage, CELTISS failed also in 4G incar coverage.
Chart: RSRP Distribution (%)
| Indoor > -78 | Incar > -90 | Outdoor > -95
MTN | 0.2406 | 0.8802 | 0.9642
MOOV | 0.2688 | 0.8833 | 0.9599
CELTISS | 0.2303 | 0.6095 | 0.9794

## Slide 22: Benchmarking – 4G coverage - Maps 2G coverage plots are quite similar for the 3 operators except in few roads.

## Slide 23
Benchmarking voice service
05

## Slide 24: Benchmarking: CS Accessibility 2G/3G BLOCKED CALLS MTN has the best accessibility to voice service compared to competitors, MTN 3G blocked rate is higher than competitors
Chart: Call Blocked Rate (%)
| CBR (%)
MTN | 0.0024
MOOV | 0.0027
CELTISS | 0.0032
Chart: Call Blocked Rate per Technology (%)
| CBR (%)
MTN 2G | 0.0027
MTN 3G | 0.0198
MOOV 2G | 0
MOOV 3G | 0.0027
CELTISS 2G | 0
CELTISS 3G | 0.0032

## Slide 25: Benchmarking: CS Integrity Voice quality Mean Opinion Score MOOV has the best ratio of excellent and good Voice Quality samples MTN needs to improve its voice quality MOS by pushing CS traffic to 3G and increase 2G full rate penetration.
Chart: Average MOS
| Avrege MOS
MTN | 3.85
MOOV | 4.01
CELTISS | 3.94
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Excel+Goog
MTN | 0.5036 | 0.4661 | 0.0187 | 0.0116 | 0.9697
MOOV | 0.9173 | 0.0731 | 0.0029 | 0.0067 | 0.9904
CELTISS | 0.6015 | 0.3865 | 0.0111 | 0.0009 | 0.988

## Slide 26: Benchmarking: CS Retainability 2G/3G DROPPED CALLS All operators satisfy ARCEP thresholds regarding Call Drop Rate.
Chart: Call Drop Rate (%)
| CDR (%)
MTN | 0.0115
MOOV | 0.0244
CELTISS | 0

## Slide 27: Benchmarking Voice service Band usage(%) 20% of MTN voice calls is carried by 2G while all voice traffic is carried by 3G for competitors Its recommended for MTN to reduce 2G utilization and increase 3G penetration for better audio quality. MTN's 2G band usage: 76,76% GSM 900 and 23,24% GSM 1800 Mhz, 43 % of MTN 3G CS traffic is carried on U900 compared to 24% and 7% for MOOV and CELTISS.
Chart: System Technology usage(%)
| GSM | UMTS
MTN | 0.1881 | 0.8119
MOOV | 0 | 1
CELTISS | 0 | 1
Chart: 2G band usage(%)
| GSM 900 | GSM 1800
MTN | 0.7676 | 0.2324
MOOV
CELTISS
Chart: 3G band usage(%)
| UMTS 900 | UMTS 2100
MTN | 0.4305 | 0.5695
MOOV | 0.2382 | 0.7618
CELTISS | 0.0732 | 0.9268

## Slide 28: Benchmarking – CS Integrity Voice quality maps (MOS) MTN has around 1% of MOS samples lower than 2.2, Values lower than 2,2 pose risk of bad users perceived voice quality 3d

## Slide 29: Benchmarking: Radio parameters EC/NO comparison Only 18% of MTN 3G EcNo samples are within acceptable range compared to 73% and 95% for MOOV and CELTISS. This is correlated to the number of 3G carriers and the fact that more than 40% of MTN 3G traffic is carried by U900
Chart: Ec/No Distribution (%)
| -8 to 0 | -12 to -8 | -16 to -12 | -34 to -16 | ACCEPTABLE EC/N0
MTN | 0.0355 | 0.1411 | 0.7259 | 0.0976 | 0.1766
MOOV | 0.453 | 0.2738 | 0.2214 | 0.0518 | 0.7268
CELTISS | 0.7251 | 0.2275 | 0.0393 | 0.0082 | 0.9526

## Slide 30: Benchmarking: Radio parameters EC/NO 3G MOOV and CELTISS EC/N0 is better than MTN

## Slide 31: Benchmarking – SINR comparison Drive tests are showing a acceptable level of MTN Network SINR.
Chart: SINR Comparison
| (Min,-4) | (-4,0) | (0,7) | (7,15 <) | ACCEPTABLE SINR
MTN | 0.0024 | 0.019 | 0.0974 | 0.8812 | 0.9786
MOOV | 0.0141 | 0.0431 | 0.2879 | 0.6549 | 0.9428
CELTISS | 0.0012 | 0.0149 | 0.2171 | 0.7668 | 0.9839

## Slide 32: Benchmarking – SNIR comparison map 4G MOOV have more bad quality samples compared to MTN and CELTISS.

## Slide 33: Benchmarking – 2G/3G CALL SETUP TIME MTN have the best Call setup time.
Chart: Call Setup Time (s)
| Call Setup Time
MTN | 6.16
MOOV | 6.35
CELTISS | 6.29

## Slide 34: Benchmarking – CALL SETUP TIME/Call Mode MTN have the best 4G CSBF Call setup Time, Call setup time 2G is higher than in 3G/4G.
Chart: CS Call setup Time by technology (s)
| 4G CSFB CST | 3G CST | 2G CST
MTN | 5.44 | 6.21 | 6.68
MOOV | 7.33 | 6.12
CELTISS | 6.48 | 6.91

## Slide 35: Benchmarking – SMS SENDING FAILURE MTN SMS SETUP/RESPONSE is better than CELTIS & MOOV. SMS service KPIs of the three operators are not compliant with the ARCEP requirements because of the 6s criteria.
Chart: SMS
| SMS Sending message success rate (%) | SMS Receving message success rate (%)
MTN | 0.9871 | 0.9733
MOOV | 0.9657 | 0.9451
CELTISS | 0.9381 | 0.9189
Chart: SMS Send Time(%)
| (0,3) | (3,6) | >6
MTN | 0.6801 | 0.307 | 0.0129
MOOV | 0.6342 | 0.3315 | 0.0343
CELTISS | 0.6366 | 0.3015 | 0.0619

## Slide 36
Benchmarking Data service
06

## Slide 37: Benchmarking – DATA 3G All operators have a good rate of successful Internet connection
Chart: PS Attach & PDP Contex Act(%)
| PS Attach success(%) | PDP Context Act Success (%)
MTN | 0.9986 | 0.9978
MOOV | 0.98 | 0.9908
CELTISS | 0.9835 | 0.9981
Chart: Attach & PDP Activation Time (s)
| PS Attach Setup Time | PDP Context Act Time
MTN | 1.45 | 1.11
MOOV | 1.43 | 1.25
CELTISS | 1.49 | 1.49

## Slide 38: Benchmarking – DATA 3G All operators have a good web service success rate. MTN have best PS connection setup time
Chart: PS Connection setup time
| PS Connection setup time
MTN | 5.09
MOOV | 6.31
CELTISS | 5.98
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9904
MOOV | 0.9972
CELTISS | 0.9878

## Slide 39: Benchmarking – DATA 3G All operators have a good downlink and uplink FTP success rate.
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9866 | 1
MOOV | 0.9988 | 1
CELTISS | 0.9951 | 0.9949

## Slide 40: Benchmarking – 3G FTP MEAN THROUGHPUT MTN 3G Throughput DL/UL is less than MOOV’s and CELTISS’s
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 3259 | 1147.85 | 14782.99 | 11128.18
MOOV | 5853.58 | 1458.95 | 15775.47 | 13706.09
CELTISS | 7928.99 | 2163.03 | 13559.53 | 16096.56
MTN FTP DL AVERAGE Throughout is less than MOOV and CELTISS DL Throughout
DL Throughput mean for all operators satisfies ARCEP thresholds
MTN FTP UL AVERAGE Throughout is less than CELTISS’s MOOV’s
UL Throughput mean for all operators satisfy ARCEP thresholds

## Slide 41: Benchmarking – 3G FTP MEAN THROUGHPUT comparison map All samples exceed 2Mbps

## Slide 42: Benchmarking – 4G HTTP Browsing All operators have a very good HTTP Browsing success rate.
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 1
MOOV | 1
CELTISS | 1

## Slide 43: Benchmarking – 4G FTP THROUGHPUT comparison All operators have a good FTP success rate.
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 1 | 1
MOOV | 0.991 | 0.9954
CELTISS | 1 | 1

## Slide 44: Benchmarking – 4G FTP THROUGHPUT comparison MTN FTP DL/UL AVERAGE Throughput is better than CELTISS and MOOV.
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 53331.19 | 17146.62 | 190186.08 | 53794.21
MOOV | 36338.56 | 13019.58 | 214519.32 | 61217.72
CELTISS | 13943.75 | 11937.85 | 27570.85 | 20634.98

## Slide 45: Benchmarking – 4G FTP THROUGHPUT comparison map MOOV’s average throughput DL rate is better than MTN and CELTISS.

## Slide 46: Benchmarking – BAND and TECHNOLOGY UTILISATION Most of MTN LTE samples are in 2600 band. Most of CELTIS LTE samples are in 1800 band. Most of MOOV LTE samples are in 2600 and 800 bands. Usage of 3G U900 is lower for competitors compared to MTN
Chart: 3G band Distribution (%)
| UMTS 900 | UMTS 2100
MTN | 0.2033 | 0.7967
MOOV | 0.1022 | 0.8978
CELTISS | 0.0069 | 0.9931
Chart: 4G Band Distribution (%)
| LTE 800 | LTE 700 | LTE 1800 | LTE 2100 | LTE 2600
MTN | 0.0057 | 0.0003 | 0.0211 | 0.0033 | 0.9697
MOOV | 0.4197 | 0 | 0.0181 | 0 | 0.5622
CELTISS | 0.0845 | 0 | 0.9155 | 0 | 0

## Slide 47: Benchmarking – Data TECHNOLOGY Usage(%) MTN have the highest LTE CA Carrier Aggregation usage.
Chart: 3G Packet Technology usage (%)
| DC-HSPA | HSPA | HSDPA | UMTS
MTN | 0.4737 | 0.0613 | 0.0066 | 0.4585
MOOV | 0.4879 | 0.0501 | 0 | 0.462
CELTISS | 0.4724 | 0.0248 | 0.0226 | 0.4802
Chart: 4G Packet Technology usage (%)
| LTE | LTE CA
MTN | 0.2227 | 0.7773
MOOV | 0.49 | 0.51
CELTISS | 0.3178 | 0.6822

## Slide 48
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2023 Deloitte Bénin SARL. Société du réseau Deloitte