## Slide 1
Network QoS
PARAKOU Intermediate report
November 22nd, 2023

## Slide 2: Summary
Scope of Intermediate Report | 3
Executive Summary | 5
Benchmarking Key Results | 11
Benchmarking Coverage | 16
Benchmarking Voice Service | 23
Benchmarking Data Service | 36

## Slide 3
Introduction: Scope of Intermediate Report
01

## Slide 4: Intermediate report
Scope of this report
  1. Network benchmarking results for the PARAKOU area between MTN, MOOV, and CELTISS from September 9th to September 13th, 2023..

## Slide 5
Benchmarking Executive Summary
02

## Slide 6: Executive Summary – Benchmarking coverage 2G/3G/4G
Coverage 2G/3G/4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
MTN, MOOV, and CELTISS have quite similar 2G coverage, All of them satisfy the ARCEP requirements
MTN is ranked first in 3G coverage where all operators satisfy the ARCEP requirements
All operators failed to satisfy the ARCEP requirements in terms of Indoor 4G coverage. CELTISS and MTN fails in Incar 4G coverage as well
Tune and align power settings mainly in 3G/4G. Actual setting may impact the coverage strength specially at Indoor locations
Review the design at the coverage and quality blackspots
We highlight that 4G ARCEP coverage Thresholds are aggressive

## Slide 7: Executive Summary – Benchmarking voice service 2G/3G
Voice service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Accessibility: MTN is ranked first for the accessibility to voice
MTN is ranked third in term of voice retainability
All operators satisfy the voice ARCEP thresholds
MTN have the best average MOS
Voice quality is always better in 3G due to its better codec rate , we recommend to push as much as possible the voice traffic to 3G.
Actual selection/reselection/Irat parameters need to be reviewed and aligned.
2G Full Rate/Half Rate settings need to be tuned in order to improve Full rate penetration

## Slide 8: Executive Summary – Benchmarking SMS service
SMS service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Only MTN succeeded to reach ARCEP SMS target results
End to End investigation need to be performed to analyses the high delivery time including mainly Core/SMS parts: SM Sserver...

## Slide 9: Executive Summary – Benchmarking 4G Data service
Data service 4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
All operators met the 4G Data ARCEP requirements except CELTISS in FTP Failure rate.
MTN is ranked first in all kinds of 4G data tests, with 29.5/15.5Mbps DL/UL Throughput compared to 12.9/11.9 Mbps and 12.6/10.3 Mbps for MOOV and MTN.
MTN spectrum need to be used with a better efficiency, Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles

## Slide 10: Executive Summary – Benchmarking 3G Data service
Data service 3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
MTN met all the 3G Data ARCEP requirements.
MOOV and CELTISS failed in Web service and FTP failure rate. MOOV failed also in UL FTP throughput
MTN is in 2nd position for 3G DL throughput with 4.8Mbps, compared to 6.8Mbps for CELTISS and 3Mbps for MOOV.
MTN is ranked first in term of 3G UL throughput with 2.3 Mbps against 0.91 Mbps for MOOV and 1.91Mbps for CELTISS,
Its recommended to push as much as possible the data traffic to 4G in order to:
- Improve end user perception, Both DT and stats are showing that users in average are served with up to 700% better throughput in 4G than in 3G
- Offload the 3G network which will improve the 3G throughput and the 3G radio quality
Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles

## Slide 11
Benchmarking Key Results
03

## Slide 12: Benchmarking Key Results – Coverage MTN, MOOV, and CELTISS have quite similar 2G coverage, All of them satisfy the ARCEP requirements MTN is ranked first in 3G coverage where all operators satisfy the ARCEP requirements All operators failed to satisfy the ARCEP requirements in terms of Indoor 4G coverage. CELTISS and MTN fails in Incar 4G coverage as well
KPI |  | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
2G Coverage Rate | Incar | More than 90% with Incar: Rxlev >-87 dBm | 99,79% | OK | 99,99% | OK | 99,94% | OK | 3
 | Outdoor | More than 90% with Outdoor: Rxlev >-92 dBm | 100% | OK | 100% | OK | 99,99% | OK | 1
 | Indoor | More than 90% with Outdoor: Rxlev >-74 dBm | 95,63% | OK | 94,59% | OK | 93,09% | OK | 1
3G Coverage Rate | Incar,Indoor,Outdoor | More than 90% with RSCP <-85 dBm | 97,95% | OK | 93,96% | NOK | 97,29% | OK | 1
4G Coverage Rate | Incar | More than 90% with RSRP <-90 dBm* | 89,19% | NOK | 93,22% | OK | 87,62% | NOK | 2
 | Outdoor | More than 90% with RSRP <-95 dBm* | 99,21% | OK | 99,61% | OK | 98,12% | OK | 2
 | Indoor | More than 90% with RSRP <-78 dBm* | 51,11% | NOK | 67,37% | NOK | 60,83% | NOK | 3

## Slide 13: Benchmarking Key Results – 2G/3G voice and SMS Summary MTN is ranked first in term of voice accessibility MTN is ranked third in term of voice retainability All operators satisfy the voice ARCEP thresholds All operators met the MOS ARCEP thresholds. MTN have the best average MOS Only MTN succeeded to reach ARCEP SMS target results
KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  | Value | Conformity | Value | Conformity | Value | Conformity | 
Accesibility: Blocking rate | <1% | 0,29% | OK | 0,63% | OK | 0,31 | OK | 1
Retainability: Call drop rate | <1% | 0,46% | OK | 0,23% | OK | 0,37% | OK | 3
Call Completetion Rate (%) | =<99% | 99,25% | OK | 99,14% | OK | 99,32% | OK | 2
Integrity: Voice quality | Note requise> 2,8 | 3,98 | OK | 3,63 | OK | 3,85 | OK | 1
SMS sending success rate % (E2E delivery Time<6 sec) | >99% | 99,77% | OK | 96,34% | NOK | 89,08% | NOK | 1
SMS receving success rate % | >99% | 99,11% | OK | 95,33% | NOK | 88,91% | NOK | 1

## Slide 14: Benchmarking Key Results – 3G Data Summary MTN met all the 3G Data ARCEP requirements. MOOV and MTN failed in Web service and FTP failure rate. MOOV failed also in UL FTP throughput
Services | KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
3G HTTP | Successful internet connexion rate | >96% | 98,81% | OK | 99,07% | OK | 98,27% | OK | 2
 | Connexion setup time | <=10sec | 5,77 | OK | 7,35 | OK | 7,32 | OK | 1
 | Web service failure rate | <3% | 2,02% | OK | 3,13% | NOK | 4,92% | NOK | 1
3G FTP | FTP failure rate UL/DL | <3 % | 0,31%/1,14% | OK | 0%/8,85% | OK/NOK | 2,99%/3,49% | OK/NOK | 1
 | FTP Data transmission average (DL) | >= 2Mbps | 4,830 | OK | 3,008 | OK | 6,810 | OK | 2
 | FTP Data transmission average (UL) | >= 1Mbps | 2,318 | OK | 0,91 | NOK | 1,919 | OK | 1

## Slide 15: Benchmarking Key Results – 4G Data Summary All operators met the 4G Data ARCEP requirements except CELTISS in FTP Failure rate. MTN is ranked first in almost all kinds of 4G data tests
Services | KPI | Threshorlds* | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
4G HTTP Browsing | Web service failure rate (%) | <3% | 0,00% | OK | 0,45% | OK | 1,23% | OK | 1
 | Connexion setup time | <=3sec | 1,57 | OK | 1,68 | OK | 1,88 | OK | 1
4G FTP | FTP failure rate UL/DL | <3 % | 0,33%/0% | OK | 0%/0% | OK | 4,61%/2,86% | NOK | 2
 | FTP Data transmission average (DL) | 4G >= 5 Mbps | 29,498 | OK | 12,899 | OK | 12,572 | OK | 1
 | FTP Data transmission average (UL) | 4G: >= 2Mbps | 15,470 | OK | 11,821 | OK | 10,259 | OK | 1

## Slide 16
Benchmarking 2G/3G/4G coverage
04

## Slide 17: Benchmarking: 2G coverage MTN, MOOV and CELTISS 2G coverage met the ARCEP RxLev thresholds.
Chart: RxLev Distribution (%)
| Indoor>-74 | Incar >-87 | Outdoor >-92
MTN | 0.9563 | 0.9979 | 1
MOOV | 0.9459 | 0.9999 | 1
CELTISS | 0.9309 | 0.9994 | 0.9999

## Slide 18: Benchmarking: 2G coverage - Maps 2G coverage plots are quite similar for the 3 operators

## Slide 19: Benchmarking: 3G coverage MTN is ranked first in 3G coverage where all operators satisfy the ARCEP requirements
Chart: RSCP Distribution (%)
| Indoor,Incar,Outdoor >-85
MTN | 0.9795
MOOV | 0.9396
CELTISS | 0.9729

## Slide 20: Benchmarking: 3G coverage-Maps 3G coverage plots are quite similar for the 3 operators

## Slide 21: Benchmarking: 4G coverage All operators failed to satisfy the ARCEP requirements in terms of Indoor 4G coverage.
Chart: RSRP Distribution (%)
| Indoor > -78 | Incar > -90 | Outdoor > -95
MTN | 0.5111 | 0.8919 | 0.9921
MOOV | 0.6737 | 0.9322 | 0.9961
CELTISS | 0.6083 | 0.8762 | 0.9812

## Slide 22: Benchmarking – 4G coverage - Maps 4G coverage plots are quite similar for the 3 operators except in few roads

## Slide 23
Benchmarking voice service
05

## Slide 24: Benchmarking: CS Accessibility 2G/3G BLOCKED CALLS MTN is ranked first in voice accessibility.
Chart: Call Blocked Rate (%)
| CBR (%)
MTN | 0.0029
MOOV | 0.0063
CELTISS | 0.0031
Chart: Call Blocked Rate per Technology (%)
| CBR (%)
MTN 2G | 0
MTN 3G | 0.0113
MOOV 2G | 0.0222
MOOV 3G | 0.0189
CELTISS 2G | 0.0127
CELTISS 3G | 0.0098

## Slide 25: Benchmarking: CS Integrity Voice quality Mean Opinion Score MTN have the best ratio of excellent and good Voice Quality samples
Chart: Average MOS
| Avrege MOS
MTN | 3.98
MOOV | 3.63
CELTISS | 3.85
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Excel+Goog
MTN | 0.5807 | 0.3983 | 0.0047 | 0.0163 | 0.979
MOOV | 0.0023 | 0.984 | 0.0107 | 0.0031 | 0.9863
CELTISS | 0.4061 | 0.5789 | 0.0134 | 0.0016 | 0.985

## Slide 26: Benchmarking: CS Retainability 2G/3G DROPPED CALLS All operators satisfie the retainability ARCEP thresholds
Chart: Call Drop Rate (%)
| CDR (%)
MTN | 0.0046
MOOV | 0.0023
CELTISS | 0.0037

## Slide 27: Benchmarking Voice service Band usage(%) Most of voice traffic is carried by 3G for all operators MTN's 2G band usage: 63,16% GSM 900 and 36,84% GSM 1800 Mhz, 23,9 % of MTN 3G CS traffic is carried on U900 compared to 16% and 3,5% for MOOV and CELTISS.
Chart: System Technology usage(%)
| GSM | UMTS
MTN | 0.0035 | 0.9965
MOOV | 0.0339 | 0.9661
CELTISS | 0.0125 | 0.9875
Chart: 2G band usage(%)
| GSM 900 | GSM 1800
MTN | 0.6316 | 0.3684
MOOV | 0.6676 | 0.3324
CELTISS | 0.3433 | 0.6567
Chart: 3G band usage(%)
| UMTS 900 | UMTS 2100
MTN | 0.2389 | 0.7611
MOOV | 0.1611 | 0.8389
CELTISS | 0.0351 | 0.9649

## Slide 28: Benchmarking – CS Integrity Voice quality maps (MOS) MTN has around 1,63% of MOS samples lower than 2.2, Values lower than 2,2 pose risk of bad users perceived voice quality 3d

## Slide 29: Benchmarking: Radio parameters EC/NO comparison CELLTIS have the best 3G EcNo samples within acceptable range
Chart: Ec/No Distribution (%)
| -8 to 0 | -12 to -8 | -16 to -12 | -34 to -16 | ACCEPTABLE EC/N0
MTN | 0.1888 | 0.2779 | 0.4084 | 0.1249 | 0.4667
MOOV | 0.4249 | 0.4257 | 0.1407 | 0.0088 | 0.8506
CELTISS | 0.666 | 0.2358 | 0.075 | 0.0233 | 0.9018

## Slide 30: Benchmarking: Radio parameters EC/NO CELLTIS and MOOV have a better 3G EcNo samples distribution, This is could be correlated not only to the traffic but also to the number of carriers and U900 penetration

## Slide 31: Benchmarking – SINR comparison Drive tests are showing that CELTISS have the best acceptable level range of SINR.
Chart: SINR Comparison
| (Min,-4) | (-4,0) | (0,7) | (7,15 <) | ACCEPTABLE SINR
MTN | 0.0315 | 0.1492 | 0.4279 | 0.3914 | 0.8193
MOOV | 0.037 | 0.0817 | 0.1916 | 0.6897 | 0.8813
CELTISS | 0.0071 | 0.0258 | 0.153 | 0.8141 | 0.9671

## Slide 32: Benchmarking – SNIR comparison map 4G CELTISS have a better quality of signal distribution compared to MTN and MOOV.

## Slide 33: Benchmarking – 2G/3G CALL SETUP TIME MTN have the best Call setup time.
Chart: Call Setup Time (s)
| Call Setup Time
MTN | 6.87
MOOV | 7.49
CELTISS | 7.59

## Slide 34: Benchmarking – CALL SETUP TIME/Call Mode MTN have the best 4G CSBF Call setup Time, Call setup time 2G is higher than in 3G/4G.
Chart: CS Call setup Time by technology (s)
| 4G CSFB CST | 3G CST | 2G CST
MTN | 6.67 | 6.89 | 7.11
MOOV | 7.09 | 8.01 | 7.2
CELTISS | 7.33 | 8.32

## Slide 35: Benchmarking – SMS SENDING FAILURE All operators failed in SMS service due to the delivery time exceeding 6s however MTN have the best SMS results
Chart: SMS SR(%)
| SMS Sending message success rate (%) | SMS Receving message success rate (%)
MTN | 0.9977 | 0.9911
MOOV | 0.9634 | 0.9533
CELTISS | 0.8908 | 0.8891
Chart: SMS Send Time(%)
| (0,3) | (3,6) | >6
MTN | 0.7082 | 0.2911 | 0.0003
MOOV | 0.6184 | 0.348 | 0.0336
CELTISS | 0.5561 | 0.3347 | 0.1092
Only MTN succeeded to reach ARCEP SMS target results

## Slide 36
Benchmarking Data service
06

## Slide 37: Benchmarking – DATA 3G All operators have a good rate of successful Internet connection
Chart: PS Attach & PDP Contex Act(%)
| PS Attach success(%) | PDP Context Act Success (%)
MTN | 0.9881 | 0.9926
MOOV | 0.9907 | 0.9987
CELTISS | 0.9827 | 0.9915
Chart: Attach & PDP Activation Time (s)
| PS Attach Setup Time | PDP Context Act Time
MTN | 1.46 | 1.71
MOOV | 1.39 | 1.89
CELTISS | 1.4 | 1.42

## Slide 38: Benchmarking – DATA 3G CELLTISS failed in Web service MTN shows the best results compared to competitors
Chart: PS Connection setup time
| PS Connection setup time
MTN | 5.77
MOOV | 7.35
CELTISS | 7.32
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9798
MOOV | 0.9687
CELTISS | 0.9508

## Slide 39: Benchmarking – DATA 3G CELLTISS AND MOOV failed in ftp service
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9969 | 0.9886
MOOV | 1 | 0.9115
CELTISS | 0.9701 | 0.9651

## Slide 40: Benchmarking – 3G FTP MEAN THROUGHPUT
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 4830.86 | 2318.31 | 21354.11 | 17847.22
MOOV | 3008.55 | 908.33 | 15874.22 | 9547.28
CELTISS | 6810.93 | 1919.2 | 13122.22 | 16321.82
All operators met the ARCEP downlink and uplink FTP success rate thresholds.
MTN FTP DL AVERAGE Throughout is ranked second
MTN FTP UL AVERAGE Throughout is ranked first

## Slide 41: Benchmarking – 3G FTP MEAN THROUGHPUT comparison map All samples exceed 2Mbps

## Slide 42: Benchmarking – 4G HTTP Browsing MTN Have the best HTTP Browsing success rate.
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 1
MOOV | 0.9955
CELTISS | 0.9877

## Slide 43: Benchmarking – 4G FTP THROUGHPUT comparison CELLTISS failed in DL ftp SR service
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9967 | 1
MOOV | 1 | 1
CELTISS | 0.9539 | 0.9714

## Slide 44: Benchmarking – 4G FTP THROUGHPUT comparison MTN is ranked first in all kinds of 4G FTP tests
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 29498.84 | 15470.95 | 190101.62 | 33054.88
MOOV | 12899.09 | 11821.62 | 188111.17 | 21203.09
CELTISS | 12572.95 | 10259.33 | 25774.77 | 16058.12

## Slide 45: Benchmarking – 4G FTP THROUGHPUT comparison map MTN Shows the best 4G FTP throughput samples distribution.

## Slide 46: Benchmarking – BAND and TECHNOLOGY UTILISATION Most of MTN LTE samples are in 2600 band. Most of CELTIS LTE samples are in 1800 band. Most of MOOV LTE samples are in 2600 band Usage of 3G U900 is lower for CELTISS
Chart: 3G band Distribution(%)
| UMTS 900 | UMTS 2100
MTN | 0.1596 | 0.8404
MOOV | 0.2192 | 0.7808
CELTISS | 0.0495 | 0.9505
Chart: 4G Band Distribution (%)
| LTE 800 | LTE 700 | LTE 1800 | LTE 2100 | LTE 2600
MTN | 0.018 | 0.1156 | 0.0239 | 0 | 0.8425
MOOV | 0.1937 | 0 | 0 | 0 | 0.8063
CELTISS | 0.1937 | 0 | 0.8063 | 0 | 0

## Slide 47: Benchmarking – Data TECHNOLOGY Usage(%)
Chart: 3G Packet Technology usage (%)
| DC-HSPA | HSPA | HSDPA | UMTS
MTN | 0.5208 | 0.0772 | 0 | 0.4021
MOOV | 0.3743 | 0.3265 | 0 | 0.2992
CELTISS | 0.4349 | 0.044 | 0.0254 | 0.4957
Chart: 4G Packet Technology usage (%)
| LTE | LTE CA
MTN | 0.1233 | 0.8767
MOOV | 0.4384 | 0.5616
CELTISS | 0.4859 | 0.5141

## Slide 48
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2023 Deloitte Bénin SARL. Société du réseau Deloitte