## Slide 1: Benchmarking Voice service Band usage(%) MTN has 40% of voice calls carried by 2G, CELTISS and MOOV have more than 98% of voice calls carried by 3G, Recommended for MTN to reduce 2G utilization and increase 3G penetration for better audio quality. MTN's 2G band usage: 76,57% GSM 900 and 23,43% GSM 1800 Mhz, 3G band usage: MTN uses mainly UMTS2100, CELTISS uses mainly UMTS900 and MOOV has an equitable utilization for both bands U2100 and U900.
Chart: System Technology usage(%)
| GSM | UMTS
MTN | 0.1951 | 0.8049
MOOV | 0.0059 | 0.9941
CELTISS | 0.0165 | 0.9835
Chart: 2G band usage(%)
| GSM 900 | GSM 1800
MTN | 0.7521 | 0.2479
MOOV | 0.6912 | 0.3088
CELTISS | 0.7663 | 0.2337
Chart: 3G band usage(%)
| UMTS 900 | UMTS 2100
MTN | 0.3331 | 0.6669
MOOV | 0.33 | 0.6667
CELTISS | 0.215 | 0.785

## Slide 2: Benchmarking: Voice quality 3G Codec Rate distribution AMR WB HD-voice is activated in MTN’s and CELTISS’s Network. AMR WB 12,65 is the main used codec for MTN.
Chart: MTN 3G codec distibution (%)
| UMTS FDD NB 12.2 | UMTS FDD NB 5.9 | UMTS FDD NB 7.4 | UMTS FDD WB 12.65 | UMTS FDD WB 15.85
 | 0.3 | 0.0014 | 0.0048 | 0.6561 | 0.0048
Chart: MTN 2G codec distibution (%)
| GSM Full rate NB 12.2 | GSM Full rate NB 7.4 | GSM Half rate NB 4.75 | GSM Half rate NB 5.9 | GSM Half rate NB 7.4 | GSM Wideband rate WB 12.65 | GSM Wideband rate WB 6.6 | GSM Wideband rate WB 8.85
 | 0.054008 | 0.07755 | 0.021947 | 0.092765 | 0.20304 | 0.23798 | 0.21355 | 0.099167
Chart: MOOV 3G codec distibution (%)
| UMTS FDD NB 10.2 | UMTS FDD NB 12.2 | UMTS FDD NB 4.75 | UMTS FDD NB 7.95
 | 0.0056 | 0.9698 | 0.008 | 0.0166
Chart: MOOV 2G codec distibution (%)
| GSM Full rate NB 12.2 | GSM Full rate NB 4.75 | GSM Full rate NB 5.9 | GSM Full rate NB 7.4
 | 0.63434 | 0.09221 | 0.11129 | 0.16216
Chart: CELTISS 3G codec distibution (%)
| UMTS FDD NB 12.2 | UMTS FDD WB 12.65
 | 0.97843 | 0.021574
Chart: CELTISS 2G codec distibution (%)
| GSM Full rate NB 12.2 | GSM Full rate NB 4.75 | GSM Full rate NB 5.9 | GSM Full rate NB 7.4 | GSM Half rate NB 4.75 | GSM Half rate NB 5.9 | GSM Half rate NB 7.4
 | 0.29674 | 0.20226 | 0.20346 | 0.19037 | 0.045729 | 0.027397 | 0.034045

## Slide 3: Benchmarking – BAND and TECHNOLOGY UTILISATION Most of MTN LTE samples in Cotonou are in 2600 band. Most of MOOV LTE samples in Cotonou are in 800 band and 2600 band. Most of MOOV LTE samples in Cotonou are in 1800 band. Usage of 3G U900 is very low for competitors.
Chart: 3G Band Distribution (%)
| 900 | 2100
MTN | 0.2488 | 0.7512
MOOV | 0.1269 | 0.8731
CELTISS | 0.0542 | 0.9458
Chart: 4G Band Distribution (%)
| LTE 800 | LTE 700 | LTE 1800 | LTE 2100 | LTE 2600
MTN | 0.0792 | 0.0428 | 0.0308 | 0.0033 | 0.8439
MOOV | 0.3978 | 0 | 0.0206 | 0.0005 | 0.5811
CELTISS | 0.2786 | 0 | 0.6874 | 0.0011 | 0.0329

## Slide 4: Benchmarking – Data TECHNOLOGY Usage(%) MTN has the highest LTE CA Carrier Aggregation usage. HSDPA-DC not used for MTN.
Chart: 4G Packet Technology Usage(%)
| LTE | LTE CA
MTN | 0.177 | 0.823
MOOV | 0.4639 | 0.5361
CELTISS | 0.4986 | 0.5014
Chart: 3G Packet Technology Usage(%)
| DC-HSPA | HSPA | HSDPA | UMTS
MTN | 0.2916 | 0.3022 | 0.0012 | 0.4051
MOOV | 0.4583 | 0.1291 | 0.0035 | 0.4091
CELTISS | 0.4496 | 0.0448 | 0.0253 | 0.4803

## Slide 5: Benchmarking – Data 4G Carrier Aggregation Usage(%) MTN has the highest LTE CA Carrier Aggregation 3CC usage 70.5% compared to 23.59% for MOOV and 0% for CELTISS.
Chart: MTN - Carrier aggregation usage (%)
| 3CC | 2CC | LTE
 | 0.441 | 0.376 | 0.183
Chart: MOOV - Carrier aggregation usage (%)
| 3CC | 2CC | LTE
 | 0.0992 | 0.5839 | 0.3169
Chart: CELTISS - Carrier aggregation usage (%)
| 3CC | 2CC | LTE
 | 0.0244 | 0.4925 | 0.4831

## Slide 6: Benchmarking – Data 4G MIMO usage (%)
Chart: MTN MIMO usage (%)
| Rank 1 | Rank 2 | Rank 3 | Rank 4
 | 0.2722 | 0.6527 | 0.0745 | 0.0006
Chart: MOOV MIMO usage (%)
| Rank 1 | Rank 2 | Rank 3
 | 0.4411 | 0.5255 | 0.0329
Chart: CELTISS MIMO usage (%)
| Rank 1 | Rank 2 | Rank 3
 | 0.2964 | 0.6597 | 0.0419

## Slide 7: Benchmarking – Data 4G detected Bandwidth MTN has the highest LTE Bandwidth, LTE BW: 60 MHz for MTN compared to 40 MHz for MOOV and 30MHz for CELTISS.
Chart: CELTISS-LTE Bandwidh (MHz)
| Bandwidh
LTE 800 | 10
LTE 1800 | 20
Chart: MOOV-LTE Bandwidth (MHz)
| Bandwidh
LTE 800 | 10
LTE 1800 | 10
LTE 2600 | 20
Chart: MTN-LTE Bandwidh
| Bandwidh
LTE 700 | 10
LTE 800 | 10
LTE 1800 | 10
LTE 2100 | 10
LTE 2600 | 20