## Slide 1
Network QoS
Benchmarking report « DJOUGOU »
November 7th, 2023

## Slide 2: Summary
Scope of Intermediate Report | 3
Executive Summary | 5
Benchmarking Key Results | 11
Benchmarking Coverage | 16
Benchmarking Voice Service | 23
Benchmarking Data Service | 33

## Slide 3
Introduction: Scope of Intermediate Report
01

## Slide 4: Intermediate report
Scope of this report
  1. Network benchmarking results for the DJOUGOU area between MTN, MOOV, and CELTISS from October 29th to October 31th, 2023..

## Slide 5
Benchmarking Executive Summary
02

## Slide 6: Executive Summary – Benchmarking coverage 2G/3G/4G
Coverage 2G/3G/4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Tune and align power settings mainly in 3G/4G. Actual setting may impact the coverage strength specially at Indoor locations
Review the design at the coverage and quality blackspots
We highlight that 4G ARCEP coverage Thresholds are aggressive
* Final recommendations will be shared in the final report including details and findings from ongoing Configuration Audit
For 2G RF coverage, all operators meet ARCEP obligation for all morphologies,
MTN is ranked second in term of 2G coverage for Indoor morphology and ranked third for Incar and outdoor morphologies,
MTN is leading in terms of 3G coverage rate with (91,33%) against (90,65%) for CELTISS and (76,30%) for MOOV
Only MTN and CELTISS meet ARCEP 3G coverage obligation
MTN has the best 4G coverage for Indoor and outdoor morphologies,
All operators failed to satisfied the ARCEP threshold for indoor coverage for 4G network.

## Slide 7: Executive Summary – Benchmarking voice service 2G/3G
Voice service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Accessibility: MTN is ranked third in terms of accessibility to voice service ,
MTN and CELTISS failed to meet ARCEP accessibility thresholds,
Retainability: MTN is ranked first in term of retainability better than MOOV and CELTISS,
MTN's Call Drop Rate is 0.44% compared to 2.96% for CELTISS and 0.55% for MOOV. Only MTN and CELTISS meet ARCEP retainabilty requirements,
Integrity: MTN is in third position in terms of voice quality lower than MOOV and CELTISS with average Mean Opinion Score 3.87 as opposed to 3.91 for CELTISS and 4.09 for MOOV.
Voice quality is always better in 3G due to its better codec rate , we recommend to push as much as possible the voice traffic to 3G.
Actual selection/reselection/Irat parameters need to be reviewed and aligned.
2G Full Rate/Half Rate settings need to be tuned in order to improve Full rate penetration
* Final recommendations will be shared in the final report including details and findings from ongoing Configuration Audit

## Slide 8: Executive Summary – Benchmarking SMS service
SMS service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
In DJOUGOU, MTN has an excellent performance for SMS service and satisfys alone the ARCEP requirements.
In DJOUGOU, MTN has recorded an excellent performance for SMS service.

## Slide 9: Executive Summary – Benchmarking 4G Data service
Data service 4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 4G data service, and all operators meet ARCEP's requirements.
MTN is leading in terms of 4G DL throughput with 38.98Mbps, better than MOOV 17.04Mbps and CELTISS 12.89Mbps.
MTN is ranked first in terms of 4G UL throughput with 18.16Mbps, as opposed to 11.62Mbps for MOOV and 11.56Mbps for CELTISS.
For 4G network, all operators meet ARCEP’s End User Throughput obligation in download and upload.
In DJOUGOU, MTN has an excellent performance in terms of 4G End User KPIs.

## Slide 10: Executive Summary – Benchmarking 3G Data service
Data service 3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 3G data service, and all operators meet ARCEP's requirements.
MTN is in third position for 3G DL throughput with 4.62Mbps, compared to 6.82Mbps for CELTISS and 4.74Mbps for MOOV.
MTN is ranked first in terms of 3G UL throughput with 2.35 Mbps against 1.52Mbps for MOOV and 1.88Mbps for CELTISS,
All operators meets ARCEP’s 3G End User Throughput obligation for download and upload.
All operators meet ARCEP’s web browsing service accessibility thresholds.
Its recommended to push as much as possible the data traffic to 4G in order to:
- Improve end user perception, Both DT and stats are showing that users in average are served with up to 700% better throughput in 4G than in 3G
- Offload the 3G network which will improve the 3G throughput and the 3G radio quality
Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles
* Final recommendations will be shared in the final report including details and findings from ongoing Configuration Audit

## Slide 11
Benchmarking Key Results
03

## Slide 12: Benchmarking Key Results – Coverage In DJOUGOU, MOOV has the best 3G coverage for all morphologies, MTN has the best 3G coverage, MTN has the best 4G coverage for Indoor and outdoor morphologies, All operators failed to meet ARCEP requirements for 4G Indoor coverage.
KPI |  | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
2G Coverage Rate | Incar | More than 90% with Incar: Rxlev >-87 dBm | 97,87% | OK | 99,36% | OK | 99,36% | OK | 3
 | Outdoor | More than 90% with Outdoor: Rxlev >-92 dBm | 99,58% | OK | 99,98% | OK | 99,91% | OK | 2
 | Indoor | More than 90% with Outdoor: Rxlev >-74 dBm | 91,05% | OK | 96,28% | OK | 85,66% | NOK | 2
3G Coverage Rate | Incar,Indoor,Outdoor | More than 90% with RSCP <-85 dBm | 91,33% | OK | 76,30% | NOK | 90,65% | OK | 1
4G Coverage Rate | Incar | More than 90% with RSRP <-90 dBm* | 91,50% | OK | 93,39% | OK | 89,50% | NOK | 2
 | Outdoor | More than 90% with RSRP <-95 dBm* | 98,92% | OK | 96,73% | OK | 97,96% | OK | 1
 | Indoor | More than 90% with RSRP <-78 dBm* | 46,25% | NOK | 37,39% | NOK | 20,63% | NOK | 1

## Slide 13: Benchmarking Key Results – 2G/3G voice and SMS Summary MTN is ranked third in terms of accessibility to voice service , MTN is leading in retainability by having the lowest Call Drop Rate(%), In DJOUGOU, MTN has an excellent performance for SMS service and satisfys alone the ARCEP requirements, MTN is ranked third in term of voice quality MOS but satisfys ARCEP requirements.
KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  | Value | Conformity | Value | Conformity | Value | Conformity | 
Accesibility: Blocking rate | <1% | 2,70% | NOK | 2,02% | NOK | 0,97 | OK | 3
Retainability: Call drop rate | <1% | 0,44% | OK | 2,96% | NOK | 0,95% | OK | 1
Call Completetion Rate (%) | =<98% | 96,86% | NOK | 95,02% | NOK | 98,02% | OK | 2
Integrity: Voice quality | Note requise> 2,8 | 3,87 | OK | 4,09 | OK | 3,91 | OK | 3
SMS sending success rate % (E2E delivery Time<6 sec) | >99% | 99,45% | OK | 92,43% | NOK | 90,84% | NOK | 1
SMS receving success rate % | >99% | 99,17% | OK | 91,33% | NOK | 88,97% | NOK | 1

## Slide 14: Benchmarking Key Results – 3G Data Summary MTN’s network in 3G DATA meets ARCEP requirements.
Services | KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
3G HTTP | Successful internet connexion rate | >96% | 98,44% | OK | 98,10% | OK | 98,58% | OK | 2
 | Connexion setup time | <=10sec | 5,78 | OK | 6,29 | OK | 6,19 | OK | 1
 | Web service failure rate | <3% | 0,35% | OK | 1,22% | OK | 0,19% | OK | 2
3G FTP | FTP failure rate UL/DL | <3 % | 0%/0% | OK | 2,06%/0,37% | OK | 0%/0,19% | OK | 1
 | FTP Data transmission average (DL) | >= 2Mbps | 4,622 | OK | 4,717 | OK | 6,828 | OK | 3
 | FTP Data transmission average (UL) | >= 1Mbps | 2,355 | OK | 1,527 | OK | 1,880 | OK | 1

## Slide 15: Benchmarking Key Results – 4G Data Summary MTN’s 4G DATA End User KPIs satisfy extensively ARCEP requirements, MTN is ranked first in terms of FTP DL/UL throughput, MTN has an excellent FTP DL throughput with 38,98Mbps against 17,04Mbps for MOOV and 12,89Mbps for CELTISS.
Services | KPI | Threshorlds* | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
4G HTTP Browsing | Web service failure rate (%) | <3% | 0% | OK | 1,61% | OK | 0,92% | OK | 1
 | Connexion setup time | <=3sec | 1,07 | OK | 0,98 | OK | 1,12 | OK | 2
4G FTP | FTP failure rate UL/DL | <3 % | 0%/0% | OK | 0,33%/0,34% | OK | 0%/0% | OK | 1
 | FTP Data transmission average (DL) | 4G >= 5 Mbps | 38,987 | OK | 17,045 | OK | 12,899 | OK | 1
 | FTP Data transmission average (UL) | 4G: >= 2Mbps | 18,164 | OK | 11,628 | OK | 11,562 | OK | 1

## Slide 16
Benchmarking 2G/3G/4G coverage
04

## Slide 17: Benchmarking: 2G coverage MTN’s, MOOV’s and CELTISS’s 2G coverage meets ARCEP RxLev thresholds, MTN needs to improve its 2G indoor coverage.
Chart: 2G RxLev Distribution (%)
| Indoor>-74 | Incar >-87 | Outdoor >-92
MTN | 0.9105 | 0.9787 | 0.9958
MOOV | 0.9628 | 0.9936 | 0.9998
CELTISS | 0.8566 | 0.9936 | 0.9991

## Slide 18: Benchmarking: 2G coverage - Maps MOOV has the best ratio of RxLev samples great than -74dBm.

## Slide 19: Benchmarking: 3G coverage In DJOUGOU, MTN has the best 3G coverage and meets ARCEP requirements.
Chart: 3G RSCP Distribution (%)
| Indoor,Incar,Outdoor >-85
MTN | 0.9133
MOOV | 0.763
CELTISS | 0.9065

## Slide 20: Benchmarking: 3G coverage-Maps In DJOUGOU, MTN is clair leader in terms of 3G coverage and has the best distribution of RSCP samples.

## Slide 21: Benchmarking: 4G coverage MTN's 4G Radio coverage meets ARCEP requirements for Incar and outdoor morphologies. For Indoor coverage, all operators failed to meet ARCEP requirements but MTN has the best ratio.
Chart: 4G RSRP Distribution (%)
| Indoor > -78 | Incar > -90 | Outdoor > -95
MTN | 0.4625 | 0.915 | 0.9892
MOOV | 0.3739 | 0.9339 | 0.9873
CELTISS | 0.2063 | 0.895 | 0.9798

## Slide 22: Benchmarking – 4G coverage - Maps MTN’s 4G coverage is better than MOOV’s and CELTISS’s.

## Slide 23
Benchmarking voice service
05

## Slide 24: Benchmarking: CS Accessibility 2G/3G BLOCKED CALLS In DJOUGOU, MTN has the worst accessibility to voice service compared to competitors, MTN exceeds ARCEP requirements in terms of accessibility.
Chart: Call Blocked Rate (%)
| CBR (%)
MTN | 0.027
MOOV | 0.0202
CELTISS | 0.0097
Chart: Call Blocked Rate per Technology (%)
| CBR (%)
MTN 2G | 0
MTN 3G | 0.0171
MOOV 2G | 0
MOOV 3G | 0.0196
CELTISS 2G | 0
CELTISS 3G | 0.0082

## Slide 25: Benchmarking: CS Integrity Voice quality Mean Opinion Score In DJOUGOU, CELTISS has the best ratio of excellent and good Voice Quality samples and MOS compared to MTN and MOOV.MTN needs to improve its voice quality MOS by pushing CS traffic to 3G as much as possible and improving 3G radio pamameter Ec/No.
Chart: Average MOS
| Avrege MOS
MTN | 3.87
MOOV | 4.09
CELTISS | 3.91
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Excellent+Good
MTN | 0.4361 | 0.5226 | 0.0246 | 0.0167 | 0.9587
MOOV | 0.8241 | 0.1286 | 0.0288 | 0.0185 | 0.9527
CELTISS | 0.446 | 0.5432 | 0.0091 | 0.0034 | 0.9892

## Slide 26: Benchmarking – CS Integrity Voice quality maps (MOS) MTN has around 4,13% of MOS samples lower than 2.2 against 1,08% for CELTISS and 4,73 for MOOV MOS Values lower than 2,2 pose risk of bad users perceived voice quality and silent calls. 3d

## Slide 27: Benchmarking: CS Retainability 2G/3G DROPPED CALLS MTN is clair leader in terms of retainability by having the best CDR(%), MTN and CELTISS satisfy ARCEP thresholds regarding Call Drop Rate.
Chart: Call Drop Rate (%)
| CDR (%)
MTN | 0.0044
MOOV | 0.0296
CELTISS | 0.0095

## Slide 28: Benchmarking Voice service Band usage(%) All operators have more than 96% of voice calls carried out over 3G, MTN and CELTISS use mainly UMTS2100 (>75%).
Chart: System Technology usage(%)
| GSM | UMTS
MTN | 0.0376 | 0.9624
MOOV | 0.001 | 0.999
CELTISS | 0.0179 | 0.9821
Chart: 2G band usage(%)
| GSM 900 | GSM 1800
MTN | 0.702 | 0.298
MOOV | 0.2 | 0.8
CELTISS | 0.1784 | 0.8216
Chart: 3G band usage(%)
| UMTS 900 | UMTS 2100
MTN | 0.211 | 0.789
MOOV | 0.5742 | 0.4258
CELTISS | 0.2205 | 0.7795

## Slide 29: Benchmarking: Radio parameters EC/NO comparison 11,39% of drive test samples are showing a very low level of EcNo for 3G MTN opposed to MOOV 5,64% and CELTISS 1,25%. MTN needs to improve its Ec/No samples ditribution in order to improve voice quality MOS.
Chart: 3G Ec/No Distribution (%)
| -8 to 0 | -12 to -8 | -16 to -12 | -34 to -16 | ACCEPTABLE EC/N0
MTN | 0.1706 | 0.2563 | 0.4591 | 0.1139 | 0.4269
MOOV | 0.2354 | 0.3928 | 0.3154 | 0.0564 | 0.6282
CELTISS | 0.5389 | 0.3635 | 0.0851 | 0.0125 | 0.9024

## Slide 30: Benchmarking: Radio parameters EC/NO 3G MOOV’s and CELTISS’s EC/N0 is better than MTN’s due to the number of 3G used carriers .

## Slide 31: Benchmarking – 2G/3G CALL SETUP TIME MTN is clear leader in terms of Call Setup Time.
Chart: Call Setup Time (s)
| Call Setup Time
MTN | 6.14
MOOV | 7.52
CELTISS | 7.59
Chart: CS Call setup Time by technology (s)
| 4G CSFB CST | 3G CST | 2G CST
MTN | 6.05 | 5.52 | 6.87
MOOV | 7.06 | 7.98
CELTISS | 7.44 | 7.56 | 7.77

## Slide 32: Benchmarking – SMS Service MTN has outperformed its competitors in terms of SMS service, In DJOUGOU, Compared to others areas, MTN has an excellent SMS performance.
Chart: SMS
| SMS Sending message success rate (%) | SMS Receving message success rate (%)
MTN | 0.9945 | 0.9917
MOOV | 0.9243 | 0.9133
CELTISS | 0.9084 | 0.8897
Chart: SMS Send Time(%)
| (0,3) | (3,6) | >6
MTN | 0.5546 | 0.4399 | 0.0055
MOOV | 0.5267 | 0.3976 | 0.0757
CELTISS | 0.4811 | 0.4273 | 0.0916

## Slide 33
Benchmarking Data service
06

## Slide 34: Benchmarking – DATA 3G All operators have a good rate of successful Internet connection.
Chart: PS Attach & PDP Contex Act(%)
| PS Attach success(%) | PDP Context Act Success (%)
MTN | 0.9844 | 1
MOOV | 0.981 | 1
CELTISS | 0.9856 | 0.9981
Chart: Attach & PDP Activation Time (s)
| PS Attach Setup Time | PDP Context Act Time
MTN | 1.65 | 1.16
MOOV | 1.82 | 1.71
CELTISS | 2.01 | 1.49

## Slide 35: Benchmarking – DATA 3G Web Browsing service All operators have very good web service success rate and meet ARCEP requirements. MTN has the best PS connection setup time.
Chart: PS Connection setup time
| PS Connection setup time
MTN | 5.78
MOOV | 6.29
CELTISS | 6.19
Chart: 3G HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9965
MOOV | 0.9878
CELTISS | 0.9981

## Slide 36: Benchmarking – DATA 3G MTN has an excellent performance for downlink and uplink FTP success rate.
Chart: 3G FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 1 | 1
MOOV | 0.9794 | 0.9963
CELTISS | 1 | 0.9981

## Slide 37: Benchmarking – 3G FTP MEAN THROUGHPUT MTN’s 3G dowlink Throughput is less than MOOV’s and CELTISS’s, MTN has the best 3G UL thropughput.
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 4622.48 | 2355.19 | 16245.97 | 11024.54
MOOV | 4717.91 | 1527.06 | 12608 | 10108.26
CELTISS | 6828.5 | 1880.52 | 13542.02 | 9559.88

## Slide 38: Benchmarking – 3G FTP MEAN THROUGHPUT comparison map All operators meet ARCEP requirements by having 100% of 3G DL throughput samples better than 2Mbps.

## Slide 39: Benchmarking – 4G HTTP Browsing service All operators have very good HTTP Browsing success rate.
Chart: 4G HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 1
MOOV | 0.9839
CELTISS | 0.9908

## Slide 40: Benchmarking – 4G FTP THROUGHPUT comparison MTN’s 4G network has an excellent FTP success rate.
Chart: 4G FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 1 | 1
MOOV | 0.9967 | 0.9966
CELTISS | 1 | 1

## Slide 41: Benchmarking – 4G FTP THROUGHPUT comparison In DJOUGOU, MTN is leading in terms of FTP DL/UL AVERAGE Throughput, MTN has outperformed its competitors with an excellent DL/UL speed.
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 38987.91 | 18164.79 | 170709.66 | 34333.55
MOOV | 17045.28 | 11628.13 | 185108.91 | 24365.11
CELTISS | 12899.65 | 11562.18 | 29215.09 | 13012.47

## Slide 42: Benchmarking – 4G FTP THROUGHPUT comparison map In DJOUGOU, MTN has an excellent end user throughput with more than 40,37% of samples better than 30Mbps .

## Slide 43: Benchmarking – BAND and TECHNOLOGY UTILISATION Most of MTN’s and MOOV’s LTE samples are carried out over LTE 2600 as first carrier, Most of CELTISS’s samples are carried out over LTE 1800 as first carrier, For all operators, most of 3G samples are carried out over U2100.
Chart: 3G band Distribution (%)
| UMTS 900 | UMTS 2100
MTN | 0.0986 | 0.9014
MOOV | 0.2255 | 0.7745
CELTISS | 0.0377 | 0.9623
Chart: 4G Band Distribution (%)
| LTE 800 | LTE 700 | LTE 1800 | LTE 2100 | LTE 2600
MTN | 0.2459 | 0 | 0.0069 | 0 | 0.7472
MOOV | 0.417 | 0 | 0 | 0 | 0.583
CELTISS | 0.1778 | 0 | 0.8081 | 0 | 0.0141

## Slide 44: Benchmarking – Data TECHNOLOGY Usage(%) MTN has the highest LTE CA Carrier Aggregation usage with 83,40% against 48,91% for MOOV and 50,75% for CELTISS.
Chart: 3G Packet Technology usage (%)
| DC-HSPA | HSPA | HSDPA | UMTS
MTN | 0.5129 | 0.0759 | 0 | 0.4112
MOOV | 0.4392 | 0.1513 | 0 | 0.4094
CELTISS | 0.4377 | 0.0359 | 0.0262 | 0.5002
Chart: 4G Packet Technology usage (%)
| LTE | LTE CA
MTN | 0.166 | 0.834
MOOV | 0.5109 | 0.4891
CELTISS | 0.4925 | 0.5075

## Slide 45: Benchmarking – SINR comparison Drive tests are showing a acceptable level of MTN Network SINR.
Chart: 4G SINR Comparison
| (Min,-4) | (-4,0) | (0,7) | (7,15 <) | ACCEPTABLE SINR
MTN | 0.0175 | 0.0604 | 0.2902 | 0.6319 | 0.9221
MOOV | 0.0146 | 0.1009 | 0.3611 | 0.5234 | 0.8845
CELTISS | 0.0037 | 0.0165 | 0.1699 | 0.8099 | 0.9798

## Slide 46: Benchmarking – SNIR comparison map Drive tests are showing an acceptable level of MTN Network SINR.

## Slide 47
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2023 Deloitte Bénin SARL. Société du réseau Deloitte