## Slide 1
Network QoS
LOKOSSA Benchmarking report
November23th, 2023

## Slide 2: Summary
Scope of Intermediate Report | 3
Executive Summary | 5
Benchmarking Key Results | 11
Benchmarking Coverage | 16
Benchmarking Voice Service | 23
Benchmarking Data Service | 33

## Slide 3
Introduction: Scope of Benchmarking Report «
01

## Slide 4: Intermediate report
Scope of this report
  1. Network benchmarking results for the BOHICON area between MTN, MOOV, and CELTISS from October 20th to October 21th, 2023..

## Slide 5
Benchmarking Executive Summary
02

## Slide 6: Executive Summary – Benchmarking coverage 2G/3G/4G
Coverage 2G/3G/4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Tune and align power settings mainly in 3G/4G. Actual setting may impact the coverage strength specially at Indoor locations
Review the design at the coverage and quality blackspots
We highlight that 4G ARCEP coverage Thresholds are aggressive
* Final recommendations will be shared in the final report including details and findings from ongoing Configuration Audit
MTN has outperformed its competitors in terms of 2G coverage for outdoor and Indoor morphologies ,
For 2G RF coverage, Only MTN meets ARCEP obligation for all morphologies,
MTN is leading in terms of 3G coverage rate with (94,09%) against (86,16%) for CELTISS and (88,98%) for MOOV
Only MTN meets ARCEP 3G coverage obligation
MTN is in the second position in terms of 4G coverage rate for Incar and Outdoor morphologies but meets ARCEP thresholds,
All operators failed to satisfied the ARCEP threshold for indoor coverage for 4G network.

## Slide 7: Executive Summary – Benchmarking voice service 2G/3G
Voice service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Accessibility: MTN is leading in terms of accessibility to voice service by having the best Call Blocked ratio with 0,58% against 0,86% for MOOV and 0,84% for CELTISS,
All operators failed to meet ARCEP accessibility thresholds,
Retainability: MTN is ranked first in term of retainability better than MOOV and CELTISS,
MTN's Call Drop Rate is 0.38% compared to 0.78% for CELTISS and 0.55% for MOOV.All operators meet ARCEP retainabilty requirements,
Integrity: MTN is in second position in terms of voice quality with average Mean Opinion Score equal to 4,02 lower than MOOV 4,21 and better than CELTISS 3,94
In LOKOSSA the MTN’s MOS value is better than other area, because the voice quality is carried out mainly over 3G unlike other areas .
Voice quality is always better in 3G due to its better codec rate , we recommend to push as much as possible the voice traffic to 3G,
Drive test results are showing that MTN has a bad Ec/No, by improving this radio parameter we can improve further the voice quality MOS.
further

## Slide 8: Executive Summary – Benchmarking SMS service
SMS service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
All operators failed to meet ARCEP for SMS Send Success with End To End Delivery Time who should be less than < 6 sec as defined by ARCEP.
MTN is better than MOOV and lower than CELTISS.
There is no issue in radio accessibility that could be correlated to the SMS high delivery time.
End to End investigation need to be performed to analyses the high delivery time including mainly Core/SMS parts: SM Sserver...
* Final recommendations will be shared in the final report including details and findings from ongoing Configuration Audit

## Slide 9: Executive Summary – Benchmarking 4G Data service
Data service 4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 4G data service, and all operators meet ARCEP's requirements.
MTN is leading in terms of 4G DL throughput with 57.41Mbps, better than MOOV 27.51Mbps and CELTISS 12.93Mbps.
MTN is ranked first in terms of 4G UL throughput with 18.74Mbps, as opposed to 13.53Mbps for MOOV and 11.47Mbps for CELTISS.
For 4G network, all operators meet ARCEP’s End User Throughput obligation in download and upload.
In LOKOSSA, MTN has an excellent performance in term of 4G KPIs.

## Slide 10: Executive Summary – Benchmarking 3G Data service
Data service 3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 3G data service, and all operators meet ARCEP's requirements.
MTN is in third position for 3G DL throughput with 2.2Mbps, compared to 4.62Mbps for CELTISS and 3.33Mbps for MOOV.
MTN is ranked second in term of 3G UL throughput with 1.04 Mbps against 1.01 Mbps for MOOV and 2.15Mbps for CELTISS,
All operators meets ARCEP’s 3G End User Throughput obligation for download and upload.
All operators meet ARCEP’s web browsing service accessibility thresholds.
Its recommended to push as much as possible the data traffic to 4G in order to:
- Improve end user perception, Both DT and stats are showing that users in average are served with an excellent throughput in 4G,
- Offload the 3G network which will improve the 3G throughput and the 3G radio quality
Increasing the utilization of 3G data technology HSPA-DC can improve 3G throughput,
Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles

## Slide 11
Benchmarking Key Results
03

## Slide 12: Benchmarking Key Results – Coverage For 2G RF coverage, Only MTN meets ARCEP obligation for all morphologies, In LOKOSSA, MTN has recorded the best RF 3G coverage, MTN is ranked second in term of RF 4G coverage for Incar and outdoor morphologies, All operators failed to meet ARCEP requirements for 4G indoor coverage.
KPI |  | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
2G Coverage Rate | Incar | More than 90% with Incar: Rxlev >-87 dBm | 98,11% | OK | 98,48% | OK | 98,06% | OK | 2
 | Outdoor | More than 90% with Outdoor: Rxlev >-92 dBm | 99,97% | OK | 99,73% | OK | 99,62% | OK | 1
 | Indoor | More than 90% with Outdoor: Rxlev >-74 dBm | 91,02% | OK | 88,82% | NOK | 86,16% | NOK | 1
3G Coverage Rate | Incar,Indoor,Outdoor | More than 90% with RSCP <-85 dBm | 94,09% | OK | 88,98% | NOK | 86,69% | NOK | 1
4G Coverage Rate | Incar | More than 90% with RSRP <-90 dBm* | 90,75% | OK | 91,91% | OK | 78,56% | NOK | 2
 | Outdoor | More than 90% with RSRP <-95 dBm* | 97,32% | OK | 99,36% | OK | 93,38% | OK | 2
 | Indoor | More than 90% with RSRP <-78 dBm* | 58,04% | NOK | 59,69% | NOK | 64,80% | NOK | 3

## Slide 13: Benchmarking Key Results – 2G/3G voice and SMS Summary MTN is leading in accessibility and retainability in LOKOSSA, MTN is ranked second in terms of voice quality MOS but satisfys ARCEP requirements, MTN needs to improve its SMS Send duration, All operators failed to meet ARCEP requirements for SMS service due to due to the timeout of sending duration that should be less than (< 6s).
KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  | Value | Conformity | Value | Conformity | Value | Conformity | 
Accesibility: Blocking rate | <1% | 0,58% | OK | 0,86% | OK | 0,84 | OK | 1
Retainability: Call drop rate | <1% | 0,38% | OK | 0,55% | OK | 0,78% | OK | 1
Call Completetion Rate (%) | =<98% | 99,04% | OK | 98,56% | OK | 98,38% | OK | 1
Integrity: Voice quality | Note requise> 2,8 | 4,02 | OK | 4,21 | OK | 3,94 | OK | 2
SMS sending success rate % (E2E delivery Time<6 sec) | >99% | 97,51% | NOK | 91,80% | NOK | 98,89% | NOK | 2
SMS receving success rate % | >99% | 96,33% | NOK | 89,01% | NOK | 96,46% | NOK | 2

## Slide 14: Benchmarking Key Results – 3G Data Summary MTN network in 3G DATA meets ARCEP requirements, MTN has the lowest FTP DL/UL throughput.
Services | KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
3G HTTP | Successful internet connexion rate | >96% | 100,00% | OK | 99,92% | OK | 100,00% | OK | 1
 | Connexion setup time | <=10sec | 6,09 | OK | 6,12 | OK | 5,87 | OK | 2
 | Web service failure rate | <3% | 2,42% | OK | 0,45% | OK | 1,89% | OK | 3
3G FTP | FTP failure rate UL/DL | <3 % | 0,85%/1,77% | OK | 0,43%/4,98% | OK/NOK | 0%/1,23% | OK | 2
 | FTP Data transmission average (DL) | >= 2Mbps | 3,482 | OK | 4,651 | OK | 7,631 | OK | 3
 | FTP Data transmission average (UL) | >= 1Mbps | 1,156 | OK | 1,272 | OK | 1,986 | OK | 3

## Slide 15: Benchmarking Key Results – 4G Data Summary MTN’s 4G DATA End User KPIs satisfy extensively ARCEP requirements, MTN is ranked first in terms of FTP DL/UL throughput, MTN has an excellent FTP DL throughput with 57,41Mbps against 27,51Mbps for MOOV and 12,93Mbps for CELTISS.
Services | KPI | Threshorlds* | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
4G HTTP Browsing | Web service failure rate (%) | <3% | 0,00% | OK | 0,00% | OK | 0,00% | OK | 1
 | Connexion setup time | <=3sec | 0,47 | OK | 0,58 | OK | 0,62 | OK | 1
4G FTP | FTP failure rate UL/DL | <3 % | 0%/0,87% | OK | 0%/0,47% | OK | 0%/0% | OK | 3
 | FTP Data transmission average (DL) | 4G >= 5 Mbps | 57,419 | OK | 27,516 | OK | 12,933 | OK | 1
 | FTP Data transmission average (UL) | 4G: >= 2Mbps | 18,741 | OK | 13,537 | OK | 11,474 | OK | 1

## Slide 16
Benchmarking 2G/3G/4G coverage
04

## Slide 17: Benchmarking: 2G coverage Only MTN’s 3G coverage meets ARCEP RxLev thresholds for all morphologies Indoor, Incar and outdoor, MTN has the best 2G coverage for Indoor and outdoor categories and closely simular to competitors for Incar category.
Chart: 2G RxLev Distribution (%)
| Indoor>-74 | Incar >-87 | Outdoor >-92
MTN | 0.9102 | 0.9811 | 0.9997
MOOV | 0.8882 | 0.9848 | 0.9973
CELTISS | 0.8616 | 0.9806 | 0.9962

## Slide 18: Benchmarking: 2G coverage - Maps In LOKOSSA, MTN has 91,02% of samples better than -74dBm against 88,82% for MOOV and 86,16% for CELTISS.

## Slide 19: Benchmarking: 3G coverage In LOKOSSA, MTN is clair leader in terms of 3G coverage and alone satisfys the ARCEP requirements.
Chart: 3G RSCP Distribution (%)
| Indoor,Incar,Outdoor >-85
MTN | 0.9409
MOOV | 0.8898
CELTISS | 0.8669

## Slide 20: Benchmarking: 3G coverage-Maps In LOKOSSA, MTS offers the best 3G coverage.

## Slide 21: Benchmarking: 4G coverage MTN is ranked second for 4G coverage for Incar and Outdoor morphologies and meets ARCEP requirements, but all operators failed to meet ARCEP threshold for Indoor category.
Chart: 4G RSRP Distribution (%)
| Indoor > -78 | Incar > -90 | Outdoor > -95
MTN | 0.5804 | 0.9075 | 0.9732
MOOV | 0.5969 | 0.9191 | 0.9936
CELTISS | 0.648 | 0.7856 | 0.9338

## Slide 22: Benchmarking – 4G coverage - Maps MTN’s 4G coverage is lower than MOOV’s and CELTISS, Low 4G coverage was recorded near to the road to Doukonta.

## Slide 23
Benchmarking voice service
05

## Slide 24: Benchmarking: CS Accessibility 2G/3G BLOCKED CALLS MTN has the best accessibility to voice service compared to competitors, All operators satisfy ARCEP requirements.
Chart: Call Blocked Rate (%)
| CBR (%)
MTN | 0.0058
MOOV | 0.0086
CELTISS | 0.0084
Chart: Call Blocked Rate per Technology (%)
| CBR (%)
MTN 2G | 0
MTN 3G | 0.006
MOOV 2G | 0
MOOV 3G | 0.0187
CELTISS 2G | 0.0125
CELTISS 3G | 0.0078

## Slide 25: Benchmarking: CS Integrity Voice quality Mean Opinion Score In LOKOSSA, MTN has the best ratio of excellent and good Voice Quality samples compared to CELTISS’s and MOOV’S. MTN is ranked second in terms of voice quality with an average MOS equal to 4,02 opposed to 4,21 for MOOV and 3,94 for CELTISS.
Chart: Average MOS
| Avrege MOS
MTN | 4.02
MOOV | 4.21
CELTISS | 3.94
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Excellent+Good
MTN | 0.7724 | 0.2252 | 0.0024 | 0 | 0.9976
MOOV | 0.8918 | 0.092 | 0.0068 | 0.0094 | 0.9838
CELTISS | 0.5947 | 0.3959 | 0.0068 | 0.0026 | 0.9906

## Slide 26: Benchmarking – CS Integrity Voice quality maps (MOS) MTN has around 99,76% of MOS samples better than 2.8 against 98,38% for MOOV and 99,1% for CELTISS. 3d

## Slide 27: Benchmarking: CS Retainability 2G/3G DROPPED CALLS MTN is clair leader in term of retainability by having the lowest Call Drop Rate, All operators meets ARCEP requirements.
Chart: Call Drop Rate (%)
| CDR (%)
MTN | 0.0038
MOOV | 0.0055
CELTISS | 0.0078

## Slide 28: Benchmarking Voice service Band usage(%) All operators have more than 97% of voice calls carried out over 3G, All operators use mainly UMTS2100 band.
Chart: System Technology usage(%)
| GSM | UMTS
MTN | 0.0012 | 0.9988
MOOV | 0.0006 | 0.9994
CELTISS | 0.0272 | 0.9728
Chart: 2G Band usage(%)
| GSM 900 | GSM 1800
MTN | 1 | 0
MOOV | 0.3333 | 0.6667
CELTISS | 0.7952 | 0.2048
Chart: 3G Band usage(%)
| UMTS 900 | UMTS 2100
MTN | 0.2217 | 0.7783
MOOV | 0.2635 | 0.7365
CELTISS | 0.249 | 0.751

## Slide 29: Benchmarking: Radio parameters EC/NO comparison 7,42% of drive test samples are showing a very low level of EcNo for 3G MTN opposed to MOOV with 4,63% and CELTISS with 4,88%.
Chart: 3G Ec/No Distribution (%)
| -8 to 0 | -12 to -8 | -16 to -12 | -34 to -16 | ACCEPTABLE EC/N0
MTN | 0.3515 | 0.2387 | 0.3356 | 0.0742 | 0.5902
MOOV | 0.184 | 0.3694 | 0.4004 | 0.0463 | 0.5534
CELTISS | 0.6805 | 0.1969 | 0.0737 | 0.0488 | 0.8774

## Slide 30: Benchmarking: Radio parameters EC/NO MTN has the highest ratio of very bad Ec/No samples (<-16db).

## Slide 31: Benchmarking – 2G/3G CALL SETUP TIME MTN is clear leader in terms of Call Setup Time.
Chart: Call Setup Time (s)
| Call Setup Time
MTN | 5.66
MOOV | 7.14
CELTISS | 7.21
Chart: CS Call setup Time by technology (s)
| 4G CSFB CST | 3G CST | 2G CST
MTN | 5.01 | 5.85 | 4.41
MOOV | 7.98 | 7.22
CELTISS | 7.8 | 7.43 | 8.15

## Slide 32: Benchmarking – SMS Service MTN’s SMS SEND/RECEIVE SR(%) is better than MOOV and less than CELTISS . SMS service KPIs for all operators are not compliant with the ARCEP requirements due to the timeout of sending duration (< 6s).
Chart: SMS Send/Received SR(%)
| SMS Sending message success rate (%) | SMS Receving message success rate (%)
MTN | 0.9751 | 0.9633
MOOV | 0.918 | 0.8901
CELTISS | 0.9889 | 0.9646
Chart: SMS Send Time(%)
| (0,3) | (3,6) | >6
MTN | 0.6581 | 0.317 | 0.0249
MOOV | 0.6133 | 0.3047 | 0.082
CELTISS | 0.6453 | 0.3436 | 0.0111

## Slide 33
Benchmarking Data service
06

## Slide 34: Benchmarking – DATA 3G All operators have a good rate of successful Internet connection.
Chart: PS Attach & PDP Contex Act(%)
| PS Attach success(%) | PDP Context Act Success (%)
MTN | 1 | 0.9905
MOOV | 0.9992 | 0.9898
CELTISS | 1 | 0.9733
Chart: Attach & PDP Activation Time (s)
| PS Attach Setup Time | PDP Context Act Time
MTN | 0.94 | 1.45
MOOV | 1.01 | 1.12
CELTISS | 1.17 | 1.89

## Slide 35: Benchmarking – DATA 3G Web Browsing service MTN has the lowest HTTP browsing success, All operators meet ARCEP requirement for web service.
Chart: PS Connection setup time (sec)
| PS Connection setup time
MTN | 6.09
MOOV | 6.12
CELTISS | 5.87
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9756
MOOV | 0.9955
CELTISS | 0.9811

## Slide 36: Benchmarking – DATA 3G FTP service Only MTN and CELTISS meet ARCEP requirements for FTP DL/UL success ratio. CELTISS has the best FTP DL/UL success ratio.
Chart: 3G FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9915 | 0.9823
MOOV | 0.9957 | 0.9502
CELTISS | 1 | 0.9877

## Slide 37: Benchmarking – 3G FTP MEAN THROUGHPUT MTN 3G Throughput DL/UL is less than MOOV’s and CELTISS’s, but satisfys ARCEP requirements.
Chart: 3G FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 3482.24 | 1156.47 | 21421.47 | 16221.4
MOOV | 4651.89 | 1272.73 | 19541.24 | 17456.07
CELTISS | 7631.54 | 1986.65 | 18172.09 | 8225.22

## Slide 38: Benchmarking – 3G FTP MEAN THROUGHPUT comparison map All operators meets ARCEP requirements with 100% of throughput samples better than 2Mbps.

## Slide 39: Benchmarking – 4G HTTP Browsing All operators have very good HTTP Browsing success rate.
Chart: 4G HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 1
MOOV | 1
CELTISS | 1

## Slide 40: Benchmarking – 4G FTP service All operators have an excellent FTP DL/UL success ratio for 4G network.
Chart: 4G FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 1 | 0.9913
MOOV | 1 | 0.9953
CELTISS | 1 | 1

## Slide 41: Benchmarking – 4G FTP THROUGHPUT comparison In LOKOSSA, MTN is leading in terms of FTP DL/UL AVERAGE Throughput, MTN has outperformed its competitors with an excellent DL/UL speed.
Chart: 4G FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 57419.807 | 18741.88 | 192208.11 | 39935.56
MOOV | 27516.67 | 13537.6 | 199029.09 | 25547.6
CELTISS | 12933.84 | 11474.41 | 25800.11 | 14517.41

## Slide 42: Benchmarking – 4G FTP THROUGHPUT comparison map In LOKOSSA, MTN has an excellent end user throughput with more than 46,13% of samples better than 30Mbps .

## Slide 43: Benchmarking – BAND and TECHNOLOGY UTILISATION Most of MTN’s and MOOV’s LTE samples are carried out over LTE 2600 as first carrier, Most of CELTISS’s samples are carried out over LTE 1800 as first carrier, For all operators,most of 3G samples are carried out over U2100, but MTN has the highest ratio of U900 usage.
Chart: 3G Band Distribution(%)
| UMTS 900 | UMTS 2100
MTN | 0.1053 | 0.8947
MOOV | 0.0653 | 0.9347
CELTISS | 0.0778 | 0.9222
Chart: 4G Band Distribution (%)
| LTE 800 | LTE 700 | LTE 1800 | LTE 2100 | LTE 2600
MTN | 0.0134 | 0.0111 | 0.0246 | 0 | 0.951
MOOV | 0.3405 | 0 | 0.0239 | 0 | 0.6356
CELTISS | 0.3933 | 0 | 0.6067 | 0 | 0

## Slide 44: Benchmarking – Data TECHNOLOGY Usage(%) MTN has the highest LTE CA Carrier Aggregation usage with 83,12% against 52,89% for MOOV and 50,75% for CELTISS.
Chart: 3G Packet Technology usage (%)
| DC-HSPA | HSPA | HSDPA | UMTS
MTN | 0.5165 | 0.0527 | 0.0004 | 0.4304
MOOV | 0.5498 | 0.0116 | 0.0111 | 0.4275
CELTISS | 0.374 | 0.0624 | 0.0177 | 0.5458
Chart: 4G Packet Technology usage (%)
| LTE | LTE CA
MTN | 0.1688 | 0.8312
MOOV | 0.4711 | 0.5289
CELTISS | 0.4925 | 0.5075

## Slide 45: Benchmarking – SINR comparison For 4G Network Drive tests are showing that MTN has the best ratio of acceptable SINR.
Chart: 4G SINR Comparison
| (Min,-4) | (-4,0) | (0,7) | (7,15 <) | ACCEPTABLE SINR
MTN | 0.0073 | 0.0362 | 0.242 | 0.7145 | 0.9565
MOOV | 0.0099 | 0.0512 | 0.3749 | 0.564 | 0.9389
CELTISS | 0.0168 | 0.0316 | 0.1012 | 0.8504 | 0.9516

## Slide 46: Benchmarking – SNIR comparison map MTN has the better quality of signal compared to MOOV and CELTISS.

## Slide 47
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2019 Deloitte Bénin SARL. Société du réseau Deloitte