## Slide 1
Network QoS
NATITINGO Intermediate report
November 23rd, 2023

## Slide 2: Summary
Scope of Intermediate Report | 3
Executive Summary | 5
Benchmarking Key Results | 11
Benchmarking Coverage | 16
Benchmarking Voice Service | 23
Benchmarking Data Service | 33

## Slide 3
Introduction: Scope of Intermediate Report
01

## Slide 4: Intermediate report
Scope of this report
  1. Network benchmarking results for the Natitingo area between MTN, MOOV, and CELTISS from October 21th to October 23th, 2023..

## Slide 5
Benchmarking Executive Summary
02

## Slide 6: Executive Summary – Benchmarking coverage 2G/3G/4G
Coverage 2G/3G/4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Only MTN satisfied the ARCEP 2G Coverage requirements, MOOV, and CELTISS failed in Indoor coverage
Only MTN satisfied the ARCEP 3G Coverage requirements
MTN is ranked first in term of 4g Coverage
All operators failed to reach ARCËP 4G Indoor threshold. CELTISS failed also in Incar 4g coverage.
Tune and align power settings mainly in 3G/4G. Actual setting may impact the coverage strength specially at Indoor locations
Review the design at the coverage and quality blackspots
We highlight that 4G ARCEP coverage Thresholds are aggressive

## Slide 7: Executive Summary – Benchmarking voice service 2G/3G
Voice service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
MTN is ranked first in all voice tests
MTN is the only operator that satisfied all voice tests
MOOV and CELTISS failed in all voice except the voice quality
Voice quality is always better in 3G due to its better codec rate , we recommend to push as much as possible the voice traffic to 3G.
Actual selection/reselection/Irat parameters need to be reviewed and aligned.
2G Full Rate/Half Rate settings need to be tuned in order to improve Full rate penetration

## Slide 8: Executive Summary – Benchmarking SMS service
SMS service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
MTN is ranked first in all SMS tests
MTN is the only operators that satisfied SMS tests ARCEP threshold
There is no issue in radio accessibility that could be correlated to the SMS high delivery time.
End to End investigation need to be performed to analyses the high delivery time including mainly Core/SMS parts: SM Sserver...

## Slide 9: Executive Summary – Benchmarking 4G Data service
Data service 4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 4G data service, and all operators met ARCEP's requirements except CELTISS in ftp failure rate.
MTN is ranked first in all kind of 4G data tests
MTN is ranked first in Both DL and UL of 4G ftp tests, with 52.66/21.18Mbps DL/UL Throughput compared to 15.47/8.07 Mbps and 14.02/10.44 Mbps for MOOV and CELTISS.
MTN spectrum need to be used with a better efficiency, Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles

## Slide 10: Executive Summary – Benchmarking 3G Data service
Data service 3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 3G data service, and all operators met ARCEP's requirements except MOOV in Web failure Rate
MTN is ranked first in all kind of 3G data tests except ftp failure rate
MTN is in 1st position for 3G DL throughput with 6.97Mbps, compared to 6.54Mbps for CELTISS and 4.49Mbps for MOOV.
MTN is ranked first in term of 3G UL throughput with 2.63 Mbps against 1.39 Mbps for MOOV and 2.01Mbps for CELTISS,
Its recommended to push as much as possible the data traffic to 4G in order to:
- Improve end user perception, Both DT and stats are showing that users in average are served with up to 700% better throughput in 4G than in 3G
- Offload the 3G network which will improve the 3G throughput and the 3G radio quality
Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles

## Slide 11
Benchmarking Key Results
03

## Slide 12: Benchmarking Key Results – Coverage Only MTN satisfied the ARCEP 2G Coverage requirements, MOOV, and CELTISS failed in Indoor coverage Only MTN satisfied the ARCEP 3G Coverage requirements All operators failed to reach ARCËP 4G Indoor threshold. CELTISS failed also in Incar 4g coverage MTN is ranked first in term of 4g Coverage
KPI |  | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
2G Coverage Rate | Incar | More than 90% with Incar: Rxlev >-87 dBm | 99,70% | OK | 98,53% | OK | 96,39% | OK | 1
 | Outdoor | More than 90% with Outdoor: Rxlev >-92 dBm | 99,97% | OK | 99,59% | OK | 96,23% | OK | 1
 | Indoor | More than 90% with Outdoor: Rxlev >-74 dBm | 96,92% | OK | 74,82% | NOK | 69,17% | NOK | 1
3G Coverage Rate | Incar,Indoor,Outdoor | More than 90% with RSCP <-85 dBm | 92,45% | OK | 73,14% | NOK | 66,15% | NOK | 1
4G Coverage Rate | Incar | More than 90% with RSRP <-90 dBm* | 94,63% | OK | 94,12% | OK | 82,62% | NOK | 1
 | Outdoor | More than 90% with RSRP <-95 dBm* | 99,54% | OK | 98,83% | OK | 98,40% | OK | 1
 | Indoor | More than 90% with RSRP <-78 dBm* | 64,38% | NOK | 60,86% | NOK | 44,47% | NOK | 1

## Slide 13: Benchmarking Key Results – 2G/3G voice and SMS Summary MTN is ranked first in all voice and SMS tests MTN is the only operators that satisfied all voice and SMS tests MOOV and CELTISS failed in all voice and SMS tests except the voice quality
KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  | Value | Conformity | Value | Conformity | Value | Conformity | 
Accesibility: Blocking rate | <1% | 1,06% | OK | 2,97% | NOK | 4,25 | NOK | 1
Retainability: Call drop rate | <1% | 0,40% | OK | 1,71% | NOK | 1,71% | NOK | 1
Call Completetion Rate (%) | =<98% | 98,54% | OK | 95,32% | NOK | 94,04% | NOK | 1
Integrity: Voice quality | Note requise> 2,8 | 4,03 | OK | 3,73 | OK | 3,93 | OK | 1
SMS sending success rate % (E2E delivery Time<6 sec) | >99% | 99,36% | OK | 93,59% | NOK | 85,21% | NOK | 1
SMS receving success rate % | >99% | 98,87% | OK | 90,38% | NOK | 84,44% | NOK | 1

## Slide 14: Benchmarking Key Results – 3G Data Summary All operators met the 3G Data ARCEP requirements except MOOV in Web failure Rate MTN is ranked first in all kind of 3G data tests except ftp failure rate
Services | KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
3G HTTP | Successful internet connexion rate | >96% | 100,00% | OK | 100,00% | OK | 100,00% | OK | 1
 | Connexion setup time | <=10sec | 6,66 | OK | 6,98 | OK | 7,01 | OK | 1
 | Web service failure rate | <3% | 0,22% | OK | 4,67% | NOK | 0,94% | OK | 1
3G FTP | FTP failure rate UL/DL | <3 % | 0,44%/0,84% | OK | 1,3%/0% | OK | 0%/0,62% | OK | 2
 | FTP Data transmission average (DL) | >= 2Mbps | 6,970 | OK | 4,493 | OK | 6,544 | OK | 1
 | FTP Data transmission average (UL) | >= 1Mbps | 2,627 | OK | 1,391 | OK | 2,015 | OK | 1

## Slide 15: Benchmarking Key Results – 4G Data Summary MTN is ranked first in all kind of 4G data tests All operators met the ARCEP thresholds except CELTISS in ftp failure rate
Services | KPI | Threshorlds* | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
4G HTTP Browsing | Web service failure rate (%) | <3% | 1,89% | OK | 2,55% | OK | 2,12% | OK | 1
 | Connexion setup time | <=3sec | 0,88 | OK | 1,13 | OK | 1,89 | OK | 1
4G FTP | FTP failure rate UL/DL | <3 % | 0,43%/0% | OK | 0,22%/0,45% | OK | 8,33%/0% | NOK/OK | 1
 | FTP Data transmission average (DL) | 4G >= 5 Mbps | 52,666 | OK | 15,471 | OK | 14,025 | OK | 1
 | FTP Data transmission average (UL) | 4G: >= 2Mbps | 21,183 | OK | 8,075 | OK | 10,441 | OK | 1

## Slide 16
Benchmarking 2G/3G/4G coverage
04

## Slide 17: Benchmarking: 2G coverage Only MTN satisfied the ARCEP 2G Coverage requirements, MOOV, and CELTISS failed in Indoor coverage
Chart: RxLev Distribution (%)
| Indoor>-74 | Incar >-87 | Outdoor >-92
MTN | 0.9692 | 0.997 | 0.9997
MOOV | 0.7482 | 0.9853 | 0.9959
CELTISS | 0.6917 | 0.9639 | 0.9823

## Slide 18: Benchmarking: 2G coverage - Maps MTN have the best 2G coverage distribution

## Slide 19: Benchmarking: 3G coverage Only MTN satisfied the ARCEP 2G Coverage requirements
Chart: RSCP Distribution (%)
| Indoor,Incar,Outdoor >-85
MTN | 0.9245
MOOV | 0.7314
CELTISS | 0.6615

## Slide 20: Benchmarking: 3G coverage-Maps MTN have the best 3G coverage distribution

## Slide 21: Benchmarking: 4G coverage All operators failed to reach ARCËP 4G Indoor threshold. CELTISS failed also in Incar 4g coverage MTN is ranked first in term of 4g Coverage
Chart: RSRP Distribution (%)
| Indoor > -78 | Incar > -90 | Outdoor > -95
MTN | 0.6438 | 0.9463 | 0.9954
MOOV | 0.6086 | 0.9412 | 0.9883
CELTISS | 0.4447 | 0.8282 | 0.984

## Slide 22: Benchmarking – 4G coverage - Maps MTN have the best 4G coverage distribution

## Slide 23
Benchmarking voice service
05

## Slide 24: Benchmarking: CS Accessibility 2G/3G BLOCKED CALLS Only MTN satisfied the ARCEP voice accessibility requirements
Chart: Call Blocked Rate (%)
| CBR (%)
MTN | 0.0106
MOOV | 0.0297
CELTISS | 0.0425
Chart: Call Blocked Rate per Technology (%)
| CBR (%)
MTN 2G | 0
MTN 3G | 0.0095
MOOV 2G | 0
MOOV 3G | 0.0189
CELTISS 2G | 0.0189
CELTISS 3G | 0.0261

## Slide 25: Benchmarking: CS Integrity Voice quality Mean Opinion Score MTN have the best ratio of excellent and good Voice Quality samples and the best average MOS
Chart: Average MOS
| Avrege MOS
MTN | 4.03
MOOV | 3.73
CELTISS | 3.93
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Excel+Goog
MTN | 0.6407 | 0.3451 | 0.0076 | 0.0067 | 0.9858
MOOV | 0.5964 | 0.232 | 0.0561 | 0.1155 | 0.8284
CELTISS | 0.548 | 0.4307 | 0.0171 | 0.0043 | 0.0017

## Slide 26: Benchmarking – CS Integrity Voice quality maps (MOS) MTN have only 0,67% of MOS samples lower than 2.2, Values lower than 2,2 pose risk of bad users perceived voice quality 3d

## Slide 27: Benchmarking: CS Retainability 2G/3G DROPPED CALLS Only MTN satisfied the ARCEP voice drop requirements
Chart: Call Drop Rate (%)
| CDR (%)
MTN | 0.004
MOOV | 0.0171
CELTISS | 0.0128

## Slide 28: Benchmarking Voice service Band usage(%) Voice calls are mainly carried by 3G for all operators. MTN's 2G band usage: 100% GSM 900 and 0% DCS 1800 Mhz, 23,42 % of MTN 3G CS traffic is carried on U900 compared to 47,78% and 29,42% for MOOV and CELTISS.
Chart: System Technology usage(%)
| GSM | UMTS
MTN | 0.0375 | 0.9625
MOOV | 0.0017 | 0.9983
CELTISS | 0.0255 | 0.9745
Chart: 2G band usage(%)
| GSM 900 | GSM 1800
MTN | 1 | 0
MOOV | 1 | 0
CELTISS | 0.9286 | 0.0714
Chart: 3G band usage(%)
| UMTS 900 | UMTS 2100
MTN | 0.2342 | 0.7658
MOOV | 0.4778 | 0.5222
CELTISS | 0.2942 | 0.7058

## Slide 29: Benchmarking: Radio parameters EC/NO comparison CELLTIS have the best 3G EcNo samples within acceptable range while MTN have less bad samples than competitors
Chart: Ec/No Distribution (%)
| -8 to 0 | -12 to -8 | -16 to -12 | -34 to -16 | ACCEPTABLE EC/N0
MTN | 0.496 | 0.2403 | 0.2497 | 0.014 | 0.7363
MOOV | 0.3499 | 0.3548 | 0.2493 | 0.046 | 0.7047
CELTISS | 0.5302 | 0.2596 | 0.1584 | 0.0519 | 0.7898

## Slide 30: Benchmarking: Radio parameters EC/NO MTN have less bad samples than competitors

## Slide 31: Benchmarking – 2G/3G CALL SETUP TIME MTN have the best Call setup time. MTN have the best 4G CSBF Call setup Time, Call setup time 2G is higher than in 3G/4G.
Chart: Call Setup Time (s)
| Call Setup Time
MTN | 6.1
MOOV | 7.61
CELTISS | 8.01
Chart: CS Call setup Time by technology (s)
| 4G CSFB CST | 3G CST | 2G CST
MTN | 5.54 | 5.82 | 7.05
MOOV | 8.15 | 6.99 | 7.7
CELTISS | 8.09 | 7.95 | 8.01

## Slide 32: Benchmarking – SMS SENDING FAILURE MTN is ranked first in all kind of SMS tests MTN is the only operators that satisfied SMS tests ARCEP threshold
Chart: SMS
| SMS Sending message success rate (%) | SMS Receving message success rate (%)
MTN | 0.9936 | 0.9887
MOOV | 0.9359 | 0.9038
CELTISS | 0.8521 | 0.8444
Chart: SMS Send Time(%)
| (0,3) | (3,6) | >6
MTN | 0.4911 | 0.5025 | 0.0064
MOOV | 0.4237 | 0.5122 | 0.0641
CELTISS | 0.435 | 0.4171 | 0.1479

## Slide 33
Benchmarking Data service
06

## Slide 34: Benchmarking – DATA 3G All operators have a very good rate of successful Internet connection
Chart: PS Attach & PDP Contex Act(%)
| PS Attach success(%) | PDP Context Act Success (%)
MTN | 1 | 1
MOOV | 1 | 1
CELTISS | 1 | 1
Chart: Attach & PDP Activation Time (s)
| PS Attach Setup Time | PDP Context Act Time
MTN | 0.98 | 1.43
MOOV | 1.11 | 1.69
CELTISS | 1.27 | 1.58

## Slide 35: Benchmarking – DATA 3G
Chart: PS Connection setup time
| PS Connection setup time
MTN | 6.66
MOOV | 6.98
CELTISS | 7.01
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9978
MOOV | 0.9533
CELTISS | 0.9906
MOOV failed in http browsing SR

## Slide 36: Benchmarking – DATA 3G All operators have good downlink and uplink FTP success rate.
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9956 | 0.9916
MOOV | 0.987 | 1
CELTISS | 1 | 0.9938

## Slide 37: Benchmarking – 3G FTP MEAN THROUGHPUT All operators met the ARCEP downlink and uplink FTP success rate thresholds MTN Is ranked first in all kind of FTP Tests
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 6970.1 | 2627.48 | 15345.48 | 14584.11
MOOV | 4493.77 | 1391.74 | 15328.65 | 12547.88
CELTISS | 6544.37 | 2015.55 | 13188.59 | 8474.45

## Slide 38: Benchmarking – 3G FTP MEAN THROUGHPUT comparison map All samples exceed 2Mbps

## Slide 39: Benchmarking – 4G HTTP Browsing All operators have good HTTP Browsing success rate. MTN is ranked first
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9811
MOOV | 0.9745
CELTISS | 0.9788

## Slide 40: Benchmarking – 4G FTP THROUGHPUT comparison CELLTIS failed to reach the ARCEP threshold in term of FTP SR.
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9957 | 1
MOOV | 0.9978 | 0.9955
CELTISS | 0.9167 | 1

## Slide 41: Benchmarking – 4G FTP THROUGHPUT comparison All operators met the ARCEP downlink and uplink FTP success rate thresholds MTN Is ranked first in all kind of FTP Tests
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 52666.45 | 21183.75 | 201254.19 | 37847.54
MOOV | 15471.21 | 8075.06 | 165414.21 | 9987.47
CELTISS | 14025.19 | 10441.17 | 35621.37 | 13287.98

## Slide 42: Benchmarking – 4G FTP THROUGHPUT comparison map MTN Shows the best 4G FTP throughput samples distribution.

## Slide 43: Benchmarking – BAND and TECHNOLOGY UTILISATION
Chart: 3G band Distribution (%)
| UMTS 900 | UMTS 2100
MTN | 0.081 | 0.919
MOOV | 0.305 | 0.695
CELTISS | 0.0513 | 0.9487
Chart: 4G Band Distribution (%)
| LTE 800 | LTE 700 | LTE 1800 | LTE 2100 | LTE 2600
MTN | 0.0026 | 0 | 0.0097 | 0 | 0.9877
MOOV | 0.6586 | 0 | 0 | 0 | 0.3414
CELTISS | 0.9331 | 0 | 0.0106 | 0 | 0.0563
Most of MTN LTE samples are in 2600 band. Most of CELTIS LTE samples are in 800 band. Most of MOOV LTE samples are in 800 and 2600 band Usage of 3G U900 is lower for CELTISS

## Slide 44: Benchmarking – Data TECHNOLOGY Usage(%) MTN have the highest LTE CA Carrier Aggregation usage.
Chart: 3G Packet Technology usage (%)
| DC-HSPA | HSPA | HSDPA | UMTS
MTN | 0.5074 | 0.0119 | 0 | 0.4807
MOOV | 0.4633 | 0.1255 | 0 | 0.4112
CELTISS | 0.4428 | 0.0298 | 0.0145 | 0.5129
Chart: 4G Packet Technology usage (%)
| LTE | LTE CA
MTN | 0.1534 | 0.8466
MOOV | 0.532 | 0.468
CELTISS | 0.4795 | 0.5205

## Slide 45: Benchmarking – SINR comparison Drive tests are showing that MTN have the best acceptable level range of SINR
Chart: SINR Comparison
| (Min,-4) | (-4,0) | (0,7) | (7,15 <) | ACCEPTABLE SINR
MTN | 0.0019 | 0.0137 | 0.1352 | 0.8492 | 0.9844
MOOV | 0.0074 | 0.0547 | 0.2941 | 0.6438 | 0.9379
CELTISS | 0.0138 | 0.0702 | 0.2916 | 0.6244 | 0.916

## Slide 46: Benchmarking – SNIR comparison map 4G MTN have a better quality of signal compared to CELTISS and MOOV

## Slide 47
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2023 Deloitte Bénin SARL. Société du réseau Deloitte