## Slide 1
Network QoS
Benchmarking report PORTO-NOVO
November 23th, 2023

## Slide 2: Summary
Scope of Intermediate Report | 3
Executive Summary | 5
Benchmarking Key Results | 11
Benchmarking Coverage | 16
Benchmarking Voice Service | 23
Benchmarking Data Service | 33

## Slide 3
Introduction: Scope of Benchmarking Report
01

## Slide 4: Intermediate report
Scope of this report
  1. Network benchmarking results for the PORTO-NOVO area between MTN, MOOV, and CELTISS from Octobre 13th to September 15th, 2023..

## Slide 5
Benchmarking Executive Summary
02

## Slide 6: Executive Summary – Benchmarking coverage 2G/3G/4G
Coverage 2G/3G/4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
MTN has outperformed its competitors in terms of 2G coverage for all morphologies Indoor, outdoor and Incar,
Only MTN’s 2G RF coverage meets ARCEP obligation for all morphologies,
3G MTN’s coverage rate (91,03%) is lower than CELTISS (91,29%) and better than MOOV with (83,54%),
Only MTN and CELTISS meet ARCEP 3G coverage obligation
4G MTN’s coverage rate is better than MOOV’s and CELTISS’s coverage for outdoor and Incar morphologies,
All operators failed to satisfied the indoor coverage ARCEP threshold.
Tune and align power settings mainly in 3G/4G. Actual setting may impact the coverage strength specially at Indoor locations
Review the design at the coverage and quality blackspots
We highlight that 4G ARCEP coverage Thresholds are aggressive
* Final recommendations will be shared in the final report including details and findings from ongoing Configuration Audit

## Slide 7: Executive Summary – Benchmarking voice service 2G/3G
Voice service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Accessibility: MTN is ranked first for the accessibility to voice service , better than CELTISS and MOOV, only MTN meets ARCEP requirements.
MOOV and CELTISS failed to meet ARCEP accessibility thresholds,
Retainability: MTN is ranked first in term of retainability better than MOOV and CELTISS,
MTN's Call Drop Rate is (0.60%) better than CELTISS (1.11%) and MOOV (2.48%).Only MTN meets ARCEP retainabilty requirements,
Integrity: MTN is in third position in terms of voice quality lower than MOOV and better than CELTISS with average Mean Opinion Score 3.8 as opposed to 3.79 for CELTISS and 3.83 for MOOV.
To improve its Mean Opinion Score MOS MTN needs to improve its 3G radio parameter Ec/No that is closely related to voice quality .
* Final recommendations will be shared In the final report including details and findings from ongoing Configuration Audit

## Slide 8: Executive Summary – Benchmarking SMS service
SMS service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
All operators failed to meet ARCEP for SMS Send Success with End To End Delivery Time < 6 sec,
MTN is better than MOOV and lower than CELTISS.
There is no issue in radio accessibility that could be correlated to the SMS high delivery time.
End to End investigation need to be performed to analyses the high delivery time including mainly Core/SMS parts: SM Sserver...
* Final recommendations will be shared in the final report including details and findings from ongoing Configuration Audit

## Slide 9: Executive Summary – Benchmarking 4G Data service
Data service 4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 4G data service, and all operators meet ARCEP's requirements.
MTN is ranked second in terms of 4G DL throughput with 17.35Mbps, which is better than CELTISS's 13.12Mbps but lower than MOOV's 22.22Mbps.
MTN is ranked first in terms of 4G UL throughput with 16.73Mbps, as opposed to 10.63Mbps for MOOV and 12.15Mbps for CELTISS.
All operators meet ARCEP's 4G End User Throughput obligation for download and upload.
MTN spectrum need to be used with a better efficiency, Some features and parameters need to be tuned and aligned,
To improve its 4G DL Throughput, MTN needs to optimize the carrier aggregation, MIMO settings and modulation,
To ensure that no throughput limitation is applied on users profiles.

## Slide 10: Executive Summary – Benchmarking 3G Data service
Data service 3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 3G data service, and all operators meet ARCEP's requirements.
MTN is in third position for 3G DL throughput with 4.25Mbps, compared to 6.13Mbps for CELTISS and 4.97Mbps for MOOV.
MTN is ranked first in term of 3G UL throughput with 2.19 Mbps against 1.18 Mbps for MOOV and 2.00Mbps for CELTISS,
All operators meets ARCEP’s 3G End User Throughput obligation for download and upload.
All operators meet ARCEP’s web browsing service accessibility thresholds.
Its recommended to push as much as possible the data traffic to 4G in order to:
- Improve end user perception, Both DT and stats are showing that users in average are served with up to 4x better throughput in 4G than in 3G
- Offload the 3G network which will improve the 3G throughput and the 3G radio quality
Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles
* Final recommendations will be shared in the final report including details and findings from ongoing Configuration Audit

## Slide 11
Benchmarking Key Results
03

## Slide 12: Benchmarking Key Results – Coverage In Porto-Novo, MTN is clear leader in 2G coverage for all morphologies, Only MTN and CELTISS meet ARCEP requirements for 3G coverage, MTN has outperformed its competitors in terms of 4G coverage for Incar and outdoor morphologies. All operators failed to meet ARCEP requirements in Indoor coverage.
KPI |  | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
2G Coverage Rate | Incar | More than 90% with Incar: Rxlev >-87 dBm | 100% | OK | 99,93% | OK | 99,98% | OK | 1
 | Outdoor | More than 90% with Outdoor: Rxlev >-92 dBm | 100% | OK | 100% | OK | 100% | OK | 1
 | Indoor | More than 90% with Outdoor: Rxlev >-74 dBm | 96,66% | OK | 83,9% | NOK | 88,68% | NOK | 1
3G Coverage Rate | Incar,Indoor,Outdoor | More than 90% with RSCP <-85 dBm | 91,03% | OK | 83,54% | NOK | 91,29% | OK | 2
4G Coverage Rate | Incar | More than 90% with RSRP <-90 dBm* | 91,5% | OK | 89,43% | NOK | 90,66% | OK | 1
 | Outdoor | More than 90% with RSRP <-95 dBm* | 96,90% | OK | 95,73% | OK | 96,47% | OK | 1
 | Indoor | More than 90% with RSRP <-78 dBm* | 54,31% | NOK | 46,27% | NOK | 59,91% | NOK | 2

## Slide 13: Benchmarking Key Results – 2G/3G voice and SMS Summary MTN is leading in accessibility and retainability in Porto-Novo, Only MTN meets ARCEP requirements in terms of accessibility and retainability, MTN is ranked second in terms of voice quality MOS but satisfys ARCEP requirements, MTN needs to improve its Voice Quality MOS and SMS Send duration.
KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  | Value | Conformity | Value | Conformity | Value | Conformity | 
Accesibility: Blocking rate | <1% | 0,64% | OK | 1,99% | NOK | 1,80 | NOK | 1
Retainability: Call drop rate | <1% | 0,6% | OK | 2,48% | NOK | 1,11% | NOK | 1
Call Completetion Rate (%) | =<98% | 98,76% | OK | 96,21% | NOK | 97,09% | NOK | 1
Integrity: Voice quality | Note requise> 2,8 | 3,80 | OK | 3,83 | OK | 3,79 | OK | 2
SMS sending success rate % (E2E delivery Time<6 sec) | >99% | 93,16% | NOK | 92,70% | NOK | 93,74% | NOK | 2
SMS receving success rate % | >99% | 90,83% | NOK | 89,78% | NOK | 91,88% | NOK | 2

## Slide 14: Benchmarking Key Results – 3G Data Summary MTN’s network in 3G DATA meets ARCEP requirements.
Services | KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
3G HTTP | Successful internet connexion rate | >96% | 100,00% | OK | 100,00% | OK | 100,00% | OK | 1
 | Connexion setup time | <=10sec | 6,22 | OK | 6,33 | OK | 5,74 | OK | 2
 | Web service failure rate | <4% | 2,01% | OK | 1,61% | OK | 1,56% | OK | 3
3G FTP | FTP failure rate UL/DL | <3 % | 0,85%/0,59% | OK | 1,27%/0,63% | OK | 0,07%/0,29% | OK | 2
 | FTP Data transmission average (DL) | >= 2Mbps | 4,256 | OK | 4,975 | OK | 6,136 | OK | 3
 | FTP Data transmission average (UL) | >= 1Mbps | 2,197 | OK | 1,183 | OK | 2,007 | OK | 1

## Slide 15: Benchmarking Key Results – 4G Data Summary MTN’s 4G DATA End User KPIs satisfy ARCEP requirements, MTN is ranked second in 4G DL THP after MOOV’s , MTN is outperforming MOOV’s & CELTISS in 4G UL THP.
Services | KPI | Threshorlds* | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
4G HTTP Browsing | Web service failure rate (%) | <3% | 1,49% | OK | 2,13% | OK | 1,89% | OK | 1
 | Connexion setup time | <=3sec | 0,77 | OK | 0,84 | OK | 0,27 | OK | 2
4G FTP | FTP failure rate UL/DL | <3 % | 0,13%/1,56% | OK | 0,79%/1,12% | OK | 0,96%/1,76% | OK | 1
 | FTP Data transmission average (DL) | 4G >= 5 Mbps | 17,358 | OK | 22,227 | OK | 13,120 | OK | 2
 | FTP Data transmission average (UL) | 4G: >= 2Mbps | 16,738 | OK | 10,633 | OK | 12,150 | OK | 1

## Slide 16
Benchmarking 2G/3G/4G coverage
04

## Slide 17: Benchmarking: 2G coverage MTN has the best 2G coverage for all morphologies Indoor, Incar and outdoor, Only MTN’s network meets ARCEP requirements for all morphologies.
Chart: 2G RxLev Distribution (%)
| Indoor>-74 | Incar >-87 | Outdoor >-92
MTN | 0.9666 | 1 | 1
MOOV | 0.839 | 0.9993 | 1
CELTISS | 0.8858 | 0.9998 | 1

## Slide 18: Benchmarking: 2G coverage - Maps MTN’s 2G coverage is better than MOOV’s and CELTISS’s, MTN has more than 96,66% of RxLev samples better than -74dBm,against 83,90% for MOOV and 88,85% for CELTISS.

## Slide 19: Benchmarking: 3G coverage MTN’s and CELTISS’s 3G coverage are closely similar and meet ARCEP requirements, MOOV’s 3G coverage failed to meet ARCEP obligation.
Chart: 3G RSCP Distribution (%)
| Indoor,Incar,Outdoor >-85
MTN | 0.9103
MOOV | 0.8354
CELTISS | 0.9129

## Slide 20: Benchmarking: 3G coverage-Maps MTN’s 3G coverage is closely similar to CELTISS with 91,03% of samples better than -85 dBm against 91,29% for MOOV and 75,76% for CELTISS.

## Slide 21: Benchmarking: 4G coverage MTN has the best 4G coverage and meets ARCEP requirements for incar and outdoor morphologies but, all operators failed to satisfy ARCEP requirements for indoor.
Chart: 4G RSRP Distribution (%)
| Indoor > -78 | Incar > -90 | Outdoor > -95
MTN | 0.5431 | 0.915 | 0.969
MOOV | 0.4627 | 0.8943 | 0.9573
CELTISS | 0.5991 | 0.9066 | 0.9647

## Slide 22: Benchmarking – 4G coverage - Maps CELTISS’s 4G coverage is slightly better than MTN’s.

## Slide 23
Benchmarking voice service
05

## Slide 24: Benchmarking: CS Accessibility 2G/3G BLOCKED CALLS MTN has the best accessibility to voice service compared to competitors, Only MTN and CELTISS meet ARCEP requirements.
Chart: Call Blocked Rate (%)
| CBR (%)
MTN | 0.0064
MOOV | 0.0199
CELTISS | 0.008
Chart: Call Blocked Rate per Technology (%)
| CBR (%)
MTN 2G | 0
MTN 3G | 0.006
MOOV 2G | 0
MOOV 3G | 0.018
CELTISS 2G | 0
CELTISS 3G | 0.0282

## Slide 25: Benchmarking: CS Integrity Voice quality Mean Opinion Score In Porto-Novo, MOOV has the best MOS and ratio of excellent and good Voice Quality samples compared to MTN’s and CELTISS’S, MTN’s speech quality MOS (3,8) is closely simular to MOOV’s (3,83) and CELTISS’s MOS (3,79).
Chart: Average MOS
| Avrege MOS
MTN | 3.8
MOOV | 3.83
CELTISS | 3.79
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Excel+Goog
MTN | 0.3242 | 0.6251 | 0.018 | 0.0328 | 0.9493
MOOV | 0.7677 | 0.1822 | 0.018 | 0.0322 | 0.9499
CELTISS | 0.564 | 0.3743 | 0.0069 | 0.0549 | 0.9383

## Slide 26: Benchmarking – CS Integrity Voice quality maps (MOS) MTN has around 3,28% of MOS samples lower than 2.2 against 3,22% for MOOV and 5,49% for CELTISS, Values lower than 2,2 pose risk of bad users perceived voice quality and silente calls. 3d

## Slide 27: Benchmarking: CS Retainability 2G/3G DROPPED CALLS MTN is clair leader in term of retainability by having the lowest Call Drop Rate, Only MTN meets ARCEP requirements.
Chart: Call Drop Rate (%)
| CDR (%)
MTN | 0.006
MOOV | 0.0248
CELTISS | 0.0111

## Slide 28: Benchmarking Voice service Band usage(%) All operators have more than 98% of voice calls carried out over 3G, All operators use mainly U2100, but MTN has the highest ratio of U900 usage with 23,70% against 17,44% for MOOV and 13,74% for CELTISS.
Chart: System Technology usage(%)
| GSM | UMTS
MTN | 0.0164 | 0.9836
MOOV | 0.004 | 0.996
CELTISS | 0.0051 | 0.9949
Chart: 2G band usage(%)
| GSM 900 | GSM 1800
MTN | 0.8002 | 0.1998
MOOV | 0.6667 | 0.3333
CELTISS | 0.9418 | 0.0582
Chart: 3G band usage(%)
| UMTS 900 | UMTS 2100
MTN | 0.237 | 0.763
MOOV | 0.1744 | 0.8256
CELTISS | 0.1374 | 0.8626

## Slide 29: Benchmarking: Radio parameters EC/NO comparison 24,59% of drive test samples are showing a very low level of EcNo for 3G MTN. This is correlated to the number of 3G carriers : MTN is using 2 carriers against 3 and 4 for CELTISS and MOOV respectively. Also3G traffic is carried mainly by U2100 for competitors while it’s distributed over U900 and U2100 for MTN.
Chart: Ec/No Distribution (%)
| -8 to 0 | -12 to -8 | -16 to -8 | -34 to -16 | ACCEPTABLE EC/N0
MTN | 0.1172 | 0.2418 | 0.3951 | 0.2459 | 0.359
MOOV | 0.3812 | 0.3255 | 0.2328 | 0.0604 | 0.7067
CELTISS | 0.6332 | 0.2675 | 0.0814 | 0.0179 | 0.9007

## Slide 30: Benchmarking: Radio parameters EC/NO 3G MOOV’s and CELTISS’s EC/N0 is better than MTN’s due to the number of 3G used carriers . The bad Ec/No has a high impact on voice quality.

## Slide 31: Benchmarking – 2G/3G CALL SETUP TIME MTN has the best Call setup time. MTN has the best 4G CSBF Call setup Time, Call setup time 2G is higher than in 3G/4G.
Chart: Call Setup Time (s)
| Call Setup Time
MTN | 6.83
MOOV | 7.01
CELTISS | 6.99
Chart: CS Call setup Time by technology (s)
| 4G CSFB CST | 3G CST | 2G CST
MTN | 5.45 | 5.58 | 5.14
MOOV | 8.35 | 8.77 | 8.28
CELTISS | 8.46 | 8.96 | 7.43

## Slide 32: Benchmarking – SMS Service CELTISS SMS SETUP/RESPONSE is better than MTN’s & MOOV’s. SMS service KPIs all operators are not compliant with the ARCEP requirements due to the timeout of sending duration (< 6s).
Chart: SMS Send Time Distribution(%)
| (0,3) | (3,6) | >6
MTN | 0.6066 | 0.325 | 0.0684
MOOV | 0.525 | 0.2493 | 0.073
CELTISS | 0.7648 | 0.1726 | 0.0626
Chart: SMS Send & Received SR(%)
| SMS Sending message success rate (%) | SMS Receving message success rate (%)
MTN | 0.9316 | 0.9083
MOOV | 0.927 | 0.8978
CELTISS | 0.9374 | 0.9188

## Slide 33
Benchmarking Data service
06

## Slide 34: Benchmarking – DATA 3G All operators have a good rate of successful Internet connection, MTN has the best PS attach and PDP Context Activation delays.
Chart: PS Attach & PDP Contex Act(%)
| PS Attach success(%) | PDP Context Act Success (%)
MTN | 1 | 1
MOOV | 1 | 1
CELTISS | 1 | 1
Chart: Attach & PDP Activation Time (s)
| PS Attach Setup Time | PDP Context Act Time
MTN | 1.08 | 1.32
MOOV | 1.28 | 1.45
CELTISS | 1.37 | 1.51

## Slide 35: Benchmarking – DATA 3G Web service All operators have very good web service success rate. MOOV has the highest PS connection setup time.
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9799
MOOV | 0.9839
CELTISS | 0.9844
Chart: PS Connection setup time
| PS Connection setup time
MTN | 6.22
MOOV | 6.33
CELTISS | 5.74

## Slide 36: Benchmarking – DATA 3G FTP service All operators have good downlink and uplink FTP success rate and meet ARCEP requirements.
Chart: 3G FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9915 | 0.9941
MOOV | 0.9873 | 0.9937
CELTISS | 0.9993 | 0.9971

## Slide 37: Benchmarking – 3G FTP MEAN THROUGHPUT All operators meet ARCEP requirement in terms of FTP DL/UL throughput, MTN has the lowest 3G FTP D throughput, MTN has the best 3G FTP UL throughput.
Chart: 3G FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 4256.87 | 2197.08 | 23625.5 | 13678.3
MOOV | 4975.2 | 1183.54 | 25220.5 | 18341.33
CELTISS | 6136.24 | 2007.05 | 18458.33 | 9003.4

## Slide 38: Benchmarking – 3G FTP MEAN DL THROUGHPUT maps CELTISS has the best DL throughput distribution with 99,27% of samples better than 2Mbps against 97,56% for MTN and 96,59% for MOOV.

## Slide 39: Benchmarking – 4G Web Browsing service All operators meet ARCEP requirements and MTN has the best HTTP Browsing success rate.
Chart: 4G HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9851
MOOV | 0.9787
CELTISS | 0.9811

## Slide 40: Benchmarking – 4G FTP service All operators have acceptable FTP success rate. MTN has the best FTP DL Succes ratio and closely lower than MOOV for FTP UL Success ratio.
Chart: 4G FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9987 | 0.9844
MOOV | 0.9921 | 0.9888
CELTISS | 0.9904 | 0.9824

## Slide 41: Benchmarking – 4G FTP THROUGHPUT comparison MTN is ranked second in terms of FTP DL throughput, MTN has outperformed its competitors in terms of FTP UL throughput, All operators meet ARCEP requirements for 4G DL/UL throughput.
Chart: 4G FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 17358.51 | 16738.8 | 214833.4 | 54922.61
MOOV | 22727.79 | 10633.13 | 161577.47 | 61351.48
CELTISS | 13012.4 | 12150.4 | 191324.22 | 20782.06

## Slide 42: Benchmarking – 4G FTP THROUGHPUT comparison maps CELTISS has 100% of DL throughput samples better than 5Mbps against 10,2% for MTN and 10,9% for MOOV.

## Slide 43: Benchmarking – BAND and TECHNOLOGY UTILISATION Most of MTN’s and MOOV’s LTE samples are carried out over LTE 2600 as first carrier, Most of CELTISS’s samples are carried out over LTE 1800 as first carrier, For all operators,most of 3G samples are carried out over U2100, but MTN has the highest ratio of U900 usage.
Chart: 3G Band Distribution (%)
| UMTS 900 | UMTS 2100
MTN | 0.1106 | 0.8894
MOOV | 0.0766 | 0.9234
CELTISS | 0.019 | 0.981
Chart: 4G Band Distribution (%)
| LTE 800 | LTE 700 | LTE 1800 | LTE 2100 | LTE 2600
MTN | 0.0254 | 0.0178 | 0.0042 | 0 | 0.9525
MOOV | 0.254 | 0 | 0.0201 | 0 | 0.7259
CELTISS | 0.0197 | 0 | 0.9789 | 0.0014 | 0

## Slide 44: Benchmarking – Data TECHNOLOGY Usage(%) MTN has the highest LTE Carrier Aggregation usage, with 80,56% against 40,45% for MOOV and 51,14% for CELTISS, MTN needs to improve its LTE CA usage to get the best 4G throughput, MTN has the highest HSDPA-DC 3G data technology usage
Chart: 4G Packet Technology usage (%)
| LTE | LTE CA
MTN | 0.1944 | 0.8056
MOOV | 0.5955 | 0.4045
CELTISS | 0.4886 | 0.5114
Chart: 3G Packet Technology usage (%)
| DC-HSPA | HSPA | HSDPA | UMTS
MTN | 0.502 | 0.0967 | 0 | 0.4013
MOOV | 0.4142 | 0.1769 | 0 | 0.409
CELTISS | 0.4621 | 0.0376 | 0.0258 | 0.4746

## Slide 45: Benchmarking – Radio parameter SINR comparison Drive tests are showing that CELTISS has the best ratio of acceptable level of SINR.
Chart: SINR Comparison
| (Min,-4) | (-4,0) | (0,7) | (7,15 <) | ACCEPTABLE SINR
MTN | 0.0164 | 0.0527 | 0.2086 | 0.7223 | 0.9309
MOOV | 0.047 | 0.1061 | 0.2509 | 0.596 | 0.8469
CELTISS | 0.0084 | 0.0285 | 0.175 | 0.7881 | 0.9631

## Slide 46: Benchmarking – SNIR comparison maps CELTISS has the better Signal of quality compared to MTN and MOOV.

## Slide 47
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2019 Deloitte Bénin SARL. Société du réseau Deloitte