## Slide 1
Network QoS
Benchmarking report ALL ROADS
November 30th, 2023

## Slide 2: Summary
Scope of Intermediate Report | 3
Executive Summary | 5
Benchmarking Key Results | 11
Benchmarking Coverage | 16
Benchmarking Voice Service | 23
Benchmarking Data Service | 33

## Slide 3
Introduction: Scope of Benchmarking Report «
01

## Slide 4: Intermediate report
Scope of this report
  1. Network benchmarking results for the ALL ROADS area between MTN, MOOV, and CELTISS from September 9th to October 31th, 2023..

## Slide 5
Benchmarking Executive Summary
02

## Slide 6: Executive Summary – Benchmarking coverage 2G/3G/4G
Coverage 2G/3G/4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Tune and align power settings mainly in 3G/4G. Actual setting may impact the coverage strength specially at Indoor locations
Review the design at the coverage and quality blackspots
We highlight that 4G ARCEP coverage Thresholds are aggressive
* Final recommendations will be shared in the final report including details and findings from ongoing Configuration Audit
MTN has outperformed its competitors in terms of 2G coverage for outdoor and Indoor morphologies ,
For 2G RF coverage, Only MTN meets ARCEP obligation for all morphologies,
MTN is leading in terms of 3G coverage rate with (94,09%) against (86,16%) for CELTISS and (88,98%) for MOOV
Only MTN meets ARCEP 3G coverage obligation
MTN is in the second position in terms of 4G coverage rate for Incar and Outdoor morphologies but meets ARCEP thresholds,
All operators failed to satisfied the ARCEP threshold for indoor coverage for 4G network.

## Slide 7: Executive Summary – Benchmarking voice service 2G/3G
Voice service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Accessibility: MTN is leading in terms of accessibility to voice service by having the best Call Blocked ratio with 0,58% against 0,86% for MOOV and 0,84% for CELTISS,
All operators failed to meet ARCEP accessibility thresholds,
Retainability: MTN is ranked first in term of retainability better than MOOV and CELTISS,
MTN's Call Drop Rate is 0.38% compared to 0.78% for CELTISS and 0.55% for MOOV.All operators meet ARCEP retainabilty requirements,
Integrity: MTN is in second position in terms of voice quality with average Mean Opinion Score equal to 4,02 lower than MOOV 4,21 and better than CELTISS 3,94
In LOKOSSA the MTN’s MOS value is better than other area, because the voice quality is carried out mainly over 3G unlike other areas .
Voice quality is always better in 3G due to its better codec rate , we recommend to push as much as possible the voice traffic to 3G,
Drive test results are showing that MTN has a bad Ec/No, by improving this radio parameter we can improve further the voice quality MOS.
further

## Slide 8: Executive Summary – Benchmarking SMS service
SMS service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
All operators failed to meet ARCEP for SMS Send Success with End To End Delivery Time who should be less than < 6 sec as defined by ARCEP.
MTN is better than MOOV and lower than CELTISS.
There is no issue in radio accessibility that could be correlated to the SMS high delivery time.
End to End investigation need to be performed to analyses the high delivery time including mainly Core/SMS parts: SM Sserver...
* Final recommendations will be shared in the final report including details and findings from ongoing Configuration Audit

## Slide 9: Executive Summary – Benchmarking 4G Data service
Data service 4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 4G data service, and all operators meet ARCEP's requirements.
MTN is leading in terms of 4G DL throughput with 57.41Mbps, better than MOOV 27.51Mbps and CELTISS 12.93Mbps.
MTN is ranked first in terms of 4G UL throughput with 18.74Mbps, as opposed to 13.53Mbps for MOOV and 11.47Mbps for CELTISS.
For 4G network, all operators meet ARCEP’s End User Throughput obligation in download and upload.
In LOKOSSA, MTN has an excellent performance in term of 4G KPIs.

## Slide 10: Executive Summary – Benchmarking 3G Data service
Data service 3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 3G data service, and all operators meet ARCEP's requirements.
MTN is in third position for 3G DL throughput with 2.2Mbps, compared to 4.62Mbps for CELTISS and 3.33Mbps for MOOV.
MTN is ranked second in term of 3G UL throughput with 1.04 Mbps against 1.01 Mbps for MOOV and 2.15Mbps for CELTISS,
All operators meets ARCEP’s 3G End User Throughput obligation for download and upload.
All operators meet ARCEP’s web browsing service accessibility thresholds.
Its recommended to push as much as possible the data traffic to 4G in order to:
- Improve end user perception, Both DT and stats are showing that users in average are served with an excellent throughput in 4G,
- Offload the 3G network which will improve the 3G throughput and the 3G radio quality
Increasing the utilization of 3G data technology HSPA-DC can improve 3G throughput,
Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles

## Slide 11
Benchmarking Key Results
03

## Slide 12: Benchmarking Key Results – Coverage MTN, MOOV, and CELTISS have similar 2G and 3G coverage, but MTN's 4G coverage is lower than that of MOOV and CELTISS. The expansion of the 4G network is necessary in Cotonou to match MOOV's coverage
KPI |  | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
2G Coverage Rate | Incar | More than 90% with Incar: Rxlev >-87 dBm | 79,37% | NOK | 82,94% | NOK | 75,36% | NOK | 2
 | Outdoor | More than 90% with Outdoor: Rxlev >-92 dBm | 87,70% | NOK | 91,34% | OK | 87,60% | NOK | 2
 | Indoor | More than 90% with Outdoor: Rxlev >-74 dBm | 64,56% | NOK | 65,42% | NOK | 57,95% | NOK | 2
3G Coverage Rate | Incar,Indoor,Outdoor | More than 90% with RSCP <-85 dBm | 62,65% | NOK | 68,50% | NOK | 65,52% | NOK | 3
4G Coverage Rate | Incar | More than 90% with RSRP <-90 dBm* | 57,40% | NOK | 55,43% | NOK | 49,51% | NOK | 1
 | Outdoor | More than 90% with RSRP <-95 dBm* | 81,20% | NOK | 73,78% | NOK | 67,63% | NOK | 1
 | Indoor | More than 90% with RSRP <-78 dBm* | 28,99% | NOK | 28,35% | NOK | 25,32% | NOK | 1

## Slide 13: Benchmarking Key Results – 2G/3G voice and SMS Summary MTN network in retainability CDR (%) meets ARCEP requirements, MTN is leading in accessibility but slightly exceeds ARCEP threshold, MTN needs to improve its Voice Quality MOS and SMS Send duration.
KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  | Value | Conformity | Value | Conformity | Value | Conformity | 
Accesibility: Blocking rate | <1% | 5,88% | NOK | 7,64% | NOK | 9,58% | NOK | 1
Retainability: Call drop rate | <1% | 6% | NOK | 10,32% | NOK | 9,56% | NOK | 1
Call Completetion Rate (%) | =<98% | 88,12% | NOK | 82,04% | NOK | 80,86% | NOK | 1
Integrity: Voice quality | Note requise> 2,8 | 3,79 | OK | 3,95 | OK | 3,91 | OK | 2
SMS sending success rate % (E2E delivery Time<6 sec) | >99% | 92,20% | NOK | 89,50% | NOK | 91,12% | NOK | 1
SMS receving success rate % | >99% | 90,09% | NOK | 88,14% | NOK | 90,67% | NOK | 1

## Slide 14: Benchmarking Key Results – 3G Data Summary MTN network in 3G DATA meets ARCEP requirements.
Services | KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
3G HTTP | Successful internet connexion rate | >96% | 95,25% | NOK | 91,22% | NOK | 93,47% | NOK | 1
 | Connexion setup time | <=10sec | 7,29 | OK | 8,30 | OK | 8,77 | OK | 1
 | Web service failure rate | <3% | 6,67% | NOK | 12,11% | NOK | 11,7% | NOK | 1
3G FTP | FTP failure rate UL/DL | <3 % | 4,58%/6,08% | NOK | 6,34%/2,27% | NOK/OK | 1,32%/7,04% | OK/NOK | 2
 | FTP Data transmission average (DL) | >= 2Mbps | 4,432 | OK | 3,134 | OK | 5,867 | OK | 2
 | FTP Data transmission average (UL) | >= 1Mbps | 1,867 | OK | 1,352 | OK | 1,792 | OK | 1

## Slide 15: Benchmarking Key Results – 4G Data Summary MTN’s 4G DATA End User KPIs satisfy ARCEP requirements, MTN is ranked second in 4G DL THP after MOOV’s , MTN is outperforming MOOV’s & CELTISS in 4G UL THP.
Services | KPI | Threshorlds* | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
4G HTTP Browsing | Web service failure rate (%) | <3% | 2,92% | OK | 3,67% | NOK | 4,74% | NOK | 1
 | Connexion setup time | <=3sec | 1,37 | OK | 1,48 | OK | 1,52 | OK | 1
4G FTP | FTP failure rate UL/DL | <3 % | 0,59%/6,87% | OK/NOK | 6,74%/9,21% | NOK | 12,5%/8,97% | NOK | 1
 | FTP Data transmission average (DL) | 4G >= 5 Mbps | 39,681 | OK | 10,525 | OK | 10,351 | OK | 1
 | FTP Data transmission average (UL) | 4G: >= 2Mbps | 13,135 | OK | 7,045 | OK | 9,103 | OK | 1

## Slide 16
Benchmarking 2G/3G/4G coverage
04

## Slide 17: Benchmarking: 2G coverage All operators failed to meet ARCEP thresholds except CELTIIS IN outdoor.
Chart: RxLev Distribution (%)
| Indoor>-74 | Incar >-87 | Outdoor >-92
MTN | 0.6456 | 0.7937 | 0.877
MOOV | 0.6542 | 0.8294 | 0.9134
CELTISS | 0.5795 | 0.7536 | 0.876

## Slide 18: Benchmarking: 2G coverage - Maps MTN’s 2G coverage is very close than MOOV’s and better than CELTISS’s.

## Slide 19: Benchmarking: 3G coverage All operators failed to meet ARCEP thresholds.
Chart: RSCP Distribution (%)
| Indoor,Incar,Outdoor >-85
MTN | 0.6265
MOOV | 0.685
CELTISS | 0.6552

## Slide 20: Benchmarking: 3G coverage-Maps MTN’s 3G coverage is lower than CELTISS’s and MOOV’s.

## Slide 21: Benchmarking: 4G coverage All operators failed to meet ARCEP thresholds.
Chart: RSRP Distribution (%)
| Indoor > -78 | Incar > -90 | Outdoor > -95
MTN | 0.2899 | 0.574 | 0.812
MOOV | 0.2835 | 0.5543 | 0.7378
CELTISS | 0.2532 | 0.4951 | 0.6763

## Slide 22: Benchmarking – 4G coverage - Maps MTN’s 4G coverage is better than MOOV’s and CELTISS.

## Slide 23
Benchmarking voice service
04

## Slide 24: Benchmarking: CS Accessibility 2G/3G BLOCKED CALLS MTN has the best accessibility to voice service compared to competitors, All operators failed to meet ARCEP thresholds.
Chart: Call Blocked Rate (%)
| CBR (%)
MTN | 0.0588
MOOV | 0.0764
CELTISS | 0.0958
Chart: Call Blocked Rate per Technology (%)
| CBR (%)
MTN 2G | 0.0198
MTN 3G | 0.0235
MOOV 2G | 0.0219
MOOV 3G | 0.0425
CELTISS 2G | 0.048
CELTISS 3G | 0.0295

## Slide 25: Benchmarking: CS Retainability 2G/3G DROPPED CALLS All operators failed to meet ARCEP thresholds.
Chart: Call Drop Rate (%)
| CDR (%)
MTN | 0.06
MOOV | 0.1032
CELTISS | 0.0956

## Slide 26: Benchmarking Voice service Band usage(%) All operators have more than 88% of voice calls carried out over 3G, All operators use mainly UMTS900 band.
Chart: System Technology usage(%)
| GSM | UMTS
MTN | 0.0839 | 0.9161
MOOV | 0.019 | 0.981
CELTISS | 0.1172 | 0.8828
Chart: 2G band usage(%)
| GSM 900 | GSM 1800
MTN | 0.8764 | 0.1236
MOOV | 0.7466 | 0.2534
CELTISS | 0.817 | 0.183
Chart: 3G band usage(%)
| UMTS 900 | UMTS 2100
MTN | 0.5686 | 0.4314
MOOV | 0.7387 | 0.2613
CELTISS | 0.6003 | 0.3997

## Slide 27: Benchmarking: CS Integrity Voice quality Mean Opinion Score MOOV has the lower ratio of excellent and good Voice Quality samples compared to MTN’s and CELTISS’S,MTN needs to improve its voice quality MOS by pushing CS traffic to 3G and increase 2G full rate penetration.
Chart: Average MOS
| Avrege MOS
MTN | 3.79
MOOV | 3.95
CELTISS | 3.91
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Excel+Goog
MTN | 0.4209 | 0.4902 | 0.0327 | 0.0562 | 0.9111
MOOV | 0.7631 | 0.1869 | 0.0218 | 0.0282 | 0.95
CELTISS | 0.4022 | 0.5433 | 0.0265 | 0.0279 | 0.9455

## Slide 28: Benchmarking – CS Integrity Voice quality maps (MOS) In All roads, MTN has the lower ratio of excellent and good Voice Quality samples compared to CELTISS’s and MOOV’S. MTN is ranked third in terms of voice quality with an average MOS equal to 3,79 opposed to 3,95 for MOOV and 3,91 for CELTISS. 3d

## Slide 29: Benchmarking: Radio parameters EC/NO comparison 18,57% of drive test samples are showing a very low level of EcNo for 3G MTN MOOV with 18,57% and CELTISS with 23,55%.
Chart: Ec/No Distribution (%)
| -8 to 0 | -12 to -8 | -16 to -12 | -34 to -16 | ACCEPTABLE EC/N0
MTN | 0.3498 | 0.1778 | 0.2866 | 0.1857 | 0.5276
MOOV | 0.3128 | 0.2314 | 0.268 | 0.1878 | 0.5442
CELTISS | 0.375 | 0.2143 | 0.1752 | 0.2355 | 0.5893

## Slide 30: Benchmarking: Radio parameters EC/NO MTN has the highest ratio of very bad Ec/No samples (<-16db).

## Slide 31: Benchmarking – 2G/3G CALL SETUP TIME MTN is clear leader in terms of Call Setup Time.
Chart: Call Setup Time (s)
| Call Setup Time
MTN | 7.29
MOOV | 8.3
CELTISS | 8.9
Chart: CS Call setup Time by technology (s)
| 4G CSFB CST | 3G CST | 2G CST
MTN | 6.25 | 7.64 | 7.98
MOOV | 7.79 | 8.77 | 8.35
CELTISS | 8.91 | 8.82 | 8.98

## Slide 32: Benchmarking – SMS SENDING FAILURE MTN’s SMS SEND/RECEIVE SR(%) is better than MOOV and less than CELTISS . SMS service KPIs for all operators are not compliant with the ARCEP requirements due to the timeout of sending duration (< 6s).
Chart: SMS
| SMS Sending message success rate (%) | SMS Receving message success rate (%)
MTN | 0.922 | 0.9009
MOOV | 0.895 | 0.8814
CELTISS | 0.9112 | 0.9067
Chart: SMS Send Time(%)
| (0,3) | (3,6) | >6
MTN | 0.4011 | 0.5209 | 0.078
MOOV | 0.3654 | 0.5296 | 0.105
CELTISS | 0.392 | 0.5292 | 0.0788

## Slide 33
Benchmarking Data service
04

## Slide 34: Benchmarking – DATA 3G All operators failed to meet ARCEP thresholds.
Chart: PS Attach & PDP Contex Act(%)
| PS Attach success(%) | PDP Context Act Success (%)
MTN | 0.9525 | 0.9433
MOOV | 0.9122 | 0.941
CELTISS | 0.9347 | 0.9288
Chart: Attach & PDP Activation Time (s)
| PS Attach Setup Time | PDP Context Act Time
MTN | 2.25 | 2.09
MOOV | 2.45 | 2.66
CELTISS | 2.22 | 2.94

## Slide 35: Benchmarking – DATA 3G MTN has the lowest HTTP browsing success, All operators failled to meet ARCEP requirement for web service.
Chart: PS Connection setup time
| PS Connection setup time
MTN | 7.29
MOOV | 8.3
CELTISS | 8.77
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9333
MOOV | 0.8789
CELTISS | 0.883

## Slide 36: Benchmarking – DATA 3G Only CELTISS meet ARCEP requirements for FTP DL success ratio. Only MOOV meet ARCEP requirements for FTP UL success ratio.
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9542 | 0.9392
MOOV | 0.9366 | 0.9773
CELTISS | 0.9868 | 0.9296

## Slide 37: Benchmarking – 3G FTP MEAN THROUGHPUT MTN 3G Throughput DL is better than MOOV’s and CELTISS’s. MTN 3G Throughput UL is better than MOOV’s and less than CELTISS’s. All operators meet ARCEP thresholds.
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 4432.96 | 1867.87 | 15424.48 | 9324.11
MOOV | 3134.27 | 1352.87 | 11141.72 | 8654.88
CELTISS | 5867.9 | 1793.38 | 12444.15 | 10254.99

## Slide 38: Benchmarking – 3G FTP MEAN THROUGHPUT comparison map MTN Throughput distribution is better to MOOVand less than CELTISS.

## Slide 39: Benchmarking – 4G HTTP Browsing MTN’s HTTP Browsing success rate is best than MOOV’s and CELTISS’s. Only MTN meets ARCEP threasholds.
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9708
MOOV | 0.9533
CELTISS | 0.9526

## Slide 40: Benchmarking – 4G FTP THROUGHPUT comparison Only MTN meets ARCEP threasholds in FTP succes rate DL. All operetors failled to meet ARCEP threasholds in FTP succes rate UL.
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9941 | 0.9313
MOOV | 0.9326 | 0.9079
CELTISS | 0.875 | 0.9103

## Slide 41: Benchmarking – 4G FTP THROUGHPUT comparison MTN FTP DL AVERAGE Throughput is better than CELTISS. MTN FTP UL AVERAGE Throughput is better than MOOV & CELTISS.
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 39881.87 | 13135.49 | 180500.66 | 39240.87
MOOV | 10525.87 | 7045.87 | 181699.27 | 20106.75
CELTISS | 10351.44 | 9103.26 | 19475.22 | 14849.72

## Slide 42: Benchmarking – 4G FTP THROUGHPUT comparison map In LOKOSSA, MTN has an excellent end user throughput with more than 35,23% of samples better than 30Mbps .

## Slide 43: Benchmarking – BAND and TECHNOLOGY UTILISATION Most of MTN’s LTE samples are carried out over LTE 2600 as first carrier, Most of MOOV’s andCELTISS’s samples are carried out over LTE 800 as first carrier, For all operators,most of 3G samples are carried out over U2100, but MOOV has the highest ratio of U900 usage.
Chart: 3G band Distribution (%)
| UMTS 900 | UMTS 2100
MTN | 0.1123 | 0.8877
MOOV | 0.4855 | 0.5145
CELTISS | 0.2909 | 0.7091
Chart: 4G Band Distribution (%)
| LTE 800 | LTE 700 | LTE 1800 | LTE 2100 | LTE 2600
MTN | 0.3017 | 0.0536 | 0.1857 | 0.0027 | 0.4563
MOOV | 0.9233 | 0 | 0.0311 | 0 | 0.0456
CELTISS | 0.7467 | 0 | 0.2427 | 0 | 0.0106

## Slide 44: Benchmarking – Data TECHNOLOGY Usage(%) MTN has the highest LTE CA Carrier Aggregation usage with 81,79% against 46,12% for MOOV and 47,56% for CELTISS.
Chart: 3G Packet Technology usage (%)
| DC-HSPA | HSPA | HSDPA | UMTS
MTN | 0.3525 | 0.2314 | 0.0031 | 0.4129
MOOV | 0.1835 | 0.4067 | 0.0019 | 0.4078
CELTISS | 0.3049 | 0.1318 | 0.0266 | 0.5352
Chart: 4G Packet Technology usage (%)
| LTE | LTE CA
MTN | 0.1821 | 0.8179
MOOV | 0.5388 | 0.4612
CELTISS | 0.5244 | 0.4756

## Slide 45: Benchmarking – SINR comparison Drive tests are showing a acceptable level of MTN Network SINR.
Chart: SINR Comparison
| (Min,-4) | (-4,0) | (0,7) | (7,15 <) | ACCEPTABLE SINR
MTN | 0.0358 | 0.064 | 0.2034 | 0.6968 | 0.9002
MOOV | 0.0636 | 0.11 | 0.2551 | 0.5713 | 0.8264
CELTISS | 0.0835 | 0.1068 | 0.2268 | 0.5829 | 0.8097

## Slide 46: Benchmarking – SNIR comparison map 4G MTN has the better Signal of quality compared to MOOV’s and CELTISS’s.

## Slide 47
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2019 Deloitte Bénin SARL. Société du réseau Deloitte