## Slide 1
Network QoS
CALAVI Benchmarking report
November 7th, 2023

## Slide 2: Summary
INTRODUCTION | 5
1- Context & Report objectives 6 | 
2- Scope of Work 7 | 
3- Scope of intermediate Report 8 | 
PART1 Drive Test Results: Cotonou Benchmark | 12
PART2 OMC Audits | 65

## Slide 3: PART1 Summary
Drive tests Activity, Current Status & Progress | 12
Executive Summary | 15
Benchmarking Key Results | 21
Benchmarking Coverage | 26
Benchmarking Voice Service | 33
Benchmarking Data Service | 44
Next Steps | 63

## Slide 4: PART2 Summary
OMC Network Configuration Overview | 73
Executive Summary | Ongoing
PM Data Audit | 70
1- Traffic Distribution 71 | 
2- Network Availability 74 | 
3- Network Retainability 76 | 
4- Network Accessibility 81 | 
5- Network mobility 83 | 
6- Network Throughputs 85 | 
7- Interference 88 | 
8- ARCEP OMC KPI 90 | 
Capacity Audit | 95
1 - 2G Capacity 96 | 
2 – 3G Capacity 98 | 
3 – 4G Capacity 101 | 
4 – Bottleneck 104 | 
CM Data Audit | Ongoing

## Slide 5
Introduction: Context & Report objectives
01

## Slide 6: Context & Report objectives
1
MTN Benin holds a prominent position as a leading mobile operator in Benin, with a market share of over 60%.
2
It operates a network comprising of 675 2G, 3G and LTE sites across Benin.
3
MTN Benin wants an independent assessment and benchmarking of its radio network through drive tests
4
MTN Benin also wants to ascertain network assurance and capacities
Overview of the NW QoS assessment scope
A comprehensive drive testing exercise to assess customer-perceived radio network quality in MTN Benin's 2G, 3G, and LTE network compared to competitors and as required by the regulator.
Formulate drive test methodology and coverage
Finalize reporting format and KPIs to be measured
Conduct drive tests for MTN Benin and competitor’s network
Validate results with MTN Benin’s radio planning team
Benchmark key KPIs between MTN, competition and regulator defined KPIs levels
Recommendations for network improvement
1
2
3
4
5
6
Detailed scope
Objectives of the assignment
2G/3G/4G MTN Networks KPIs audit based on OSS counters
Parameters settings audit of 2G/3G/4G MTN network
Capacity audit of 2G/3G/4G MTN network
Evaluate and benchmark Quality levels offered by MTN to MOOV mobiles networks and regulator defined KPIs levels based on Drive Test measurements results

## Slide 7
Introduction: Scope of Work
02

## Slide 8: Scope of work (i/ii)
Conduct OSS Audit
  2G/3G/4G MTN Networks KPIs audit based on OSS counters
  Parameters settings audit of 2G/3G/4G MTN network
  Capacity audit of 2G/3G/4G MTN network
Hourly KPI review
HW / Alarms review
RAN Parameters
RAN Features
Neighbors
HW/licensing
Kick-off
Prerequisites
Data collection
Result analysis
Suggest Recommendations
audit report written
Presentation and actions
Close out report
Preparation
Early KPI
warning
Configuration Audit
Performance Analysis
Dimensioning
Reporting
Evaluate and benchmark Quality levels offered by MTN to MOOV mobiles networks and regulator’s defined KPIs levels based on Drive Test measurements results
  Voice service quality and SMS (one team with Drive test tool)
  3G Data FTP DL/UL and HTTP Browsing (one team with Drive test tool)
  4G Data FTP DL/UL and HTTP Browsing (one team with Drive test tool)
Drive Test execution
Post processing and report preparation
Kick-off
Prerequisites
Drive Test route preparation
Deep Analysis and
Recommendations
Presentation
Preparation
Network Data Collection
Post Processing
Events and layer 3 analysis
Reporting

## Slide 9: Scope of Work (ii/ii)
Cost
Cities to be covered
Cost
Drive Test KPI
Data KPIs (2G/3G/LTE)
HTTP Browsing Success Ratio
Session Setup time
FTP Session Success Rate
FTP UL/DL Throughput
Coverage rate (2G/3G/LTE)
Outoor Coverage rate
Indoor coverage rate
Incar coverage rate
Voice KPIs
Call blocking rate
Call drop rate
Call completion success rate
Call completion, with perfect quality, rate
Call completion, with good quality, rate
Voice Quality (MOS)
SMS
MO SMS delivery success rate
MT SMS delivery success rate
16 indicators to analyze
18 thousand samples to analyze

## Slide 10
Introduction: Scope of Intermediate Report
03

## Slide 11: Benchmarking report
Scope of this report
  1. Network benchmarking results for the CALAVI area between MTN, MOOV, and CELTISS from September 9th to September 13th, 2023..
2. A RAN network audit for MTN BENIN, aiming to identify weak points as well as suggests proposals to improve the network quality, and so the final user perception
  Audit is based on Performance Measurement data mainly between 19th September to 04th October 2023 and Configuration settings of 4th October
  This intermediate report includes the PM and capacity audit, CM audit is ongoing
  Comments and recommendations may be enriched on final report using CM audit findings

## Slide 12
Drive Test Results: Competitive Network Benchmarking report CALAVI
Part1

## Slide 13
Drive tests Activity, Current Status & Progress
01

## Slide 14: Drive tests Activity, Current Status & Progress Drive test and Benchmark evaluation is on track according to initial plan
The Drive Test execution is ongoing as initially planned
We have processed more than 100%

## Slide 15
Benchmarking Executive Summary
02

## Slide 16: Executive Summary – Benchmarking coverage 2G/3G/4G
Coverage 2G/3G/4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Tune and align power settings mainly in 3G/4G. Actual setting may impact the coverage strength specially at Indoor locations
Review the design at the coverage and quality blackspots
We highlight that 4G ARCEP coverage Thresholds are aggressive
* Final recommendations will be shared in the final report including details and findings from ongoing Configuration Audit
MTN has outperformed its competitors in terms of 2G coverage for outdoor and Incar morphologies ,
For 2G RF coverage, All operators meet ARCEP obligation for all morphologies,
3G MTN’s coverage rate (90,02%) is lower than CELTISS (93,13%) and better than MOOV with (89,35%),
Only MTN and CELTISS meet ARCEP 3G coverage obligation
MTN is in third position in terms of 4G coverage rate for all morphologies,
All operators failed to satisfied the ARCEP threshold for indoor coverage.
updated

## Slide 17: Executive Summary – Benchmarking voice service 2G/3G
Voice service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Accessibility: MTN is ranked first for the accessibility to voice service , better than CELTISS and MOOV,
All operators meet ARCEP requirements in terms of accessibility to voice service,
Retainability: MTN is ranked second in term of retainability,
MTN's Call Drop Rate is (0.31%) better than MOOV (1.03%) and lower than CELTISS (0.15%).Only MTN and CELTISS meet ARCEP retainabilty requirements,
Integrity: MTN is in third position in terms of voice quality lower than MOOV and CELTISS with average Mean Opinion Score 3.73 as opposed to 3.85 for CELTISS and 3.87 for MOOV.
To improve its Mean Opinion Score MOS MTN needs to improve its 3G radio parameter Ec/No that is closely related to voice quality,
Voice quality is always better in 3G due to its better codec rate , we recommend to push as much as possible the voice traffic to 3G,
2G Full Rate/Half Rate settings need to be tuned in order to improve Full rate penetration.
* Final recommendations will be shared In the final report including details and findings from ongoing Configuration Audit
updated

## Slide 18: Executive Summary – Benchmarking SMS service
SMS service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
All operators failed to meet ARCEP for SMS Send Success with End To End Delivery Time < 6 sec,
In CALAVI, MTN has the best SMS send/Receive succes ratio and the best distrution for SMS send duration.
There is no issue in radio accessibility that could be correlated to the SMS high delivery time.
End to End investigation need to be performed to analyses the high delivery time including mainly Core/SMS parts: SM Sserver...
* Final recommendations will be shared in the final report including details and findings from ongoing Configuration Audit
Updated

## Slide 19: Executive Summary – Benchmarking 4G Data service
Data service 4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 4G data service, and all operators meet ARCEP's requirements.
MTN is ranked second in terms of 4G DL throughput with 19.46Mbps, which is better than CELTISS’s 12.67Mbps but lower than MOOV’s 22.70Mbps.
MTN is ranked first in terms of 4G UL throughput with 16.19Mbps, as opposed to 14.25Mbps for MOOV and 12.26Mbps for CELTISS.
All operators meet ARCEP's 4G End User Throughput obligation for download and upload.
Updated
MTN spectrum need to be used with a better efficiency, Some features and parameters need to be tuned and aligned,
To improve its 4G DL Throughput, MTN needs to optimize the carrier aggregation, MIMO settings and modulation,
To ensure that no throughput limitation is applied on users profiles.

## Slide 20: Executive Summary – Benchmarking 3G Data service
Data service 3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 3G data service, and all operators meet ARCEP's requirements.
MTN is in third position for 3G DL throughput with 2.96Mbps, compared to 4.20Mbps for CELTISS and 3.76Mbps for MOOV.
MTN is ranked second in term of 3G UL throughput with 1.20 Mbps against 1.16 Mbps for MOOV and 2.07Mbps for CELTISS,
All operators meets ARCEP’s 3G End User Throughput obligation for download and upload.
All operators meet ARCEP’s web browsing service accessibility thresholds.
To improve its 3G throughput MTN needs to activate HSPA-DC,
Its recommended to push as much as possible the data traffic to 4G in order to:
- Improve end user perception, Both DT and stats are showing that users in average are served with up to 6x better throughput in 4G than in 3G
- Offload the 3G network which will improve the 3G throughput and the 3G radio quality
Some features and parameters need to be tuned and aligned,
To ensure that no throughput limitation is applied on users profiles.
Updated

## Slide 21
Benchmarking Key Results
03

## Slide 22: Benchmarking Key Results – Coverage MTN has the best 2G coverage except for Indoor morphology, Only MTN and CELTISS meet ARCEP requirements for 3G coverage, In CALAVI, MTN is in third position in terms of 4G coverage for all morphologies, All operators failed to meet ARCEP requirements in Indoor 4G coverage.
KPI |  | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
2G Coverage Rate | Incar | More than 90% with Incar: Rxlev >-87 dBm | 99,99% | OK | 99,97% | OK | 99,97% | OK | 1
 | Outdoor | More than 90% with Outdoor: Rxlev >-92 dBm | 100% | OK | 100% | OK | 100% | OK | 2
 | Indoor | More than 90% with Outdoor: Rxlev >-74 dBm | 92,73% | OK | 92,83% | OK | 96,73% | OK | 3
3G Coverage Rate | Incar,Indoor,Outdoor | More than 90% with RSCP <-85 dBm | 90,02% | OK | 89,35% | NOK | 93,13% | OK | 2
4G Coverage Rate | Incar | More than 90% with RSRP <-90 dBm* | 91,95% | OK | 97,91% | OK | 95,91% | OK | 3
 | Outdoor | More than 90% with RSRP <-95 dBm* | 97,27% | OK | 99,18% | OK | 98,73% | OK | 3
 | Indoor | More than 90% with RSRP <-78 dBm* | 50,29% | NOK | 57,29% | NOK | 57,38% | NOK | 3
Updated

## Slide 23: Benchmarking Key Results – 2G/3G voice and SMS Summary MTN’s network KPIs meet ARCEP requirements except for SMS service due to the high end to end delivery time, MTN is leading in terms of accessibility to voice service, MTN needs to improve its Voice Quality MOS and SMS Send duration.
KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  | Value | Conformity | Value | Conformity | Value | Conformity | 
Accesibility: Blocking rate | <1% | 0,82% | OK | 0,94% | OK | 0,91 | OK | 1
Retainability: Call drop rate | <1% | 0,31% | OK | 1,03% | NOK | 0,15% | OK | 2
Call Completetion Rate (%) | =<98% | 98,87% | OK | 98,03% | OK | 98,94% | OK | 1
Integrity: Voice quality | Note requise> 2,8 | 3,73 | OK | 3,87 | OK | 3,85 | OK | 3
SMS sending success rate % (E2E delivery Time<6 sec) | >99% | 90,59% | NOK | 89,35% | NOK | 83,67% | NOK | 1
SMS receving success rate % | >99% | 88,88% | NOK | 88,10% | NOK | 82,44% | NOK | 1
Updated

## Slide 24: Benchmarking Key Results – 3G Data Summary MTN’s network in 3G DATA meets ARCEP requirements, MTN is ranked third in term of 3G DL throughput.
Services | KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
3G HTTP | Successful internet connexion rate | >96% | 100,00% | OK | 99,27% | OK | 100,00% | OK | 1
 | Connexion setup time | <=10sec | 5,33 | OK | 6,49 | OK | 6,02 | OK | 1
 | Web service failure rate | <3% | 0,24% | OK | 2,06% | OK | 0,12% | OK | 1
3G FTP | FTP failure rate UL/DL | <3 % | 0%/0,71% | OK | 1,35%/1,89% | OK | 0,71%/0,26% | OK | 1
 | FTP Data transmission average (DL) | >= 2Mbps | 2,963 | OK | 3,762 | OK | 4,201 | OK | 3
 | FTP Data transmission average (UL) | >= 1Mbps | 1,207 | OK | 1,164 | OK | 2,078 | OK | 2
Updated

## Slide 25: Benchmarking Key Results – 4G Data Summary MTN’s 4G DATA End User KPIs satisfy ARCEP requirements, MTN is ranked second in 4G DL THP after MOOV’s , MTN has outperformed its competitors in terms of 4G UL THP.
Services | KPI | Threshorlds* | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
4G HTTP Browsing | Web service failure rate (%) | <3% | 0,09% | OK | 0,22% | OK | 0,11% | OK | 1
 | Connexion setup time | <=3sec | 0,49 | OK | 0,51 | OK | 0,66 | OK | 1
4G FTP | FTP failure rate UL/DL | <3 % | 0,43%/0,88% | OK | 0%/0,46% | OK | 0%/0,28% | OK | 3
 | FTP Data transmission average (DL) | 4G >= 5 Mbps | 19,467 | OK | 22,708 | OK | 12,677 | OK | 2
 | FTP Data transmission average (UL) | 4G: >= 2Mbps | 16,192 | OK | 14,256 | OK | 12,265 | OK | 1
Updated

## Slide 26
Benchmarking 2G/3G/4G coverage
04

## Slide 27: Benchmarking: 2G coverage MTN, MOOV and CELTISS’s 2G coverage meets ARCEP RxLev thresholds, MTN has the best 2G coverage for Incar and outdoor morphologies.
Chart: 2G RxLev Distribution (%)
| Indoor>-74 | Incar >-87 | Outdoor >-92
MTN | 0.9273 | 0.9999 | 1
MOOV | 0.9283 | 0.9997 | 1
CELTISS | 0.9673 | 0.9997 | 1
Updated

## Slide 28: Benchmarking: 2G coverage - Maps MTN has more than 92,73% of RxLev samples better than -74dBm,against 92,83% for MOOV and 96,73% for CELTISS.
Updated

## Slide 29: Benchmarking: 3G coverage CELTISS has the best 3G coverage, MTN’s and CELTISS’s 3G coverage meet ARCEP requirements.
Chart: 3G RSCP Distribution (%)
| Indoor,Incar,Outdoor >-85
MTN | 0.9002
MOOV | 0.8935
CELTISS | 0.9313
Updated

## Slide 30: Benchmarking: 3G coverage-Maps CELTISS has the best 3G coverage with 93,13% better than -85dBm against 90,02% for MTN and 89,35% for MOOV.
Updated

## Slide 31: Benchmarking: 4G coverage CELTISS has the best 4G coverage for incar and outdoor morphologies but all operators failed to satisfy ARCEP requirements for indoor, MTN is ranked third in terms of 4G coverage and closely simular to competitors for outdoor morphology.
Chart: 4G RSRP Distribution (%)
| Indoor > -78 | Incar > -90 | Outdoor > -95
MTN | 0.5029 | 0.9195 | 0.9727
MOOV | 0.5729 | 0.9791 | 0.9918
CELTISS | 0.5738 | 0.9591 | 0.9873
Updated

## Slide 32: Benchmarking – 4G coverage - Maps MTN’s 4G coverage is lower than MOOV’s and CELTISS’s.
Updated

## Slide 33
Benchmarking voice service
04

## Slide 34: Benchmarking: CS Accessibility 2G/3G BLOCKED CALLS MTN has the best accessibility to voice service compared to competitors, All operators meet ARCEP requirements in terms of accessibility.
Chart: Call Blocked Rate (%)
| CBR (%)
MTN | 0.0082
MOOV | 0.0094
CELTISS | 0.0091
Chart: Call Blocked Rate per Technology (%)
| CBR (%)
MTN 2G | 0.0127
MTN 3G | 0.011
MOOV 2G | 0
MOOV 3G | 0.014
CELTISS 2G | 0
CELTISS 3G | 0.0091
Updated

## Slide 35: Benchmarking: CS Integrity Voice quality Mean Opinion Score CELTISS has the best ratio of excellent and good Voice Quality samples compared to MTN and MOOV,MTN needs to improve its voice quality MOS by pushing CS traffic to 3G and increase 2G full rate penetration, MOOV has the best MOS with 3,73 opposed to 3,87 for MOOV and 3,85 for CELTISS.
Chart: Average MOS
| Avrege MOS
MTN | 3.73
MOOV | 3.87
CELTISS | 3.85
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Excel+Goog
MTN | 0.3513 | 0.5159 | 0.0828 | 0.05 | 0.8672
MOOV | 0.8713 | 0.1019 | 0.0154 | 0.0113 | 0.9732
CELTISS | 0.6076 | 0.3797 | 0.0093 | 0.0034 | 0.9873
Updated

## Slide 36: Benchmarking – CS Integrity Voice quality maps (MOS) MTN has around 5% of MOS samples lower than 2.2 against 1,13% for MOOV and 0,34% for CELTISS.MOS Values lower than 2,2 pose risk of bad users perceived voice quality and silent call. 3d
Updated

## Slide 37: Benchmarking: CS Retainability 2G/3G DROPPED CALLS MTN and CELTISS satisfy ARCEP thresholds regarding Call Drop Rate.
Chart: Call Drop Rate (%)
| CDR (%)
MTN | 0.0031
MOOV | 0.0103
CELTISS | 0.0015
Updated

## Slide 38: Benchmarking Voice service Band usage(%) MTN has the highest ratio of 2G use, 36.74% of voice calls carried out over 2G network but CELTISS and MOOV use mainily 3G, Recommended for MTN to reduce 2G usage and increase 3G penetration for better audio quality. MTN's 2G band usage: 77,02% GSM 900 and 22,98% GSM 1800 Mhz, 3G band usage: MTN uses mainly U900, CELTISS and MOOV use mainly U2100.
Chart: System Technology usage(%)
| GSM | UMTS
MTN | 0.3674 | 0.6326
MOOV | 0.1095 | 0.8905
CELTISS | 0 | 1
Chart: 2G Band usage(%)
| GSM 900 | GSM 1800
MTN | 0.7702 | 0.2298
MOOV | 0.7009 | 0.2991
CELTISS
Chart: 3G Band usage(%)
| UMTS 900 | UMTS 2100
MTN | 0.7525 | 0.2475
MOOV | 0.1405 | 0.8595
CELTISS | 0.1582 | 0.8418
Updated

## Slide 39: Benchmarking: Radio parameters EC/NO comparison 36,14% of drive test samples are showing a very low level of EcNo for 3G MTN. This is correlated to the number of 3G carriers : MTN is using 2 carriers against 3 and 4 for CELTISS and MOOV respectively. Also 3G traffic is carried mainly by U2100 for competitors while it’s distributed over U900 and U2100 for MTN. Bad Ec/No has great impact on voice quality.
Chart: 3G Ec/No Distribution (%)
| -8 to 0 | -12 to -8 | -16 to -12 | -34 to -16 | ACCEPTABLE EC/N0
MTN | 0.0506 | 0.1246 | 0.4634 | 0.3614 | 0.1752
MOOV | 0.399 | 0.3019 | 0.2449 | 0.0443 | 0.7009
CELTISS | 0.7287 | 0.2129 | 0.0505 | 0.0079 | 0.9416
Updated

## Slide 40: Benchmarking: Radio parameters EC/NO 3G MOOV’s and CELTISS’s EC/N0 is better than MTN’s due to the number of 3G used carriers and 3G band distribution by using mainly U900 for MTN.
Updated

## Slide 41: Benchmarking – 2G/3G CALL SETUP TIME MTN has the best Call setup time.
Chart: Call Setup Time (s)
| Call Setup Time
MTN | 6.84
MOOV | 7.01
CELTISS | 6.99
Updated

## Slide 42: Benchmarking – CALL SETUP TIME/Call Mode MTN has the best 4G CSBF Call setup Time, Call setup time 2G is higher than in 3G/4G.
Chart: CS Call setup Time by technology (s)
| 4G CSFB CST | 3G CST | 2G CST
MTN | 7.21 | 6.89 | 6.98
MOOV | 8.6 | 7.33 | 8.34
CELTISS | 8.5 | 8.61
For check

## Slide 43: Benchmarking – SMS Service In CAVALI, MTN’s SMS Send/Recieve success ratio is better than CELTISS’s & MOOV’s. SMS service KPIs for all operators are not compliant with the ARCEP requirements due to the timeout of sending duration (< 6s).
Chart: SMS Send Time Distribution (%)
| (0,3) | (3,6) | >6
MTN | 0.5801 | 0.3258 | 0.0941
MOOV | 0.6042 | 0.2893 | 0.1065
CELTISS | 0.6245 | 0.2122 | 0.1633
Chart: SMS Send/Received SR(%)
| SMS Sending message success rate (%) | SMS Receving message success rate (%)
MTN | 0.9059 | 0.8888
MOOV | 0.8935 | 0.881
CELTISS | 0.8367 | 0.8244
Updated

## Slide 44
Benchmarking Data service
04

## Slide 45: Benchmarking – DATA 3G All operators have a good rate of successful Internet connection.
Chart: PS Attach & PDP Contex Act(%)
| PS Attach success(%) | PDP Context Act Success (%)
MTN | 1 | 0.9988
MOOV | 0.9927 | 0.9941
CELTISS | 1 | 0.9971
Chart: Attach & PDP Activation Time (s)
| PS Attach Setup Time | PDP Context Act Time
MTN | 1.2 | 1.47
MOOV | 1.33 | 1.39
CELTISS | 1.34 | 1.58
Updated

## Slide 46: Benchmarking – DATA 3G Web service All operators have an excellent web service success rate. MTN has best time to connect to web service.
Chart: PS Connection setup time
| PS Connection setup time
MTN | 5.33
MOOV | 6.49
CELTISS | 6.02
Chart: 3G HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9976
MOOV | 0.9794
CELTISS | 0.9988
Updated

## Slide 47: Benchmarking – DATA 3G FTP service All operators have a good downlink and uplink FTP success rate and meet ARCEP requirements.
Chart: 3G FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 1 | 0.9929
MOOV | 0.9865 | 0.9811
CELTISS | 0.9929 | 0.9974
updated

## Slide 48: Benchmarking – 3G FTP MEAN THROUGHPUT All operators meet ARCEP requirement in terms of FTP DL/UL throughput, MTN has the lowest 3G FTP DL throughput, MTN is in the second position in terms of FTP UL Throughput.
Chart: 3G FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 2963.37 | 1207 | 11737.85 | 12512.54
MOOV | 3762.44 | 1164.53 | 26933.88 | 14925.39
CELTISS | 4201.33 | 2078.29 | 18279 | 7408.41
Updated

## Slide 49: Benchmarking – 3G FTP MEAN THROUGHPUT comparison map All operators have 100% of FTP DL Throughput samples better than 2Mbps.
Updated

## Slide 50: Benchmarking – DATA 4G Web browsing service For 4G, All operators have very good HTTP Browsing success rate and meet ARCEP requirements.
Chart: 4G HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9991
MOOV | 0.9978
CELTISS | 0.9989
Updated

## Slide 51: Benchmarking – 4G FTP THROUGHPUT comparison All operators have acceptable FTP success rate and largely meet the ARCEP criteria.
Chart: 4G FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9957 | 0.9912
MOOV | 1 | 0.9954
CELTISS | 1 | 0.9978
Updated

## Slide 52: Benchmarking – 4G FTP THROUGHPUT comparison MTN is ranked second in terms of FTP DL throughput, MTN has outperformed its competitors in terms of FTP UL throughput, All operators meet ARCEP requirements for 4G DL/UL throughput.
Chart: 4G FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 19467.82 | 16192.44 | 192461.15 | 37350.35
MOOV | 22708.55 | 14256.16 | 155977.8 | 27217.29
CELTISS | 12677.21 | 12265.83 | 32124.35 | 14522.37
Updated

## Slide 53: Benchmarking – 4G FTP THROUGHPUT comparison map CELTISS has 98,78% of DL throughput samples better than 5Mbps against 93,98% for MTN and 87,59% for MOOV.
Updated

## Slide 54: Benchmarking – BAND and TECHNOLOGY UTILISATION Most of MTN’s and MOOV’s LTE samples are carried out over LTE 2600 as first carrier, Most of CELTISS’s LTE samples in CALAVI are carried out over LTE 1800 as first carrier, Most of CELTISS’s and MOOV’s 3G samples are carried out over U2100, but MTN has the highest ratio of U900 usage (47,67%).
Chart: 3G Band Distribution (%)
| UMTS 900 | UMTS 2100
MTN | 0.4767 | 0.5233
MOOV | 0.0645 | 0.9355
CELTISS | 0.0081 | 0.9919
Chart: 4G Band Distribution (%)
| LTE 800 | LTE 700 | LTE 1800 | LTE 2100 | LTE 2600
MTN | 0.0171 | 0.0061 | 0.0092 | 0.009 | 0.9586
MOOV | 0.256 | 0 | 0.0198 | 0 | 0.7242
CELTISS | 0.0335 | 0 | 0.9643 | 0 | 0.0022
Updated

## Slide 55: Benchmarking – Data TECHNOLOGY Usage(%) MTN has the highest LTE Carrier Aggregation usage, with 86,40% against 55,36% for MOOV and 51,02% for CELTISS, MTN needs to improve its LTE CA usage to get the best 4G throughput, To improve its 3G data throughput, its is recommended for MTN to use HSPA-DC.
Updated
Chart: 4G Packet Technology usage (%)
| LTE | LTE CA
MTN | 0.136 | 0.864
MOOV | 0.4464 | 0.5536
CELTISS | 0.4898 | 0.5102
Chart: 3G Packet Technology usage (%)
| DC-HSPA | HSPA | HSDPA | UMTS
MTN | 0 | 0.6221 | 0.0006 | 0.3773
MOOV | 0.5014 | 0.0726 | 0.0078 | 0.4182
CELTISS | 0.4849 | 0.0366 | 0.0351 | 0.4433

## Slide 56: Benchmarking – SINR comparison Drive results are showing that MTN’s Network has the SINR distribution with the highest percentage of acceptable SINR.
Chart: 4G SINR Comparison
| (Min,-4) | (-4,0) | (0,7) | (7,15 <) | ACCEPTABLE SINR
MTN | 0.0178 | 0.054 | 0.3196 | 0.6085 | 0.9281
MOOV | 0.0325 | 0.0889 | 0.3587 | 0.5199 | 0.8786
CELTISS | 0.0139 | 0.0792 | 0.2869 | 0.62 | 0.9069
Updated

## Slide 57: Benchmarking – SNIR comparison maps MTN’s 4G network has the best quality of signal compared to MOOV’s and CELTISS’s.
Updated

## Slide 58
Next steps
05

## Slide 59: Next steps
Complete 2G & 3G drive tests: Remaining areas (north area of Benin)
Conduct deep analysis on drive tests results
Complete cross analysis on KPIs and OSS parameters with drive tests results and call traces
Issue final report and recommendations

## Slide 60
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2019 Deloitte Bénin SARL. Société du réseau Deloitte