## Slide 1
Network QoS
LOKOSSA Benchmarking report
November 7th, 2023

## Slide 2: Summary
INTRODUCTION | 5
1- Context & Report objectives 6 | 
2- Scope of Work 7 | 
3- Scope of intermediate Report 8 | 
PART1 Drive Test Results: Cotonou Benchmark | 12
PART2 OMC Audits | 65

## Slide 3: PART1 Summary
Drive tests Activity, Current Status & Progress | 12
Executive Summary | 15
Benchmarking Key Results | 21
Benchmarking Coverage | 26
Benchmarking Voice Service | 33
Benchmarking Data Service | 43
Next Steps | 63

## Slide 4: PART2 Summary
OMC Network Configuration Overview | 73
Executive Summary | Ongoing
PM Data Audit | 70
1- Traffic Distribution 71 | 
2- Network Availability 74 | 
3- Network Retainability 76 | 
4- Network Accessibility 81 | 
5- Network mobility 83 | 
6- Network Throughputs 85 | 
7- Interference 88 | 
8- ARCEP OMC KPI 90 | 
Capacity Audit | 95
1 - 2G Capacity 96 | 
2 – 3G Capacity 98 | 
3 – 4G Capacity 101 | 
4 – Bottleneck 104 | 
CM Data Audit | Ongoing

## Slide 5
Introduction: Context & Report objectives
01

## Slide 6: Context & Report objectives
1
MTN Benin holds a prominent position as a leading mobile operator in Benin, with a market share of over 60%.
2
It operates a network comprising of 675 2G, 3G and LTE sites across Benin.
3
MTN Benin wants an independent assessment and benchmarking of its radio network through drive tests
4
MTN Benin also wants to ascertain network assurance and capacities
Overview of the NW QoS assessment scope
A comprehensive drive testing exercise to assess customer-perceived radio network quality in MTN Benin's 2G, 3G, and LTE network compared to competitors and as required by the regulator.
Formulate drive test methodology and coverage
Finalize reporting format and KPIs to be measured
Conduct drive tests for MTN Benin and competitor’s network
Validate results with MTN Benin’s radio planning team
Benchmark key KPIs between MTN, competition and regulator defined KPIs levels
Recommendations for network improvement
1
2
3
4
5
6
Detailed scope
Objectives of the assignment
2G/3G/4G MTN Networks KPIs audit based on OSS counters
Parameters settings audit of 2G/3G/4G MTN network
Capacity audit of 2G/3G/4G MTN network
Evaluate and benchmark Quality levels offered by MTN to MOOV mobiles networks and regulator defined KPIs levels based on Drive Test measurements results

## Slide 7
Introduction: Scope of Work
02

## Slide 8: Scope of work (i/ii)
Conduct OSS Audit
  2G/3G/4G MTN Networks KPIs audit based on OSS counters
  Parameters settings audit of 2G/3G/4G MTN network
  Capacity audit of 2G/3G/4G MTN network
Hourly KPI review
HW / Alarms review
RAN Parameters
RAN Features
Neighbors
HW/licensing
Kick-off
Prerequisites
Data collection
Result analysis
Suggest Recommendations
audit report written
Presentation and actions
Close out report
Preparation
Early KPI
warning
Configuration Audit
Performance Analysis
Dimensioning
Reporting
Evaluate and benchmark Quality levels offered by MTN to MOOV mobiles networks and regulator’s defined KPIs levels based on Drive Test measurements results
  Voice service quality and SMS (one team with Drive test tool)
  3G Data FTP DL/UL and HTTP Browsing (one team with Drive test tool)
  4G Data FTP DL/UL and HTTP Browsing (one team with Drive test tool)
Drive Test execution
Post processing and report preparation
Kick-off
Prerequisites
Drive Test route preparation
Deep Analysis and
Recommendations
Presentation
Preparation
Network Data Collection
Post Processing
Events and layer 3 analysis
Reporting

## Slide 9: Scope of Work (ii/ii)
Cost
Cities to be covered
Cost
Drive Test KPI
Data KPIs (2G/3G/LTE)
HTTP Browsing Success Ratio
Session Setup time
FTP Session Success Rate
FTP UL/DL Throughput
Coverage rate (2G/3G/LTE)
Outoor Coverage rate
Indoor coverage rate
Incar coverage rate
Voice KPIs
Call blocking rate
Call drop rate
Call completion success rate
Call completion, with perfect quality, rate
Call completion, with good quality, rate
Voice Quality (MOS)
SMS
MO SMS delivery success rate
MT SMS delivery success rate
16 indicators to analyze
18 thousand samples to analyze

## Slide 10
Introduction: Scope of Benchmarking Report « LOKOSSA »
03

## Slide 11: Benchmarking report
Scope of this report
  1. Network benchmarking results for the LOKOSSA area between MTN, MOOV, and CELTISS from September 9th to September 13th, 2023..
2. A RAN network audit for MTN BENIN, aiming to identify weak points as well as suggests proposals to improve the network quality, and so the final user perception
  Audit is based on Performance Measurement data mainly between 19th September to 04th October 2023 and Configuration settings of 4th October
  This intermediate report includes the PM and capacity audit, CM audit is ongoing
  Comments and recommendations may be enriched on final report using CM audit findings

## Slide 12
Drive Test Results: Competitive Netwrk Benchmaring LOKOSSA
Part1

## Slide 13
Drive tests Activity, Current Status & Progress
01

## Slide 14: Drive tests Activity, Current Status & Progress Drive test and Benchmark evaluation is on track according to initial plan
The Drive Test execution is ongoing as initially planned
We have processed more than 100%

## Slide 15
Benchmarking Executive Summary
02

## Slide 16: Executive Summary – Benchmarking coverage 2G/3G/4G
Coverage 2G/3G/4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Tune and align power settings mainly in 3G/4G. Actual setting may impact the coverage strength specially at Indoor locations
Review the design at the coverage and quality blackspots
We highlight that 4G ARCEP coverage Thresholds are aggressive
* Final recommendations will be shared in the final report including details and findings from ongoing Configuration Audit
MTN has outperformed its competitors in terms of 2G coverage for outdoor and Indoor morphologies ,
For 2G RF coverage, Only MTN meets ARCEP obligation for all morphologies,
MTN is leading in terms of 3G coverage rate with (94,09%) against (86,16%) for CELTISS and (88,98%) for MOOV
Only MTN meets ARCEP 3G coverage obligation
MTN is in the second position in terms of 4G coverage rate for Incar and Outdoor morphologies but meets ARCEP thresholds,
All operators failed to satisfied the ARCEP threshold for indoor coverage for 4G network.
updated

## Slide 17: Executive Summary – Benchmarking voice service 2G/3G
Voice service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Accessibility: MTN is leading in terms of accessibility to voice service by having the best Call Blocked ratio with 0,58% against 0,86% for MOOV and 0,84% for CELTISS,
All operators failed to meet ARCEP accessibility thresholds,
Retainability: MTN is ranked first in term of retainability better than MOOV and CELTISS,
MTN's Call Drop Rate is 0.38% compared to 0.78% for CELTISS and 0.55% for MOOV.All operators meet ARCEP retainabilty requirements,
Integrity: MTN is in second position in terms of voice quality with average Mean Opinion Score equal to 4,02 lower than MOOV 4,21 and better than CELTISS 3,94
In LOKOSSA the MTN’s MOS value is better than other area, because the voice quality is carried out mainly over 3G unlike other areas .
Voice quality is always better in 3G due to its better codec rate , we recommend to push as much as possible the voice traffic to 3G,
Drive test results are showing that MTN has a bad Ec/No, by improving this radio parameter we can improve further the voice quality MOS.
updated
further

## Slide 18: Executive Summary – Benchmarking SMS service
SMS service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
All operators failed to meet ARCEP for SMS Send Success with End To End Delivery Time who should be less than < 6 sec as defined by ARCEP.
MTN is better than MOOV and lower than CELTISS.
There is no issue in radio accessibility that could be correlated to the SMS high delivery time.
End to End investigation need to be performed to analyses the high delivery time including mainly Core/SMS parts: SM Sserver...
* Final recommendations will be shared in the final report including details and findings from ongoing Configuration Audit
updated

## Slide 19: Executive Summary – Benchmarking 4G Data service
Data service 4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 4G data service, and all operators meet ARCEP's requirements.
MTN is leading in terms of 4G DL throughput with 57.41Mbps, better than MOOV 27.51Mbps and CELTISS 12.93Mbps.
MTN is ranked first in terms of 4G UL throughput with 18.74Mbps, as opposed to 13.53Mbps for MOOV and 11.47Mbps for CELTISS.
For 4G network, all operators meet ARCEP’s End User Throughput obligation in download and upload.
In LOKOSSA, MTN has an excellent performance in term of 4G KPIs.
updated

## Slide 20: Executive Summary – Benchmarking 3G Data service
Data service 3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 3G data service, and all operators meet ARCEP's requirements.
MTN is in third position for 3G DL throughput with 2.2Mbps, compared to 4.62Mbps for CELTISS and 3.33Mbps for MOOV.
MTN is ranked second in term of 3G UL throughput with 1.04 Mbps against 1.01 Mbps for MOOV and 2.15Mbps for CELTISS,
All operators meets ARCEP’s 3G End User Throughput obligation for download and upload.
All operators meet ARCEP’s web browsing service accessibility thresholds.
Its recommended to push as much as possible the data traffic to 4G in order to:
- Improve end user perception, Both DT and stats are showing that users in average are served with an excellent throughput in 4G,
- Offload the 3G network which will improve the 3G throughput and the 3G radio quality
Increasing the utilization of 3G data technology HSPA-DC can improve 3G throughput,
Some features and parameters need to be tuned and aligned
To ensure that no throughput limitation is applied on users profiles
updated

## Slide 21
Benchmarking Key Results
03

## Slide 22: Benchmarking Key Results – Coverage For 2G RF coverage, Only MTN meets ARCEP obligation for all morphologies, In LOKOSSA, MTN has recorded the best RF 3G coverage, MTN is ranked second in term of RF 4G coverage for Incar and outdoor morphologies, All operators failed to meet ARCEP requirements for 4G indoor coverage.
KPI |  | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
2G Coverage Rate | Incar | More than 90% with Incar: Rxlev >-87 dBm | 98,11% | OK | 98,48% | OK | 98,06% | OK | 2
 | Outdoor | More than 90% with Outdoor: Rxlev >-92 dBm | 99,97% | OK | 99,73% | OK | 99,62% | OK | 1
 | Indoor | More than 90% with Outdoor: Rxlev >-74 dBm | 91,02% | OK | 88,82% | NOK | 86,16% | NOK | 1
3G Coverage Rate | Incar,Indoor,Outdoor | More than 90% with RSCP <-85 dBm | 94,09% | OK | 88,98% | NOK | 86,69% | NOK | 1
4G Coverage Rate | Incar | More than 90% with RSRP <-90 dBm* | 90,75% | OK | 91,91% | OK | 78,56% | NOK | 2
 | Outdoor | More than 90% with RSRP <-95 dBm* | 97,32% | OK | 99,36% | OK | 93,38% | OK | 2
 | Indoor | More than 90% with RSRP <-78 dBm* | 58,04% | NOK | 59,69% | NOK | 64,80% | NOK | 3
updated

## Slide 23: Benchmarking Key Results – 2G/3G voice and SMS Summary MTN is leading in accessibility and retainability in LOKOSSA, MTN is ranked second in terms of voice quality MOS but satisfys ARCEP requirements, MTN needs to improve its SMS Send duration, All operators failed to meet ARCEP requirements for SMS service due to due to the timeout of sending duration that should be less than (< 6s).
KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  | Value | Conformity | Value | Conformity | Value | Conformity | 
Accesibility: Blocking rate | <1% | 0,58% | OK | 0,86% | OK | 0,84 | OK | 1
Retainability: Call drop rate | <1% | 0,38% | OK | 0,55% | OK | 0,78% | OK | 1
Call Completetion Rate (%) | =<98% | 99,04% | OK | 98,56% | OK | 98,38% | OK | 1
Integrity: Voice quality | Note requise> 2,8 | 4,02 | OK | 4,21 | OK | 3,94 | OK | 2
SMS sending success rate % (E2E delivery Time<6 sec) | >99% | 97,51% | NOK | 91,80% | NOK | 98,89% | NOK | 2
SMS receving success rate % | >99% | 96,33% | NOK | 89,01% | NOK | 96,46% | NOK | 2
updated

## Slide 24: Benchmarking Key Results – 3G Data Summary MTN network in 3G DATA meets ARCEP requirements, MTN has the lowest FTP DL/UL throughput.
Services | KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
3G HTTP | Successful internet connexion rate | >96% | 100,00% | OK | 99,92% | OK | 100,00% | OK | 1
 | Connexion setup time | <=10sec | 6,09 | OK | 6,12 | OK | 5,87 | OK | 2
 | Web service failure rate | <3% | 2,42% | OK | 0,45% | OK | 1,89% | OK | 3
3G FTP | FTP failure rate UL/DL | <3 % | 0,85%/1,77% | OK | 0,43%/4,98% | OK/NOK | 0%/1,23% | OK | 2
 | FTP Data transmission average (DL) | >= 2Mbps | 3,482 | OK | 4,651 | OK | 7,631 | OK | 3
 | FTP Data transmission average (UL) | >= 1Mbps | 1,156 | OK | 1,272 | OK | 1,986 | OK | 3
updated

## Slide 25: Benchmarking Key Results – 4G Data Summary MTN’s 4G DATA End User KPIs satisfy extensively ARCEP requirements, MTN is ranked first in terms of FTP DL/UL throughput, MTN has an excellent FTP DL throughput with 57,41Mbps against 27,51Mbps for MOOV and 12,93Mbps for CELTISS.
Services | KPI | Threshorlds* | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
4G HTTP Browsing | Web service failure rate (%) | <3% | 0,00% | OK | 0,00% | OK | 0,00% | OK | 1
 | Connexion setup time | <=3sec | 0,47 | OK | 0,58 | OK | 0,62 | OK | 1
4G FTP | FTP failure rate UL/DL | <3 % | 0%/0,87% | OK | 0%/0,47% | OK | 0%/0% | OK | 3
 | FTP Data transmission average (DL) | 4G >= 5 Mbps | 57,419 | OK | 27,516 | OK | 12,933 | OK | 1
 | FTP Data transmission average (UL) | 4G: >= 2Mbps | 18,741 | OK | 13,537 | OK | 11,474 | OK | 1
updated

## Slide 26
Benchmarking 2G/3G/4G coverage
04

## Slide 27: Benchmarking: 2G coverage Only MTN’s 3G coverage meets ARCEP RxLev thresholds for all morphologies Indoor, Incar and outdoor, MTN has the best 2G coverage for Indoor and outdoor categories and closely simular to competitors for Incar category.
Chart: 2G RxLev Distribution (%)
| Indoor>-74 | Incar >-87 | Outdoor >-92
MTN | 0.9102 | 0.9811 | 0.9997
MOOV | 0.8882 | 0.9848 | 0.9973
CELTISS | 0.8616 | 0.9806 | 0.9962
updated

## Slide 28: Benchmarking: 2G coverage - Maps In LOKOSSA, MTN has 91,02% of samples better than -74dBm against 88,82% for MOOV and 86,16% for CELTISS.
updated

## Slide 29: Benchmarking: 3G coverage In LOKOSSA, MTN is clair leader in terms of 3G coverage and alone satisfys the ARCEP requirements.
Chart: 3G RSCP Distribution (%)
| Indoor,Incar,Outdoor >-85
MTN | 0.9409
MOOV | 0.8898
CELTISS | 0.8669
updated

## Slide 30: Benchmarking: 3G coverage-Maps In LOKOSSA, MTS offers the best 3G coverage.
updated

## Slide 31: Benchmarking: 4G coverage MTN is ranked second for 4G coverage for Incar and Outdoor morphologies and meets ARCEP requirements, but all operators failed to meet ARCEP threshold for Indoor category.
Chart: 4G RSRP Distribution (%)
| Indoor > -78 | Incar > -90 | Outdoor > -95
MTN | 0.5804 | 0.9075 | 0.9732
MOOV | 0.5969 | 0.9191 | 0.9936
CELTISS | 0.648 | 0.7856 | 0.9338
updated

## Slide 32: Benchmarking – 4G coverage - Maps MTN’s 4G coverage is lower than MOOV’s and CELTISS, Low 4G coverage was recorded near to the road to Doukonta.
updated

## Slide 33
Benchmarking voice service
04

## Slide 34: Benchmarking: CS Accessibility 2G/3G BLOCKED CALLS MTN has the best accessibility to voice service compared to competitors, All operators satisfy ARCEP requirements.
Chart: Call Blocked Rate (%)
| CBR (%)
MTN | 0.0058
MOOV | 0.0086
CELTISS | 0.0084
Chart: Call Blocked Rate per Technology (%)
| CBR (%)
MTN 2G | 0
MTN 3G | 0.006
MOOV 2G | 0
MOOV 3G | 0.0187
CELTISS 2G | 0.0125
CELTISS 3G | 0.0078
Updated

## Slide 35: Benchmarking: CS Integrity Voice quality Mean Opinion Score In LOKOSSA, MTN has the best ratio of excellent and good Voice Quality samples compared to CELTISS’s and MOOV’S. MTN is ranked second in terms of voice quality with an average MOS equal to 4,02 opposed to 4,21 for MOOV and 3,94 for CELTISS.
Chart: Average MOS
| Avrege MOS
MTN | 4.02
MOOV | 4.21
CELTISS | 3.94
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Excellent+Good
MTN | 0.7724 | 0.2252 | 0.0024 | 0 | 0.9976
MOOV | 0.8918 | 0.092 | 0.0068 | 0.0094 | 0.9838
CELTISS | 0.5947 | 0.3959 | 0.0068 | 0.0026 | 0.9906
updated

## Slide 36: Benchmarking – CS Integrity Voice quality maps (MOS) MTN has around 99,76% of MOS samples better than 2.8 against 98,38% for MOOV and 99,1% for CELTISS. 3d
updated

## Slide 37: Benchmarking: CS Retainability 2G/3G DROPPED CALLS MTN is clair leader in term of retainability by having the lowest Call Drop Rate, All operators meets ARCEP requirements.
Chart: Call Drop Rate (%)
| CDR (%)
MTN | 0.0038
MOOV | 0.0055
CELTISS | 0.0078
updated

## Slide 38: Benchmarking Voice service Band usage(%) All operators have more than 97% of voice calls carried out over 3G, All operators use mainly UMTS2100 band.
Chart: System Technology usage(%)
| GSM | UMTS
MTN | 0.0012 | 0.9988
MOOV | 0.0006 | 0.9994
CELTISS | 0.0272 | 0.9728
Chart: 2G Band usage(%)
| GSM 900 | GSM 1800
MTN | 1 | 0
MOOV | 0.3333 | 0.6667
CELTISS | 0.7952 | 0.2048
Chart: 3G Band usage(%)
| UMTS 900 | UMTS 2100
MTN | 0.2217 | 0.7783
MOOV | 0.2635 | 0.7365
CELTISS | 0.249 | 0.751
updated

## Slide 39: Benchmarking: Radio parameters EC/NO comparison 7,42% of drive test samples are showing a very low level of EcNo for 3G MTN opposed to MOOV with 4,63% and CELTISS with 4,88%.
Chart: 3G Ec/No Distribution (%)
| -8 to 0 | -12 to -8 | -16 to -12 | -34 to -16 | ACCEPTABLE EC/N0
MTN | 0.3515 | 0.2387 | 0.3356 | 0.0742 | 0.5902
MOOV | 0.184 | 0.3694 | 0.4004 | 0.0463 | 0.5534
CELTISS | 0.6805 | 0.1969 | 0.0737 | 0.0488 | 0.8774
updated

## Slide 40: Benchmarking: Radio parameters EC/NO MTN has the highest ratio of very bad Ec/No samples (<-16db).
updated

## Slide 41: Benchmarking – 2G/3G CALL SETUP TIME MTN is clear leader in terms of Call Setup Time.
Chart: Call Setup Time (s)
| Call Setup Time
MTN | 5.66
MOOV | 7.14
CELTISS | 7.21
Updated
Chart: CS Call setup Time by technology (s)
| 4G CSFB CST | 3G CST | 2G CST
MTN | 5.01 | 5.85 | 4.41
MOOV | 7.98 | 7.22
CELTISS | 7.8 | 7.43 | 8.15

## Slide 42: Benchmarking – SMS Service MTN’s SMS SEND/RECEIVE SR(%) is better than MOOV and less than CELTISS . SMS service KPIs for all operators are not compliant with the ARCEP requirements due to the timeout of sending duration (< 6s).
Chart: SMS Send/Received SR(%)
| SMS Sending message success rate (%) | SMS Receving message success rate (%)
MTN | 0.9751 | 0.9633
MOOV | 0.918 | 0.8901
CELTISS | 0.9889 | 0.9646
Chart: SMS Send Time(%)
| (0,3) | (3,6) | >6
MTN | 0.6581 | 0.317 | 0.0249
MOOV | 0.6133 | 0.3047 | 0.082
CELTISS | 0.6453 | 0.3436 | 0.0111
Updated

## Slide 43
Benchmarking Data service
04

## Slide 44: Benchmarking – DATA 3G All operators have a good rate of successful Internet connection.
Chart: PS Attach & PDP Contex Act(%)
| PS Attach success(%) | PDP Context Act Success (%)
MTN | 1 | 0.9905
MOOV | 0.9992 | 0.9898
CELTISS | 1 | 0.9733
Chart: Attach & PDP Activation Time (s)
| PS Attach Setup Time | PDP Context Act Time
MTN | 0.94 | 1.45
MOOV | 1.01 | 1.12
CELTISS | 1.17 | 1.89
Updated

## Slide 45: Benchmarking – DATA 3G Web Browsing service MTN has the lowest HTTP browsing success, All operators meet ARCEP requirement for web service.
Chart: PS Connection setup time (sec)
| PS Connection setup time
MTN | 6.09
MOOV | 6.12
CELTISS | 5.87
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 0.9756
MOOV | 0.9955
CELTISS | 0.9811
Updated

## Slide 46: Benchmarking – DATA 3G FTP service Only MTN and CELTISS meet ARCEP requirements for FTP DL/UL success ratio. CELTISS has the best FTP DL/UL success ratio.
Chart: 3G FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9915 | 0.9823
MOOV | 0.9957 | 0.9502
CELTISS | 1 | 0.9877
Updated

## Slide 47: Benchmarking – 3G FTP MEAN THROUGHPUT MTN 3G Throughput DL/UL is less than MOOV’s and CELTISS’s, but satisfys ARCEP requirements.
Chart: 3G FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 3482.24 | 1156.47 | 21421.47 | 16221.4
MOOV | 4651.89 | 1272.73 | 19541.24 | 17456.07
CELTISS | 7631.54 | 1986.65 | 18172.09 | 8225.22

## Slide 48: Benchmarking – 3G FTP MEAN THROUGHPUT comparison map All operators meets ARCEP requirements with 100% of throughput samples better than 2Mbps.
Updated

## Slide 49: Benchmarking – 4G HTTP Browsing All operators have very good HTTP Browsing success rate.
Chart: 4G HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 1
MOOV | 1
CELTISS | 1
Updated

## Slide 50: Benchmarking – 4G FTP service All operators have an excellent FTP DL/UL success ratio for 4G network.
Chart: 4G FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 1 | 0.9913
MOOV | 1 | 0.9953
CELTISS | 1 | 1
Updated

## Slide 51: Benchmarking – 4G FTP THROUGHPUT comparison In LOKOSSA, MTN is leading in terms of FTP DL/UL AVERAGE Throughput, MTN has outperformed its competitors with an excellent DL/UL speed.
Chart: 4G FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 57419.807 | 18741.88 | 192208.11 | 39935.56
MOOV | 27516.67 | 13537.6 | 199029.09 | 25547.6
CELTISS | 12933.84 | 11474.41 | 25800.11 | 14517.41
Updated

## Slide 52: Benchmarking – 4G FTP THROUGHPUT comparison map In LOKOSSA, MTN has an excellent end user throughput with more than 46,13% of samples better than 30Mbps .
Updated

## Slide 53: Benchmarking – BAND and TECHNOLOGY UTILISATION Most of MTN’s and MOOV’s LTE samples are carried out over LTE 2600 as first carrier, Most of CELTISS’s samples are carried out over LTE 1800 as first carrier, For all operators,most of 3G samples are carried out over U2100, but MTN has the highest ratio of U900 usage.
Chart: 3G Band Distribution(%)
| UMTS 900 | UMTS 2100
MTN | 0.1053 | 0.8947
MOOV | 0.0653 | 0.9347
CELTISS | 0.0778 | 0.9222
Chart: 4G Band Distribution (%)
| LTE 800 | LTE 700 | LTE 1800 | LTE 2100 | LTE 2600
MTN | 0.0134 | 0.0111 | 0.0246 | 0 | 0.951
MOOV | 0.3405 | 0 | 0.0239 | 0 | 0.6356
CELTISS | 0.3933 | 0 | 0.6067 | 0 | 0
Updated

## Slide 54: Benchmarking – Data TECHNOLOGY Usage(%) MTN has the highest LTE CA Carrier Aggregation usage with 83,12% against 52,89% for MOOV and 50,75% for CELTISS.
Chart: 3G Packet Technology usage (%)
| DC-HSPA | HSPA | HSDPA | UMTS
MTN | 0.5165 | 0.0527 | 0.0004 | 0.4304
MOOV | 0.5498 | 0.0116 | 0.0111 | 0.4275
CELTISS | 0.374 | 0.0624 | 0.0177 | 0.5458
Chart: 4G Packet Technology usage (%)
| LTE | LTE CA
MTN | 0.1688 | 0.8312
MOOV | 0.4711 | 0.5289
CELTISS | 0.4925 | 0.5075
Updated

## Slide 55: Benchmarking – SINR comparison For 4G Network Drive tests are showing that MTN has the best ratio of acceptable SINR.
Chart: 4G SINR Comparison
| (Min,-4) | (-4,0) | (0,7) | (7,15 <) | ACCEPTABLE SINR
MTN | 0.0073 | 0.0362 | 0.242 | 0.7145 | 0.9565
MOOV | 0.0099 | 0.0512 | 0.3749 | 0.564 | 0.9389
CELTISS | 0.0168 | 0.0316 | 0.1012 | 0.8504 | 0.9516
Updated

## Slide 56: Benchmarking – SNIR comparison map MTN has the better quality of signal compared to MOOV and CELTISS.

## Slide 57
Next steps
05

## Slide 58: Next steps
Complete 2G & 3G drive tests: Remaining areas (north area of Benin)
Conduct deep analysis on drive tests results
Complete cross analysis on KPIs and OSS parameters with drive tests results and call traces
Issue final report and recommendations

## Slide 59
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2019 Deloitte Bénin SARL. Société du réseau Deloitte