## Slide 1
Network QoS
Draft final report (Benchmarking part)
February 6th, 2019

## Slide 2: Summary
Scope of Work | 03
Executive Summary | 06
Benchmarking | 10
QoS Ranking | 33
QoE Global Scoring and Ranking | 56

## Slide 3
Scope of Work
01

## Slide 4: Scope of Work (i/ii): a high level of analysed samples giving a good accuracy
Cost
Cities to be covered
Cities | Proposed Samples |  |  | 
 | Voice 2G/3G | SMS | Data 3G | Data 4G
Cotonou | 1000 | 500 | 500 | 300
Sèmè-Kpodji | 400 | 200 | 200 | -
Porto-Novo | 600 | 300 | 300 | 200
Calavi | 800 | 400 | 400 | 200
Ouidah | 400 | 200 | 200 | -
Lokossa | 400 | 200 | 200 | -
Bohicon | 400 | 200 | 200 | -
Parakou | 600 | 300 | 300 | -
Djougou | 600 | 300 | 300 | -
Natitingou | 400 | 200 | 200 | -
Allada | 400 | 200 | 200 | -
Highways | - | - | - | -
Realized Samples |  |  | 
Voice 2G/3G | SMS | Data 3G (FT DL) | Data 4G
1006 | 3525 | 1910 | 840
401 | 1356 | 697 | -
604 | 1973 | 1073 | 288
814 | 2263 | 1104 | 532
429 | 283 | 379 | -
451 | 531 | 270 | -
413 | 1210 | 532 | -
622 | 1484 | 687 | -
600 | 997 | 466 | -
421 | 593 | 270 | -
415 | 666 | 263 | -
688 | 2389 | 1236 | -

## Slide 5: Scope of Work (ii/ii)
Cost
Drive Test KPI (ARCEP KPIs)
Data KPIs (3G/LTE)
HTTP service Failure Ratio
HTTP Session Setup time
FTP UL/DL Session Failure Rate
FTP UL/DL Throughput
3G Availability Rate
Successful Internet Connexion Rate
Coverage rate (2G/3G/LTE)
Incar coverage rate
Voice KPIs
Call blocking rate
Call drop rate
Call completetion, with perfect quality, rate (MOS)
SMS
MO SMS delivery success rate
MT SMS delivery success rate

## Slide 6
Executive Summary
02

## Slide 7: Executive Summary – Benchmarking (i/iii) MTN and MOOV Networks QoS are comparable. A resource optimization enables to meet ARCEP requirements and to outperform competition’s NW QoS
2G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Coverage :
MTN coverage rate (91,22%) is slightly lower than MOOV (94,87%)
Both operators meets ARCEP 2G coverage obligation (90%).
Voice service :
Accessibility (CSSR): MTN is better than MOOV (95,1% vs 91%).
Both operators failed to meet ARCEP requirement (98%).
Retainability (Call Drop): MTN is better than MOOV (2,6% vs 3,5%).
Both operators failed to meet ARCEP oblogation (2%).
Integrity (Voice Quality): MTN is much better than MOOV (MOS 95,1% vs 91%).
MTN reach ARCEP requirement (95%), whereas it’s not the case for MOOV.
SMS service :
MTN is better than MOOV.
MTN reach SMS ARCEP obligation.
Design optimization is needed to improve 2G MTN coverage. Especially for the highways (Sites expansion, Repeaters, Swap to feeder less, power increase...)
Actions to improve accessibility are proposed in OSS analysis Chapter.

## Slide 8: Executive Summary - Benchmarking (ii/iii) MTN network QoS is globally better than the MOOV’s. A design optimization can enable a better network QoS on all KPIs
3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Coverage :
3G MTN coverage rate (73,91%) is better than MOOV (70,52%)
Both operators fail to reach ARCEP 3G coverage obligation (90%).
3G connexion service :
Accessibility: Both operators reach the ARCEP obligation
MTN 3G connexion time is better than MOOV (2,96s vs 4s).
Both operators reach the ARCEP integrity obligation
SMS service :
MTN is better than MOOV (Better SMS sending Succes rate).
Both operators meets ARCEP 3G coverage obligation.
Data service :
MTN is providing better throughput (DL:2,98M/UL:1,23M) than MOOV (DL:2,62M/UL:1,06M).
Both operators meets ARCEP 3G throughput obligations.
RF optimization (Physical and logical) is needed to improve 3G MTN coverage.
An Optimization session is needed for MTN, in order to improve the Ec/No (very important key for 3G QoS )
Actions to improve accessibility are presented in OSS analysis chapter

## Slide 9: Executive Summary - Benchmarking (iii/iii) MOOV 4G network coverage rate is better than that the one of MTN. MTN network mean throughput is better than MOOV's. A Radio extension of the MTN network will enable outperforming competition’s 4G coverage and capacity
4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Coverage :
4G MTN coverage rate (74,59%) is lower than MOOV (83,72%)
ARCEP obligations are not available
Data service :
MTN is providing better 4G throughput (DL: 14.59M / UL: 6.31M) than MOOV (DL: 10.91M / UL: 6,89M).
ARCEP obligations are not available
It is highly recommended to extend 4G sites in order to have a continuous 4G coverage, and improve customer experience and consolidate MTN position

## Slide 10
Benchmarking
03

## Slide 11: Benchmarking – 2G MTN 2G Coverage is globaly good except Ouidah, Allada and some portions of the major raods. MOOV 2G coverage is better than MTN in the majority of tested areas
MTN meet the target set by the ARCEP in all cities except Allada, Djougou and Ouidah whereas MOOV reached ARCEP taget in all tested cities.
Both operators failed to meet the target in the major roads.
Both operators reached the ARCEP target in the network level.
The size of the bubble indicates the importance of the area
Chart: 2G COVERAGE
| Cotonou | Sèmè-Kpodji | Porto-Novo | Calavi | Ouidah | Lokossa | Bohicon | Parakou | Djougou | Natitingou | Allada | Major roads | Network
MTN | 98.2 | 89.4 | 91.5 | 98.5 | 85.2 | 96.5 | 90.5 | 94.1 | 89.9 | 91 | 71 | 78.5 | 91.22
MOOV | 99.5 | 89.2 | 96.5 | 98.4 | 96.1 | 96.1 | 93.2 | 98.9 | 89 | 99.7 | 99.2 | 84.8 | 94.87
Chart: Best Network
| #Regions
MTN | 4
MOOV | 8

## Slide 12: Benchmarking – 3G COVERAGE The MTN 3G coverage is better than Moov for almost all tested areas. However, improvements are highly needed in 6 cities and the major roads
Both operators failed to reach the target set by ARCEP concerning the 3G coverage.
MTN meet the target only in 5 areas (from the 12 tested areas) whereas MOOV meet the target only in two areas.
Chart: 3G COVERAGE
| Cotonou | Sèmè-Kpodji | Porto-Novo | Calavi | Ouidah | Lokossa | Bohicon | Parakou | Djougou | Natitingou | Allada | Major roads | Network
MTN | 97.9 | 80.3 | 87.1 | 90.7 | 60.9 | 85.6 | 90.5 | 94.7 | 79 | 92.5 | 62.7 | 49.5 | 73.91
MOOV | 94.9 | 52.3 | 60.3 | 77.7 | 59.3 | 89.6 | 84.3 | 98.2 | 67.8 | 75.1 | 67.1 | 48.6 | 70.52
Chart: Best Network
| #Regions
MTN | 9
MOOV | 3
The size of the bubble indicates the importance of the area

## Slide 13: Benchmarking – 4G COVERAGE MOOV 4G coverage is better than MTN in all the tested cities
No ARCEP Thresholds Available, Proposed target: 90% with RSRP >-105 dBm
4G Moov coverage is better than MTN in all regions
Chart: 4G COVERAGE
| Cotonou | Sèmè-Kpodji | Porto-Novo | Network
MTN | 82.5 | 49.6 | 81 | 74.6
MOOV | 94.1 | 50.6 | 93.1 | 83.7
The size of the bubble indicates the importance of the area
Chart: BEST Network
| #Regions
MTN | 3
MOOV | 0

## Slide 14: Benchmarking – Accessibilty The accessibility in MTN network is better than in MOOV but it is lower than the ARCEP requirement
Chart: Best Network
 | 0
MTN | 11
MOOV | 0
CELTISS | 1
The call blocking in MTN network is better than in MOOV but it is globally high (4.9%).
The quality in the major roads is highly affecting the network level.
Both operators, MTN & MOOV, didn’t meet ARCEP requirements.
Chart: Call Blocking
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 1.03 | 1.63 | 0.64 | 0.82 | 0.24 | 0.58 | 0.53 | 0.29 | 2.7 | 1.06 | 0.61 | 5.88 | 1.35
MOOV | 1.62 | 2.05 | 1.99 | 0.94 | 0.27 | 0.86 | 2.11 | 0.63 | 2.02 | 2.97 | 1.29 | 7.64 | 1.94
CELTISS | 1.77 | 1.72 | 0.8 | 0.91 | 0.32 | 0.84 | 0.36 | 0.31 | 0.97 | 4.25 | 1.17 | 9.58 | 1.89
ARCEP Target | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 15: Benchmarking – Retainability The call retainability in MTN network is globally better than in MOOV but this KPI is lower than the ARCEP requirement
Chart: #Regions
| Ranked 1
MTN | 7
MOOV | 4
CELTISS | 1
The MTN call drop rate in is globally better than MOOV but is moderately high (2.6%) and didn’t meet ARCEP requirements.
The high call drop rate in the major roads is highly affecting the network level
Chart: Call DROP
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 0.46 | 0.23 | 0.6 | 0.31 | 1.15 | 0.38 | 1.37 | 0.46 | 0.44 | 0.4 | 0.71 | 6 | 0.93
MOOV | 1.62 | 1.66 | 2.48 | 1.03 | 2.44 | 0.55 | 1.57 | 0.23 | 2.96 | 1.71 | 0.84 | 10.32 | 2.19
CELTISS | 1.77 | 0.24 | 1.11 | 0.15 | 0 | 0.78 | 0 | 0.37 | 0.95 | 1.28 | 0.41 | 9.56 | 1.34
ARCEP Target | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 16: Benchmarking – Voice Quality MTN is offering voice quality much better than Moov and it reached the ARCEP target in all areas except Porto-novo and major roads.
Chart: BEST NETWORK
| #Regions
MTN | 2
MOOV | 9
CELTISS | 1
Voice Quality (with MOS > 2,8)
Chart: VOICE QUALITY
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 3.66 | 3.7 | 3.8 | 3.73 | 3.85 | 4.02 | 3.78 | 3.98 | 3.87 | 4.03 | 3.79 | 3.79 | 3.81
MOOV | 3.85 | 3.92 | 3.83 | 3.87 | 4.01 | 4.21 | 4.02 | 3.63 | 4.09 | 3.73 | 3.95 | 3.95 | 4.03
CELTISS | 3.94 | 3.85 | 3.79 | 3.85 | 3.94 | 3.94 | 3.86 | 3.85 | 3.91 | 3.93 | 3.91 | 3.91 | 3.9
ARCEP Target | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8

## Slide 17: Benchmarking – SMS Sending/Receiving Success Rate MTN meet the ARCEP target in all tested areas and outperform Moov in sending/receiving SMS.
Chart: SMS Sending Success
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 99.23 | 99.71 | 99.58 | 99.23 | 100 | 99.81 | 99.66 | 99.12 | 99.4 | 98.99 | 100 | 99.08 | 99.13
MOOV | 98.32 | 97.95 | 98.79 | 98.32 | 97 | 98.02 | 98.2 | 99.8 | 98.5 | 76.46 | 97.88 | 97.76 | 97.66
ARCEP Target | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99
Chart: SMS Receiving Success
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 99.7 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
MOOV | 98.4 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 99.9
ARCEP Target | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99
Chart: Best Network
| #Regions
MTN | 12
MOOV | 0
Chart: Best Network
| #Regions
MTN | 11
MOOV | 1

## Slide 18: Benchmarking – 3G Availability Rate Both operators meet the ARCEP requirements for 3G availability
MTN reach the ARCEP target in all tested areas whereas MOOV didnt reach the target in Natitingou.
Chart: 3G Availability
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 98.9 | 99.5 | 99.4 | 99.3 | 99.3 | 99.6 | 99.3 | 99.3 | 98.2 | 98.5 | 99.7 | 98.54 | 99.14
MOOV | 99.7 | 99.7 | 99.9 | 98.7 | 99.9 | 100 | 99.9 | 99.5 | 99.9 | 88.2 | 99.5 | 95.73 | 99.16
ARCEP Target | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95
Chart: Best Network
| #Regions
MTN | 4
MOOV | 8

## Slide 19: Benchmarking – 3G/4G HTTP Connexion Setup Time Both operators meet the ARCEP target in all tested areas.
Chart: 3G HTTP Connexion Setup Time
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 2.12 | 2.36 | 2.31 | 2.28 | 3.06 | 3 | 2.54 | 2.8 | 3.22 | 3.9 | 3.37 | 4.66 | 2.96
MOOV | 5.07 | 4.6 | 2.51 | 4.47 | 2.92 | 2.76 | 4.9 | 4.89 | 3.25 | 4.47 | 3.5 | 4.74 | 4
ARCEP Target | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30
Chart: BEST Network
| #Regions
MTN | 10
MOOV | 2

## Slide 20: Benchmarking – 3G Internet Connexion/Web Service Success Rate Both operators meet the ARCEP target in all tested areas.
Chart: 3G Internet Connexion SuccesS
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 98.8 | 99.1 | 99 | 99.3 | 99.3 | 99.3 | 99.5 | 98.6 | 99.3 | 98.3 | 99.6 | 98.93 | 99.05
MOOV | 99.2 | 99.3 | 99.6 | 99 | 98.7 | 99.9 | 99.4 | 99.2 | 99.8 | 93.9 | 99.8 | 98.53 | 99.19
ARCEP Target | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90
Chart: Best Network
| #Regions
MTN | 5
MOOV | 6
Chart: 3G Web Service SUCCESS
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 98.51 | 99.8 | 99.88 | 99.94 | 99.15 | 99.9 | 99.91 | 99.77 | 98.97 | 100 | 98.8 | 97.11 | 99.17
MOOV | 99.34 | 98.14 | 99.28 | 98.48 | 99.07 | 99.18 | 96.84 | 97.39 | 94.53 | 98.63 | 99.61 | 68.24 | 95.58
ARCEP Target | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90
Chart: Best Network
| #Regions
MTN | 10
MOOV | 2

## Slide 21: Benchmarking – 3G FTP UL/DL Service Success Rate Both operators meet the ARCEP target in all tested areas.
Chart: Best Network
| #Regions
MTN | 3
MOOV | 9
Chart: Best Network
| #Regions
MTN | 9
MOOV | 3
Chart: 3G FTP UL SUCCESS
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 84.1 | 98.98 | 99.63 | 98.82 | 99.47 | 98.51 | 99.43 | 99.27 | 99.36 | 99.62 | 97.68 | 97.44 | 95.91
MOOV | 83.3 | 99.37 | 99.18 | 95.5 | 99.65 | 96.23 | 98.14 | 96.8 | 97.61 | 97.34 | 99.21 | 93.99 | 94.41
ARCEP Target | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80 | 80
Chart: 3G FTP DL SUCCESS
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 99.21 | 96.27 | 96.74 | 97.64 | 97.89 | 97.78 | 99.44 | 98.84 | 99.14 | 98.15 | 98.48 | 98.22 | 98.53
MOOV | 99.01 | 99.12 | 99.06 | 98.59 | 99.31 | 99.53 | 99.38 | 97.98 | 99.21 | 98.41 | 99.3 | 97.91 | 99.18
ARCEP Target | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90

## Slide 22: Benchmarking – 3G FTP UL/DL throughput Both operators meet the ARCEP target in all tested areas. MTN is offering best 3G throughput.
Chart: Best Network
| #Regions
MTN | 10
MOOV | 2
Chart: Best Network
| #Regions
MTN | 8
MOOV | 4
Chart: 3G FTP DL THROUGHPUT
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 3534.5 | 2572.9 | 3303.7 | 3117.5 | 2795.5 | 3367.7 | 3208.6 | 2960.8 | 3090.6 | 3480.1 | 3103.7 | 2220 | 2984.6
MOOV | 2534 | 2439.1 | 2255.4 | 2357.3 | 2658.6 | 2745 | 2496.1 | 2958.6 | 4931.4 | 3986.5 | 3544.7 | 2650.4 | 2618.8
ARCEP Target | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000
Chart: 3G FTP UL THROUGHPUT
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 1449.17 | 1332.02 | 1228.63 | 1440.21 | 1514.34 | 1288.84 | 956.43 | 1186.81 | 1023.43 | 849.61 | 860.07 | 1072.33 | 1232.7
MOOV | 1261.01 | 1232.06 | 1277.67 | 1275.42 | 582.31 | 1102.08 | 702.15 | 1087.76 | 1076.73 | 833.67 | 803.55 | 807.22 | 1067.8
ARCEP Target | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000

## Slide 23: Benchmarking – 4G Connexion Service Setup Both operators meet the proposed ARCEP target in all tested areas. 4G HTTP connexion setup is faster in MTN network.
Chart: Best Network
| #Regions
MTN | 1
MOOV | 2
Chart: Best Network
| #Regions
MTN | 3
MOOV | 0
Chart: 4G Web Service SUCCESS
| COTONOU | PORTO NOVO | CALAVI | ALL NETWORK
MTN | 99.645 | 94.55 | 98.66 | 98.57
MOOV | 99.641 | 99.1 | 99.66 | 99.65
ARCEP Target | 90 | 90 | 90 | 90
Chart: 4G HTTP Connexion Setup Time
| COTONOU | PORTO NOVO | CALAVI | ALL NETWORK
MTN | 2.3 | 3.13 | 2.36 | 2.6
MOOV | 3.4 | 3.28 | 3.72 | 3.47
ARCEP Target | 10 | 10 | 10 | 10

## Slide 24: Benchmarking – 4G FTP UL/DL Service Success Rate Both operators didn’t meet the ARCEP target for 4G FTP UL success rate.
Chart: Best Network
| #Regions
MTN | 0
MOOV | 3
Chart: Best Network
| #Regions
MTN | 2
MOOV | 1
Chart: 4G FTP UL SUCCESS
| COTONOU | PORTO NOVO | CALAVI | ALL NETWORK
MTN | 84.1 | 98.98 | 99.63 | 98.82
MOOV | 83.3 | 99.37 | 99.18 | 95.5
ARCEP Target | 90 | 90 | 90 | 90
Chart: 4G FTP DL SUCCESS
| COTONOU | PORTO NOVO | CALAVI | ALL NETWORK
MTN | 97.59 | 93.07 | 93.35 | 97.14
MOOV | 98.98 | 97.14 | 97.9 | 99.21
ARCEP Target | 90 | 90 | 90 | 90

## Slide 25: Benchmarking – 4G FTP UL/DL throughput The 4G throughput of the both operators is almost comparable.
Chart: Best Network
| #Regions
MTN | 2
MOOV | 1
Chart: Best Network
| #Regions
MTN | 1
MOOV | 2
Chart: 4G FTP UL THROUGHPUT
| COTONOU | PORTO NOVO | CALAVI | ALL NETWORK
MTN | 5067.69 | 6793.48 | 9661.76 | 6313.38
MOOV | 6385.15 | 5441.42 | 10287.23 | 6894.59
ARCEP Target | 4000 | 4000 | 4000 | 4000
Chart: 4G FTP DL THROUGHPUT
| COTONOU | PORTO NOVO | CALAVI | ALL NETWORK
MTN | 13540.01 | 13365.99 | 17523.81 | 14587.94
MOOV | 9374.5 | 16473.61 | 10656.57 | 10915.36
ARCEP Target | 10000 | 10000 | 10000 | 10000

## Slide 26
QoE Global Scoring and Ranking
04

## Slide 27: QoE Scoring and Ranking based on Deloitte proposed weights
Category | Technology | Weight | KPI Item | Lower | Upper |  |  |  | 
 |  |  |  |  |  | KPI Value | KPI Value | Score | Score
PS Experience | 4G | 10 | Coverage (RSCP>=-105 dbm) | 80% | 100% | 74.6% | 83.7% | 0.00 | 1.85
 | 3G | 20 | Coverage (RSCP>=-94 dbm) | 85% | 100% | 73.9% | 70.52% | 0 | 0
 | 4G | 15 | Average FTP DL THP (kbps) | 5000 | 40000 | 14588 | 10915 | 7.85 | 6.17
 | 3G | 25 | Average FTP DL THP (kbps) | 2000 | 10000 | 3167 | 2615 | 9.55 | 6.93
 | 4G | 5 | Average FTP UL THP (kbps) | 2000 | 10000 | 6313 | 6895 | 3.67 | 3.91
 | 3G | 5 | Average FTP UL THP (kbps) | 1000 | 5000 | 1233 | 1068 | 1.21 | 0.65
 | 4G | 5 | Accessibility Rate (%) | 90% | 100% | 98.57% | 99.65% | 4.29 | 4.83
 | 3G | 5 | Accessibility Rate (%) | 90% | 100% | 99.17% | 95.58% | 4.59 | 2.79
 | 4G | 5 | Average HTTP Connexion Setup Time (s) | 1 | 3 | 3.47 | 2.60 | 0.00 | 2.24
 | 3G | 5 | Average HTTP Connexion Setup Time (s) | 2 | 5 | 2.96 | 4.00 | 4.12 | 2.89
 | 3G/4G | 100 | Total Score |  |  |  |  | 35.27 | 30.40
MTN is number 1 for mobile internet capacity through its 3G/4G Network

## Slide 28: QoE Scoring and Ranking based on Deloitte proposed weights
Category | Technology | Weight | KPI Item | Lower | Upper |  |  |  | 
 |  |  |  |  |  | KPI Value | KPI Value | Score | Score
CS Experience | 2G | 25 | Coverage (RxLev>=-87 dbm) | 90% | 100% | 91.22% | 94.87% | 3.05 | 12.18
 | 3G | 25 | Coverage (RSCP>=-94 dbm) | 85% | 100% | 73.91% | 70.52% | 0.00 | 0.00
 | 2G/3G | 15 | Call blocking rate | 90% | 100% | 98.57% | 99.65% | 12.86 | 14.48
 | 2G/3G | 15 | Call drop rate | 5% | 1% | 2.60% | 3.50% | 9.00 | 5.63
 | 2G/3G | 20 | Rate of MOS > 2.8 | 90% | 97% | 95.09% | 91.03% | 14.54 | 2.94
 | 2G/3G | 100 | Total Score |  |  |  |  | 39.45 | 35.22
MTN is number 1 for voice communication quality

## Slide 29
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2019 Deloitte Bénin SARL. Société du réseau Deloitte