## Slide 1
Network QoS
Benchmarking final report
February 6th, 2019

## Slide 2: Summary
Scope of Work | 03
Executive Summary | 06
Benchmarking | 12
QoS Ranking | 33
QoE Global Scoring and Ranking | 56

## Slide 3
Scope of Work
01

## Slide 4: Scope of Work (i/ii): a high level of analysed samples giving a good accuracy
Cost
Cities to be covered
Cities | Proposed Samples |  |  | 
 | Voice 2G/3G | SMS | Data 3G | Data 4G
Cotonou | 1000 | 500 | 500 | 300
Sèmè-Kpodji | 400 | 200 | 200 | -
Porto-Novo | 600 | 300 | 300 | 200
Calavi | 800 | 400 | 400 | 200
Ouidah | 400 | 200 | 200 | -
Lokossa | 400 | 200 | 200 | -
Bohicon | 400 | 200 | 200 | -
Parakou | 600 | 300 | 300 | -
Djougou | 600 | 300 | 300 | -
Natitingou | 400 | 200 | 200 | -
Allada | 400 | 200 | 200 | -
Highways | - | - | - | -
Realized Samples |  |  | 
Voice 2G/3G | SMS | Data 3G (FT DL) | Data 4G
1006 | 3525 | 1910 | 840
401 | 1356 | 697 | -
604 | 1973 | 1073 | 288
814 | 2263 | 1104 | 532
429 | 283 | 379 | -
451 | 531 | 270 | -
413 | 1210 | 532 | -
622 | 1484 | 687 | -
600 | 997 | 466 | -
421 | 593 | 270 | -
415 | 666 | 263 | -
688 | 2389 | 1236 | -

## Slide 5: Scope of Work (ii/ii)
Cost
Drive Test KPI (ARCEP KPIs)
Data KPIs (3G/LTE)
HTTP service Failure Ratio
HTTP Session Setup time
FTP UL/DL Session Failure Rate
FTP UL/DL Throughput
3G Availability Rate
Successful Internet Connexion Rate
Coverage rate (2G/3G/LTE)
Incar coverage rate
Voice KPIs
Call blocking rate
Call drop rate
Call completetion, with perfect quality, rate (MOS)
SMS
MO SMS delivery success rate
MT SMS delivery success rate

## Slide 6
Executive Summary
02

## Slide 7: Executive Summary – Benchmarking coverage 2G/3G/4G
Coverage 2G/3G/4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Design optimization is needed to improve 2G MTN coverage. Especially for the highways (Sites expansion, Repeaters, Swap to feeder less, power increase...)
Tune and align power settings mainly in 3G/4G. Actual setting may impact the coverage strength specially at Indoor locations
Review the design at the coverage and quality blackspots
We highlight that 4G ARCEP coverage Thresholds are aggressive
MTN is leading in terms of 2G Indoor coverage with 96,64% against 95,21% for MOOV and 95,46% for CELTISS,
MTN is in second position for Incar morphology and in third position for outdoor coverage but closely similar to competitors,
Only MTN meets ARCEP requirements for all morphologies in all regions except in roads,
MTN is leading in terms of 3G coverage rate with (94,60%) against (91,33%) for MOOV and (93,81%) for CELTISS,
MTN failed to meet ARCEP 3G coverage only in ALLADA and major roads,
MOOV is clear leader in terms of 4G coverage by having the first position in all morphologies,
MTN is in the second position in terms of 4G coverage rate for Incar and Outdoor morphologies but meets ARCEP thresholds,
All operators failed to satisfied the ARCEP threshold for indoor coverage for 4G network.

## Slide 8: Executive Summary – Benchmarking voice service 2G/3G
Voice service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Accessibility: MTN is leading in terms of accessibility to voice service by having the best Call Blocked ratio with 1,35% against 1,94% for MOOV and 1,89% for CELTISS,
All operators failed to meet ARCEP accessibility thresholds,
Retainability: MTN is ranked first in term of retainability better than MOOV and CELTISS,
MTN's Call Drop Rate is 0.93% compared to 2.19% for MOOV and 1.34% for CELTISS. Only MTN’s network satisfys ARCEP requirements in terms of retainability,
Integrity: MTN is in third position in terms of voice quality with an average Mean Opinion Score equal to 3,81 lower than MOOV 4,03 and better than CELTISS 3,9.
To improve its voice quality, it is recommended for MTN To:
  Reduce the utilization of 2G technology: Voice quality is always better in 3G due to its better codec rate (HD-voice with AMR-WB) , we recommend to push as much as possible the voice traffic to 3G,
  Improve radio parameters Ec/No, Drive test results are showing that MTN has a bad Ec/No, by improving this radio parameter we can improve further the voice quality MOS.
To improve the accessibility to voice service MTN needs to…………………………………
For update

## Slide 9: Executive Summary – Benchmarking SMS service
SMS service 2G/3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
MTN is ranked first in terms of SMS performance by having the best SMS send/Receive Success ratio,
All operators failed to meet ARCEP requirements for SMS Send Success with End To End Delivery Time who should be less than < 6 sec as defined by ARCEP.
There is no issue in radio accessibility that could be correlated to the SMS high delivery time.
End to End investigation need to be performed to analyses the high delivery time including mainly Core/SMS parts: SMSserver...

## Slide 10: Executive Summary – Benchmarking 4G Data service
Data service 4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 4G data service, and all operators meet ARCEP's requirements,
MTN is leading in terms of 4G DL throughput with 34.12 Mbps, better than MOOV 20.74Mbps and CELTISS 12.28Mbps,
MTN needs to improve its 4G End Users throughput in the followings regions: Cotonou, SEME KAPODJI, Porto Novo and CALAVI,
MTN is ranked first in terms of 4G UL throughput with 16.05Mbps, as opposed to 10.60Mbps for MOOV and 11.46Mbps for CELTISS,
MTN has the best 4G UL throughput in all regions,
For 4G network, all operators meet ARCEP End User Throughput obligation in download and upload.
MTN has an excellent performance in term of 4G KPIs.

## Slide 11: Executive Summary – Benchmarking 3G Data service
Data service 3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Performance is stable in terms of accessibility for 3G data service, and all operators meet ARCEP's requirements.
CELTISS is ranked first in terms of FTP DL/UL throughput,
MTN is in third position for 3G DL throughput with 3.56 Mbps, compared to 4.62 Mbps for MOOV and 7.29 Mbps for CELTISS,
MTN is ranked second in term of 3G UL throughput with 1.64 Mbps against 1.19 Mbps for MOOV and 2.02Mbps for CELTISS,
All operators meet ARCEP’s 3G End User Throughput obligation for download and upload,
All operators meet ARCEP’s web browsing service accessibility thresholds.
Increasing the utilization of HSPA-DC can improve 3G throughput,
Review RF Conditions by eliminating any poor EcNo region (cleaning any interference, RTWP…), Drive tests results are showing that MTN has a bad Ec/No distribution,
Review HSPA Carriers settings: number and used strategy, less handover between carriers will help overall user experience and get a higher throughput,
IuB / IuPS: whether it’s over IP or ATM; If the utilization is OK,
CE & Power Utilization: if there’s congestion, one option is to expand board,
Reduce INTER an IRAT Neighbors,
PDSCH Codes: number per cell. Maximize it to 15 per cell,
HSDPA Users: maximum number (configured),
Review HSDPA Scheduling Algorithm,
ACK/NACK Power Optimization: seeking to find NACK failure, acceptable values are about 10%,
HSPA+ Features : mainly 64QAMand Load Balancing (enabled),
Equipment and License: if there are available license on the NodeB,
Its recommended to push as much as possible the data traffic to 4G in order to Offload the 3G network.

## Slide 12
Benchmarking
03

## Slide 13: Benchmarking – 2G Coverage-Outdoor All operators has a simular 2G coverage and meet largily ARCEP requirements for outdoor morphology except in roads, MOOV is ranked first in terms of 2G outdoor coverage and slightly better than MTN and CELTISS.
Chart: 2G outdoor COVERAGE
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 99.98 | 99.99 | 100 | 100 | 99.4 | 99.97 | 99.87 | 100 | 99.58 | 99.97 | 99.84 | 87.7 | 99.64
MOOV | 99.99 | 99.97 | 100 | 100 | 99.63 | 99.73 | 100 | 100 | 99.98 | 99.59 | 100 | 91.34 | 99.75
CELTISS | 99.98 | 99.92 | 100 | 100 | 99.97 | 99.62 | 99.99 | 99.99 | 99.91 | 98.23 | 100 | 87.6 | 99.68
ARCEP Target | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90
Chart: BEST NETWORK
| #Regions
MTN | 6
MOOV | 8
CELTISS | 4
More than 90% with Outdoor: Rxlev >-92 dBm

## Slide 14: Benchmarking – 2G Coverage-Incar All operators has a simular 2G coverage and meet largily ARCEP requirements for In Car morphology except in roads, MOOV is ranked first in terms of 2G Incar coverage and slightly better than MTN and CELTISS.
Chart: BEST NETWORK
| #Regions
MTN | 4
MOOV | 5
CELTISS | 6
Chart: 2G incar COVERAGE
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 99.58 | 99.87 | 100 | 99.99 | 96.41 | 98.11 | 99.06 | 99.79 | 97.87 | 99.7 | 99.16 | 79.37 | 99.44
MOOV | 99.99 | 99.31 | 99.93 | 99.97 | 92.22 | 98.48 | 99.97 | 99.99 | 99.36 | 98.53 | 99.77 | 82.94 | 99.51
CELTISS | 98.59 | 98.68 | 99.98 | 99.97 | 99.91 | 98.06 | 99.99 | 99.94 | 99.36 | 96.39 | 99.95 | 75.36 | 99.37
ARCEP Target | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90
More than 90% with Incar: Rxlev >-87 dBm

## Slide 15: Benchmarking – 2G-Indoor MTN is leading in 2G Indoor coverage for over all, MTN meets ARCEP requirements except in SEME KAPODJI and major roads. MTN has outperformed its competitors in 5/12 regions.
Chart: BEST NETWORK
| #Regions
MTN | 5
MOOV | 4
CELTISS | 3
Chart: 2G Indoor COVERAGE
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 94.98 | 81.62 | 96.66 | 92.73 | 90.22 | 91.02 | 95.62 | 95.63 | 91.05 | 96.92 | 90.8 | 64.56 | 96.64
MOOV | 95 | 77.48 | 83.9 | 92.83 | 90.46 | 88.82 | 94.35 | 94.59 | 96.28 | 74.82 | 90.02 | 65.42 | 95.21
CELTISS | 98.59 | 81.48 | 88.58 | 96.73 | 89.28 | 86.16 | 93.7 | 93.09 | 85.66 | 69.17 | 91.41 | 57.95 | 95.46
ARCEP Target | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90
More than 90% with Indoor: Rxlev >-74 dBm

## Slide 16: Benchmarking – 3G COVERAGE MTN is leading in term of 3G coverage by having the best ratio in over all with 94,6% against 91,33% for MOOV and 93,81% for CELTISS MTN meets ARCEP requirements in all regions except in major roads.
Chart: BEST NETWORK
| #Regions
MTN | 6
MOOV | 1
CELTISS | 5
Chart: 3G COVERAGE (Indoor,INCAR,OUTDOOR)
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 96.81 | 91.68 | 91.03 | 90.02 | 92.15 | 94.09 | 94.35 | 97.95 | 91.33 | 92.45 | 86.47 | 62.65 | 94.6
MOOV | 85.35 | 83.54 | 83.54 | 89.35 | 91.56 | 88.98 | 92.33 | 93.96 | 76.3 | 73.14 | 84.84 | 68.5 | 91.33
CELTISS | 98.55 | 86.35 | 91.29 | 93.13 | 95.68 | 86.69 | 93.62 | 97.29 | 90.65 | 66.15 | 94.74 | 65.52 | 93.81
ARCEP Target | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90

## Slide 17: Benchmarking – 4G COVERAGE-Outdoor MTN is ranked second in overall 4G coverage for outdoor morphology, All operators meet ARCEP requirements for outdoor 4G coverage in all regions except in roads,
Chart: BEST NETWORK
| #Regions
MTN | 5
MOOV | 6
CELTISS | 1
Chart: 4G outdoor COVERAGE
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 98.29 | 96.1 | 96.9 | 97.27 | 96.42 | 97.32 | 97.25 | 99.21 | 98.92 | 99.54 | 96.68 | 81.2 | 94.34
MOOV | 99.59 | 95.73 | 95.73 | 99.18 | 95.99 | 99.36 | 99.13 | 99.61 | 98.73 | 98.83 | 99.92 | 73.78 | 96.32
CELTISS | 99.07 | 92.24 | 96.47 | 98.73 | 97.94 | 93.38 | 93.26 | 98.12 | 97.98 | 98.4 | 92.55 | 67.63 | 92.51
ARCEP Target | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90
More than 90% with RSRP >-95 dBm

## Slide 18: Benchmarking – 4G COVERAGE-Incar MOOV is clear leader in term of 4G coverage for incar morphology and has the best coverage in most regions, MTN needs to improve its 4 coverage in the following regions: OUIDAH, PARAKOU, ALLADA and major roads in order to satisfy ARCEP obligation.
Chart: BEST NETWORK
| #Regions
MTN | 4
MOOV | 8
CELTISS | 0
Chart: 4G incar COVERAGE
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 91.19 | 91.63 | 91.5 | 91.95 | 88.02 | 90.75 | 90.42 | 89.19 | 91.5 | 94.63 | 84.48 | 57.4 | 84.63
MOOV | 93.36 | 89.24 | 89.43 | 97.91 | 88.33 | 91.91 | 92.55 | 93.22 | 93.39 | 94.12 | 97.4 | 55.43 | 91.55
CELTISS | 93.22 | 77.64 | 90.66 | 95.91 | 60.95 | 78.56 | 76.75 | 87.62 | 89.5 | 82.82 | 77.22 | 49.51 | 83.73
ARCEP Target | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90

## Slide 19: Benchmarking – 4G Coverage-Indoor MOOV is ranked first in terms of Indoor 4G coverage in overall, All operators failed to meets ARCEP requirements for Indoor morphology, MTN is ranked second in overall and neesds to improve its mostly in OUIDAH, ALLADA and major roads.
Chart: 4G indoor COVERAGE
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 65.05 | 52.55 | 54.31 | 50.29 | 24.06 | 58.04 | 54.17 | 51.11 | 46.25 | 64.38 | 24.54 | 28.99 | 46.48
MOOV | 63.64 | 50.09 | 46.27 | 57.29 | 26.88 | 59.69 | 71.04 | 67.37 | 37.39 | 60.86 | 81.4 | 28.35 | 56.72
CELTISS | 79.56 | 46.93 | 59.91 | 57.38 | 23.03 | 64.8 | 24.53 | 60.83 | 20.63 | 44.47 | 44.23 | 25.32 | 45.88
ARCEP Target | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90
Chart: BEST NETWORK
| #Regions
MTN | 4
MOOV | 4
CELTISS | 4

## Slide 20: Benchmarking – voice service Accessibilty MTN has outperformed its competitors in term of accessibility by having the best call blocked rate in all regions except in DJOUGOU, but exceeds slightly ARCEP requirements.
Chart: Best Network
 | 0
MTN | 11
MOOV | 0
CELTISS | 1
Chart: Call Blocking
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 1.03 | 1.63 | 0.64 | 0.82 | 0.24 | 0.58 | 0.53 | 0.29 | 2.7 | 1.06 | 0.61 | 5.88 | 1.35
MOOV | 1.62 | 2.05 | 1.99 | 0.94 | 0.27 | 0.86 | 2.11 | 0.63 | 2.02 | 2.97 | 1.29 | 7.64 | 1.94
CELTISS | 1.77 | 1.72 | 0.8 | 0.91 | 0.32 | 0.84 | 0.36 | 0.31 | 0.97 | 4.25 | 1.17 | 9.58 | 1.89
ARCEP Target | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 21: Benchmarking – voice service Retainability MTN is ranked first in terms of retainability in overall, has the best call drop rate in 7/12 regions, only MTN’s network meets ARCEP requirements in overall by having a Call Drop Rate less than 1%.
Chart: BEST NETWORK
| Ranked 1
MTN | 7
MOOV | 4
CELTISS | 1
Chart: Call DROP
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 0.46 | 0.23 | 0.6 | 0.31 | 1.15 | 0.38 | 1.37 | 0.46 | 0.44 | 0.4 | 0.71 | 6 | 0.93
MOOV | 1.62 | 1.66 | 2.48 | 1.03 | 2.44 | 0.55 | 1.57 | 0.23 | 2.96 | 1.71 | 0.84 | 10.32 | 2.19
CELTISS | 1.77 | 0.24 | 1.11 | 0.15 | 0 | 0.78 | 0 | 0.37 | 0.95 | 1.28 | 0.41 | 9.56 | 1.34
ARCEP Target | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 22: Benchmarking – Integrity Voice Quality MTN is offering an acceptable voice quality and meets ARCEP requirements, but it is ranked third and outperfomed by competitors in terms Mean Opinion Score.
Chart: BEST NETWORK
| #Regions
MTN | 2
MOOV | 9
CELTISS | 1
Chart: VOICE QUALITY MOS
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 3.66 | 3.7 | 3.8 | 3.73 | 3.85 | 4.02 | 3.78 | 3.98 | 3.87 | 4.03 | 3.79 | 3.79 | 3.81
MOOV | 3.85 | 3.92 | 3.83 | 3.87 | 4.01 | 4.21 | 4.02 | 3.63 | 4.09 | 3.73 | 3.95 | 3.95 | 4.03
CELTISS | 3.94 | 3.85 | 3.79 | 3.85 | 3.94 | 3.94 | 3.86 | 3.85 | 3.91 | 3.93 | 3.91 | 3.91 | 3.9
ARCEP Target | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8

## Slide 23: Benchmarking – SMS Service MTN is ranked first in terms of SMS send/receive succes ratio and outperforms largely MOOV and CELTISS in over all and in the most regions, but all operators failed to meet ARCEP requirements due to the low E2E delivery time as defined by ARCEP (<6sec).
Chart: BEST NETWORK
| #Regions
MTN | 7
MOOV | 0
CELTISS | 5
Chart: SMS Sending Success
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 92.5 | 90.22 | 93.16 | 90.59 | 98.71 | 97.51 | 95.89 | 99.77 | 99.45 | 99.36 | 96.34 | 92.2 | 95.33
MOOV | 80.59 | 84.43 | 92.7 | 89.35 | 96.57 | 91.8 | 85.5 | 96.34 | 92.43 | 93.59 | 93.73 | 89.5 | 91.18
CELTISS | 95.01 | 95.63 | 93.74 | 83.67 | 93.81 | 98.89 | 89.6 | 89.08 | 90.84 | 85.21 | 99.67 | 91.12 | 92.07
ARCEP Target | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99
Chart: SMS Receiving Success
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 96.87 | 88.51 | 90.83 | 88.88 | 97.33 | 96.33 | 94.12 | 99.11 | 99.17 | 98.87 | 95.14 | 90.09 | 94.1
MOOV | 96.3 | 82.1 | 89.78 | 88.1 | 94.51 | 89.01 | 83.98 | 95.33 | 91.33 | 90.38 | 91.1 | 88.14 | 89.93
CELTISS | 97.66 | 92.86 | 91.88 | 82.44 | 91.89 | 96.46 | 87.65 | 88.91 | 88.97 | 84.44 | 99.36 | 90.67 | 91.01
ARCEP Target | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99 | 99
Chart: best nertwork
| #Regions
MTN | 6
MOOV | 0
CELTISS | 6

## Slide 24: Benchmarking – 3G Internet Connexion/ Web Service Success Rate MTN is leading in terms of accessibilty to data service in over all, MTN has the best accessibility to web service. All operators meet ARCEP requirement for both KPIs except in major roads.
Chart: BEST NETWORK
| #Regions
MTN | 9
MOOV | 6
CELTISS | 6
Chart: 3G Internet Connexion SuccesS
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 100 | 100 | 100 | 100 | 99.86 | 100 | 100 | 98.81 | 98.44 | 100 | 97.44 | 95.25 | 98.96
MOOV | 100 | 100 | 100 | 99.27 | 98 | 99.92 | 99.55 | 99.07 | 98.1 | 100 | 98.59 | 91.22 | 98.11
CELTISS | 100 | 100 | 100 | 100 | 98.35 | 100 | 98.9 | 98.27 | 98.56 | 100 | 97.1 | 93.47 | 98.51
ARCEP Target | 96 | 96 | 96 | 96 | 96 | 96 | 96 | 96 | 96 | 96 | 96 | 96 | 96
Chart: 3G Web Service SUCCESS
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 100 | 98.2 | 97.99 | 99.76 | 99.04 | 97.56 | 98.88 | 97.98 | 99.65 | 99.78 | 99.31 | 93.33 | 98.17
MOOV | 100 | 95.22 | 98.39 | 97.94 | 99.72 | 99.55 | 99.77 | 96.87 | 98.78 | 95.33 | 96.44 | 87.89 | 97.22
CELTISS | 100 | 84.7 | 98.44 | 99.88 | 98.78 | 98.11 | 98.26 | 95.08 | 99.81 | 99.06 | 100 | 88.3 | 96.94
ARCEP Target | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90
Chart: BEST NETWORK
| #Regions
MTN | 5
MOOV | 4
CELTISS | 5

## Slide 25: Benchmarking – 3G/4G HTTP Connexion Setup Time MTN is clear leader in HTTP connexion Setup Time, All operators meet ARCEP requirements.
Chart: BEST Network
| #Regions
MTN | 9
MOOV | 0
CELTISS | 3
Chart: 3G HTTP Connexion Setup Time
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 6.23 | 5.98 | 6.22 | 5.33 | 5.09 | 6.09 | 5.91 | 5.77 | 5.78 | 6.66 | 5.35 | 7.29 | 5.84
MOOV | 5.55 | 6.01 | 6.33 | 6.49 | 6.31 | 6.12 | 6.07 | 7.35 | 6.29 | 6.98 | 7.01 | 8.3 | 6.34
CELTISS | 4.89 | 5.89 | 5.74 | 6.02 | 5.98 | 5.87 | 6.1 | 7.32 | 6.19 | 7.01 | 6.49 | 8.77 | 6.41
ARCEP Target | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10

## Slide 26: Benchmarking – 3G FTP Service All operators meet the ARCEP target for FTP sucees ratio, CELTISS is ranked first in overall for FTP DL/UL sucess ratio and slightly better than MTN.
Chart: 3G FTP DL SUCCESS
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 99.6 | 100 | 99.15 | 100 | 98.66 | 99.15 | 98.58 | 99.69 | 100 | 99.56 | 100 | 95.42 | 99.07
MOOV | 99.83 | 99.36 | 98.73 | 98.65 | 99.88 | 99.57 | 98.69 | 100 | 97.94 | 98.7 | 99.53 | 93.66 | 98.42
CELTISS | 100 | 98.93 | 99.93 | 99.29 | 99.51 | 100 | 99.58 | 97.01 | 100 | 100 | 99.52 | 98.68 | 99.21
ARCEP Target | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97
Chart: BEST NETWORK
| #Regions
MTN | 4
MOOV | 2
CELTISS | 6
Chart: 3G FTP UL SUCCESS
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 99.64 | 98.53 | 99.41 | 99.29 | 100 | 98.23 | 97.13 | 98.86 | 100 | 99.16 | 99.55 | 93.92 | 98.51
MOOV | 99.83 | 97.69 | 99.37 | 98.11 | 100 | 95.02 | 97.26 | 91.15 | 99.63 | 100 | 100 | 97.73 | 97.88
CELTISS | 99.69 | 100 | 99.71 | 99.74 | 99.49 | 98.77 | 99.13 | 96.51 | 99.81 | 99.38 | 99.5 | 92.96 | 98.71
ARCEP Target | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97
Chart: BEST NETWORK
| #Regions
MTN | 3
MOOV | 4
CELTISS | 5

## Slide 27: Benchmarking – 3G FTP service DL/UL throughput CELTISS is clear leader in terms of FTP End User DL throughput in over all, MTN meets ARCEP requirements, but needs to improve its FTP DL/UL throughput.
Chart: 3G FTP DL THROUGHPUT
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 2200.6 | 2107.21 | 4256.87 | 2963.37 | 3259 | 3482.24 | 3506.88 | 4830.86 | 4622.48 | 6970.1 | 5344.28 | 4432.96 | 3654.24
MOOV | 3337.54 | 2007.25 | 4975.2 | 3762.44 | 5853.58 | 4651.89 | 3089.84 | 3008.55 | 4717.91 | 4493.77 | 4071.6 | 3134.27 | 4740.32
CELTISS | 4620.29 | 2083.22 | 6136.24 | 4201.33 | 7928.99 | 7631.54 | 6459.46 | 6810.93 | 6828.5 | 6544.37 | 9464.71 | 5867.9 | 7474.61
ARCEP Target | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000
Chart: BEST NETWORK
| #Regions
MTN | 2
MOOV
CELTISS | 10
Chart: 3G FTP UL THROUGHPUT
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 1045.72 | 1022.33 | 2197.08 | 1207 | 1147.85 | 1156.47 | 1982.95 | 2318.31 | 2355.19 | 2627.48 | 2002.72 | 1867.87 | 1682.37
MOOV | 1014.22 | 1009.53 | 1183.54 | 1164.53 | 1458.95 | 1272.73 | 1168.93 | 908.33 | 1527.06 | 1391.74 | 1159.53 | 1352.87 | 1226.04
CELTISS | 2151.61 | 1002.47 | 2007.05 | 2078.29 | 2163.03 | 1986.65 | 1755.94 | 1919.2 | 1880.52 | 2015.55 | 2186.94 | 1793.38 | 2072.49
ARCEP Target | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000 | 1000
Chart: BEST NETWORK
| #Regions
MTN | 7
MOOV
CELTISS | 5

## Slide 28: Benchmarking – 4G Web Service MTN is ranked first in terms of web service by having the best succes ratio in all regions except in SEME KAPODJI.
Chart: BEST NETWORK
| #Regions
MTN | 10
MOOV | 1
CELTISS | 1
Chart: 4G Web Service SUCCESS
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 100 | 98.33 | 98.51 | 99.91 | 100 | 100 | 98.96 | 100 | 100 | 98.11 | 100 | 97.08 | 99.05
MOOV | 100 | 98.78 | 97.87 | 99.78 | 100 | 100 | 98.17 | 99.55 | 98.39 | 97.45 | 100 | 95.33 | 98.7
CELTISS | 100 | 97.71 | 98.11 | 99.89 | 100 | 100 | 97.88 | 98.77 | 99.08 | 97.88 | 100 | 95.26 | 98.52
ARCEP Target | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97

## Slide 29: Benchmarking – 4G FTP service MTN is leading in terms of 4G FTP DL/UL success rate and meets ARCEP requirements except for FTP UL succes rate in major roads.
Chart: BEST NETWORK
| #Regions
MTN | 6
MOOV | 5
CELTISS | 8
Chart: BEST NETWORK
| #Regions
MTN | 7
MOOV | 6
CELTISS | 7
Chart: 4G FTP DL SUCCESS
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 99.67 | 99.68 | 99.87 | 99.57 | 100 | 100 | 100 | 99.67 | 100 | 99.57 | 100 | 99.41 | 99.68
MOOV | 99.84 | 99.86 | 99.21 | 100 | 99.1 | 100 | 100 | 100 | 99.67 | 99.78 | 100 | 93.26 | 99.11
CELTISS | 100 | 99.91 | 99.04 | 100 | 100 | 100 | 99.32 | 95.39 | 100 | 91.67 | 100 | 87.5 | 97.55
ARCEP Target | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97
Chart: 4G FTP UL SUCCESS
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 99.65 | 99.66 | 98.44 | 99.12 | 100 | 99.13 | 100 | 100 | 100 | 100 | 99.57 | 93.13 | 99.13
MOOV | 100 | 100 | 98.88 | 99.54 | 99.54 | 99.53 | 99.77 | 100 | 99.66 | 99.55 | 100 | 90.79 | 98.83
CELTISS | 99.84 | 100 | 98.24 | 99.78 | 100 | 100 | 100 | 97.14 | 100 | 100 | 100 | 91.03 | 98.71
ARCEP Target | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97 | 97

## Slide 30: Benchmarking – 4G FTP service DL/UL throughput MTN is clear leader in terms of 4G DL/UL throughput and has an excellent performance compared to its competitors. MTN is ranked first for FTP UL throughput in all regions. MTN is outperformed by CELTISS in Cotonou, SEME KAPODJI, Porto Novo and CALAVI.
Chart: BEST NETWORK
| #Regions
MTN | 12
MOOV
CELTISS | 0
Chart: BEST NETWORK
| #Regions
MTN | 8
MOOV | 4
CELTISS | 0
Chart: 4G FTP DL THROUGHPUT
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 13142.8 | 16025.78 | 17358.51 | 19467.82 | 53331.19 | 57419.807 | 36956.67 | 29498.84 | 38987.91 | 52666.45 | 46172.72 | 39881.87 | 34940.53
MOOV | 20806.22 | 19923.88 | 22727.79 | 22708.55 | 36338.56 | 27516.67 | 15662.65 | 12899.09 | 17045.28 | 15471.21 | 24826.97 | 10525.87 | 21238.29
CELTISS | 11794.11 | 12973.33 | 13012.4 | 12677.21 | 13943.75 | 12933.84 | 12999.143 | 12572.95 | 12899.65 | 14025.19 | 12997.57 | 10351.44 | 12580.27
ARCEP Target | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000 | 5000
Chart: 4G FTP UL THROUGHPUT
| COTONOU | SEME KAPODJI | PORTO NOVO | CALAVI | OUIDAH | LOKOSSA | BOHICON | PARAKOU | DJOUGOU | NATITINGOU | ALLADA | MAJOR ROADS | ALL NETWORK
MTN | 15180.9 | 14533.67 | 16738.8 | 16192.44 | 17146.62 | 18741.88 | 15436.67 | 15470.95 | 18164.79 | 21183.75 | 16624.74 | 13135.49 | 16435.88
MOOV | 9449.7 | 9630.57 | 10633.13 | 14256.16 | 13019.58 | 13537.6 | 9549.01 | 11821.62 | 11628.13 | 8075.06 | 13955.81 | 7045.87 | 10855.57
CELTISS | 12408.7 | 11336.33 | 12150.4 | 12265.83 | 11937.85 | 11474.41 | 14439.78 | 10259.33 | 11562.18 | 10441.17 | 11903.43 | 9103.26 | 11743.18
ARCEP Target | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000

## Slide 31
QoE Global Scoring and Ranking
04

## Slide 32: QoE Scoring and Ranking based on Deloitte proposed weights
Category | Technology | Weight | KPI Item | Lower | Upper |  |  |  | 
 |  |  |  |  |  | KPI Value | KPI Value | Score | Score
PS Experience | 4G | 10 | Coverage (RSCP>=-105 dbm) | 80% | 100% | 74.6% | 83.7% | 0.00 | 1.85
 | 3G | 20 | Coverage (RSCP>=-94 dbm) | 85% | 100% | 73.9% | 70.52% | 0 | 0
 | 4G | 15 | Average FTP DL THP (kbps) | 5000 | 40000 | 14588 | 10915 | 7.85 | 6.17
 | 3G | 25 | Average FTP DL THP (kbps) | 2000 | 10000 | 3167 | 2615 | 9.55 | 6.93
 | 4G | 5 | Average FTP UL THP (kbps) | 2000 | 10000 | 6313 | 6895 | 3.67 | 3.91
 | 3G | 5 | Average FTP UL THP (kbps) | 1000 | 5000 | 1233 | 1068 | 1.21 | 0.65
 | 4G | 5 | Accessibility Rate (%) | 90% | 100% | 98.57% | 99.65% | 4.29 | 4.83
 | 3G | 5 | Accessibility Rate (%) | 90% | 100% | 99.17% | 95.58% | 4.59 | 2.79
 | 4G | 5 | Average HTTP Connexion Setup Time (s) | 1 | 3 | 3.47 | 2.60 | 0.00 | 2.24
 | 3G | 5 | Average HTTP Connexion Setup Time (s) | 2 | 5 | 2.96 | 4.00 | 4.12 | 2.89
 | 3G/4G | 100 | Total Score |  |  |  |  | 35.27 | 30.40
MTN is number 1 for mobile internet capacity through its 3G/4G Network

## Slide 33: QoE Scoring and Ranking based on Deloitte proposed weights
Category | Technology | Weight | KPI Item | Lower | Upper |  |  |  |  |  | 
 |  |  |  |  |  | KPI Value | KPI Value | KPI Value | Score | score | score
CS Experience | 2G | 25 | Coverage (RxLev>=-87 dbm) | 90% | 100% | 99.44% | 99.51% | 99.37% | 23,60 | 23.98 | 23.43
 | 3G | 25 | Coverage (RSCP>=-94 dbm) | 85% | 100% | 94.60% | 91.33% | 93.81% | 16.00 | 10.55 | 14.86
 | 2G/3G | 15 | Call blocking rate | 90% | 100% | 98.65% | 98.06% | 98.11% | 12.98 | 12.09 | 12.17
 | 2G/3G | 15 | Call drop rate | 5% | 1% | 0.93% | 2.19% | 1.36% | 15 | 10.54 | 13.73
 | 2G/3G | 20 | Mean Opinion Score | 0 | 5 | 3.83 | 4.03 | 3,9 | 17,46 | 17.96 | 17.66
 | 2G/3G | 100 | Total Score |  |  |  |  |  | 85.02 | 74.91 | 81.66
MTN is number 1 for voice communication quality of Experience

## Slide 34
Mean KPIs By Districts
05

## Slide 35: Benchmarking – MTN 4G FTP DL throughput by districts For MTN’network, 97% of districts having DL End User throughput better than 5Mbps and meet ARCEP requirements.
Chart: MTN 4G FTP DL THP[Kbps] Per Districts

## Slide 36: Benchmarking – MTN 4G coverage by districts For MTN’network, 73,79% of districts having an average RSRP better than -95dBm,

## Slide 37: Benchmarking – MTN 2G coverage by districts For MTN’s 2G coverage 95,45% of districts have an average Rxlev better than -95dBm And meet ARCEP requirements.
Chart: MTN 2G coverage Per Districts

## Slide 38: Benchmarking – MTN 3G coverage by districts For MTN’s 2G coverage 84% of districts with average RSCP better than -90dBm.
Chart: MTN 3G coverage By boroughs

## Slide 39
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2019 Deloitte Bénin SARL. Société du réseau Deloitte