## Slide 1
Network QoS
Intermediate report
Octobre 30st, 2023

## Slide 2: Summary
Context & Report objectives | 03
Scope of Work | 05
Drive tests Activity, Current Status & Progress | 08
Executive Summary | 12
KPIs & Network settings Analysis | 18
Benchmarking on Cotonou area | 67
Next steps | 107

## Slide 3
Context & Report objectives
01

## Slide 4: Context & Report objectives
1
MTN Benin is a leading mobile operator in Benin with more than 60% market share.
2
It operates a network comprising of 675 2G, 3G and LTE sites across Benin.
3
MTN Benin wants an independent assessment and benchmarking of its radio network through drive tests
4
MTN Benin also wants to ascertain network assurance and capacities
Overview of the NW QoS assessment scope
A comprehensive drive testing exercise to determine customer perceived radio network quality of MTN Benin’s 2G, 3G and LTE network with that of the competition and the KPIs required by the regulator.
Formulate drive test methodology and coverage
Finalize reporting format and KPIs to be measured
Conduct drive tests for MTN Benin and competitor’s network
Validate results with MTN Benin’s radio planning team
Benchmark key KPIs between MTN, competition and regulator defined KPIs levels
Recommendations for network improvement
1
2
3
4
5
6
Detailed scope
Objectives of the assignment
2G/3G/4G MTN Networks KPIs audit based on OSS counters
Parameters settings audit of 2G/3G/4G MTN network
Capacity audit of 2G/3G/4G MTN network
Evaluate and benchmark Quality levels offered by MTN to MOOV mobiles networks and regulator defined KPIs levels based on Drive Test measurements results

## Slide 5
Scope of Work
02

## Slide 6: Scope of work (i/ii)
Conduct OSS Audit
  2G/3G/4G MTN Networks KPIs audit based on OSS counters
  Parameters settings audit of 2G/3G/4G MTN network
  Capacity audit of 2G/3G/4G MTN network
Hourly KPI review
HW / Alarms review
RAN Parameters
RAN Features
Neighbors
HW/licensing
Kick-off
Prerequisites
Data collection
Result analysis
Suggest Recommendations
audit report written
Presentation and actions
Close out report
Preparation
Early KPI
warning
Configuration Audit
Performance Analysis
Dimensioning
Reporting
Evaluate and benchmark Quality levels offered by MTN to MOOV mobiles networks and regulator’s defined KPIs levels based on Drive Test measurements results
  Voice service quality and SMS (one team with Drive test tool)
  3G Data FTP DL/UL and HTTP Browsing (one team with Drive test tool)
  4G Data FTP DL/UL and HTTP Browsing (one team with Drive test tool)
Drive Test execution
Post processing and report preparation
Kick-off
Prerequisites
Drive Test route preparation
Deep Analysis and
Recommendations
Presentation
Preparation
Network Data Collection
Post Processing
Events and layer 3 analysis
Reporting

## Slide 7: Scope of Work (ii/ii)
Cost
Cities to be covered
Cost
Drive Test KPI
Data KPIs (2G/3G/LTE)
HTTP IP-Service Access Success Ratio
HTTP Data Transfer Success Ratio
Session Setup time
HTTP mean data rate
FTP Session Success Rate
FTP UL/DL Throughput
Coverage rate (2G/3G/LTE)
Outoor Coverage rate
Indoor coverage rate
Incar coverage rate
Voice KPIs
Call blocking rate
Call drop rate
Call completetion success rate
Call completetion, with perfect quality, rate
Call completetion, with good quality, rate
Voice Quality (MOS)
SMS
MO SMS delivery success rate
MT SMS delivery success rate
19 indicators to analyze
18 thousand samples to analyze

## Slide 8
Drive tests Activity, Current Status & Progress
03

## Slide 9: Drive tests Activity, Current Status & Progress Drive test and Benchmark evaluation is on track according to initial plan
The Drive Test execution is ongoing as initially planned
We have processed more than 90% of Cotonou and SEME data

## Slide 10: Intermediate report
Scope of this report
1. A RAN network audit for MTN BENIN, aiming to identify weak points as well as suggests proposals to improve the network quality, and so the final user perception
  Current parameterization was analyzed and recommendations provided where appropriate, regarding RF environment, settings, design, etc.
  Analyzed cells which belong to:
    RNCs : HOERNC1 ,HOERNC2, BHERNC4 and DCERNC3
    BSCs : BHBSC05, BHEBSC6, DCBSC04, HOBSC02, HOBSC03.
  Network configuration and different performance measurements based on data from December 10th to 26th, 2018
  2. Network benchmarking results between MTN and MOOV on Cotonou area.

## Slide 11
Executive Summary
04

## Slide 12: Executive Summary – Benchmarking (i/iii) MTN and MOOV Networks QoS are comparable. A resource optimization enables to meet ARCEP requirements and to outperform competition’s NW QoS
2G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Coverage :
MTN coverage rate (99,97%) is comparable with its competitor's MOOV (99,99%) CELTISS (99,97%)
All operators meets ARCEP 2G coverage obligation.
Voice service :
Accessibility: MTN is better than MOOV and slightly lower than CELTISS.
All operators failed to meet ARCEP 2G coverage obligation.
Retainability: MTN is slightly lower than MOOV and CELTISS.
All operators meets ARCEP 2G coverage obligation.
Integrity: MTN is slightly lower than MOOV and CELTISS.
All operators meets ARCEP 2G coverage obligation.
SMS service :
MTN is better than MOOV and lower than CELTISS.
All operators failed to meet ARCEP 2G coverage obligations.
RF optimization (Physical and logical) is needed to improve 2G MTN coverage.
Actions to improve accessibility are already proposed.

## Slide 13: Executive Summary - Benchmarking (ii/iii) MTN network QoS is globally better than the MOOV’s. A design optimization can enable a better network QoS on all KPIs
3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Coverage :
3G MTN coverage rate (99,55%) is comparable with its competitor's MOOV (99,21%) CELTISS (99,74%)
All operators meets ARCEP 3G coverage obligation.
Voice service :
Accessibility: MTN is slightly lower than MOOV and CELTISS.
All operators failed to meet ARCEP accessibility obligation
Retainability: : MTN is better than MOOV and slightly lower than CELTISS.
Only MTN and CELTISS meets ARCEP retainability obligation
Integrity: MTN is slightly lower than MOOV and CELTISS.
All operators meets ARCEP integrity obligation
SMS service :
MTN is better than MOOV and slightly lower than CELTISS.
All operators failed to meet ARCEP 3G coverage obligation.
Data service :
MTN throughput (DL:2,2M/UL:1,04M) is slightly lower than MOOV (DL:3,3M/UL:1,01M) and CELTISS (DL:4,6M/UL:4,1M) .
All operators meets ARCEP 3G throughput obligations.
RF optimization (Physical and logical) is needed to improve 3G MTN coverage.
Actions to improve accessibility are presented in the previous chapter

## Slide 14: Executive Summary - Benchmarking (iii/iii) Ther 4G network coverage rate is comparable among all operators. MTN network mean throughput UL is better than MOOV’s and CELTISS’s. A Radio extension of the MTN network will enable outperforming competition’s 4G coverage and capacity
4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Coverage :
4G MTN coverage rate (99,28%) is comparable with MOOV’s (99,96%) and CELTISS’s (99,54)
All operators meets ARCEP 4G coverage obligation.
Data service :
MTN i 4G throughput DL (13,1M) is better than CELTISS’s (11,7M) and lower than MOOV’s(20,8M)
MTN i 4G throughput UL (15,1M) is better than MOOVS’s (9,4M) and CELTISS’s(12,4M)
All operators meets ARCEP 4G coverage obligation
It is recommended to deploy more 4G sites in order to have a continuous 4G coverage; better than competitors

## Slide 15: Benchmarking Key Results – Coverage MTN & MOOV & CELTISS have a close 2G /3G coverage but 4G coverage of MTN is lower than MOOV’s and CELTISS. 4G Network extension is needed in Cotonou to reach MOOV coverage
KPI |  | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
2G Coverage Rate | Incar | More than 70% with Incar: Rxlev >-87 dBm | 99,97% | OK | 99,99% | OK | 99,97% | OK | 2
 | Outdoor | More than 70% with Outdoor: Rxlev >-92 dBm | 99,70% | OK | 99,63% | OK | 99,74% | OK | 2
 | Indoor | More than 70% with Outdoor: Rxlev >-74 dBm |  |  |  |  |  |  | 
3G Coverage Rate | Incar | More than 90% with RSCP <-85 dBm | 96,00% | OK | 85,35% | NOK | 98,55% | OK | 2
 | Outdoor | More than 90% with RSCP <-85 dBm | 69,74% | OK | 70,00% | OK | 87,35% | OK | 3
 | Indoor | More than 90% with RSCP <-85 dBm |  |  |  |  |  |  | 
4G Coverage Rate | Incar | More than 60% with RSRP <-90 dBm* | 72,30% | OK | 93,34% | OK | 93,21% | OK | 3
 | Outdoor | More than 60% with RSRP <-95 dBm* | 28,16% | NOK | 79,22% | OK | 85,92% | OK | 3
 | Indoor | More than 60% with RSRP <-78 dBm* |  |  |  |  |  |  | 

## Slide 16: Benchmarking Key Results – 2G/3G voice and SMS Summary MTN network in retainability CDR (%) meets ARCEP requirements, MTN is leading in accessibility but slightly exceeds ARCEP threshold, MTN needs to improve its Voice Quality MOS and SMS Send duration.
KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  | Value | Conformity | Value | Conformity | Value | Conformity | 
Accesibility: Blocking rate | <1% | 1,03% | NOK | 1,62% | NOK | 1,77 | NOK | 1
Retainability: Call drop rate | <1% | 0,46% | OK | 2,21% | NOK | 0,33% | OK | 2
Integrity: Voice quality | Note requise> 2,8 | 3,66 | OK | 3,85 | OK | 3,94 | OK | 3
SMS sending success rate % (E2E delivery Time<6 sec) | >99% | 92,50% | NOK | 80,59% | NOK | 95,01% | NOK | 2
SMS receving success rate % | >99% | 96,87% | NOK | 96,30% | NOK | 97,66% | NOK | 2

## Slide 17: Benchmarking Key Results – 3G Data Summary MTN network in 3G DATA meets ARCEP requirements, MTN needs to improve its 3G Data THP compared to competitors.
Services | KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
3G DATA | 3G Availabaility | >=95% | 99,21% | OK | 99,70% | OK | 99,12% | OK | 2
3G HTTP | Successful internet connexion rate | >90% | 100,00% | OK | 100,00% | OK | 100,00% | OK | 1
 | Connexion setup time | <=30sec | 1,23 | OK | 0,65 | OK | 0,28 | OK | 3
 | Web service failure rate | <10% | 0,00% | OK | 0,00% | OK | 0% | OK | 1
3G FTP | FTP failure rate UL/DL | <20 % | 0,40%/0,36% | OK | 0,17%/0,17% | OK | 0%/0,31% | OK | 3
 | FTP Data transmission average (DL) | >= 2Mbps | 2200,6 | OK | 3337,54 | OK | 4620,2 | OK | 3
 | FTP Data transmission average (UL) | >= 1Mbps | 1045,72 | OK | 1014,22 | OK | 2151,61 | OK | 2

## Slide 18: Benchmarking Key Results – 4G Data Summary MTN’s 4G DATA network End User KPIs satisfy ARCEP requirements, MTN is ranked second in 4G DL THP after MOOV’s , MTN is outperforming MOOV’s & CELTISS in 4G UL THP.
Services | KPI | Threshorlds* | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
4G HTTP Browsing | Web service failure rate | <10% | 0,00% | OK | 0,00% | OK | 0,00% | OK | 1
 | Connexion setup time | <=10sec | 0,32 | OK | 0,37 | OK | 0,12 | OK | 2
4G FTP | FTP failure rate UL/DL | <10 % | 0,33%/0,35% | OK | 0,16%/0% | OK | 0%/0,16% | OK | 3
 | FTP Data transmission average (DL) | 4G >= 10 Mbps | 13142,8 | OK | 20806,2 | OK | 11794,11 | OK | 2
 | FTP Data transmission average (UL) | 4G: >= 4Mbps | 15180,9 | OK | 9449,7 | OK | 12408,7 | OK | 1

## Slide 19: Benchmarking – 2G coverage comparison map MOOV’s 2G coverage is very close to MTN’s CELTISS’S 2G coverage outperforming MTN’s and MOOV’s

## Slide 20: Benchmarking – 2G coverage comparison MTN & MOOV & CELTISS’s 2G coverage meets ARCEP RxLev Threshold requirements
Chart: RxLev Distribution (%)
| -74 to -10 | -87 to -74 | -92 to -87 | -110 to -92 | ACCEPTABLE COVREGE
MTN | 0.9458 | 0.0539 | 0.0003 | 0 | 0.9997
MOOV | 0.95 | 0.0499 | 0 | 0 | 0.9999
CELTISS | 0.9859 | 0.0138 | 0.0003 | 0 | 0.9997

## Slide 21: Benchmarking – 3G coverage comparison map MTN’s 3G coverage is outperforming MOOV’s 3G coverage MTN’s 2G coverage is very close to CELTISS’s

## Slide 22: Benchmarking – 3G coverage comparison CELTISS's 3G Radio coverage rate (99.74%) is outperforming MTN’s (99.55%) and MOOV’s (99,21%)
99.55% of DT 3G MTN Samples showing a good RSCP more than -86 which is satisfying ARCEP’s criteria
Chart: RSCP Distribution (%)
| -86 to -5 | -94 to -86 | -110 to -94 | ACCEPTABLE COVREGE
MTN | 0.9681 | 0.0274 | 0.0044 | 0.9955
MOOV | 0.8535 | 0.1386 | 0 | 0.9921
CELTISS | 0.9855 | 0.0119 | 0.0026 | 0.9974

## Slide 23: Benchmarking – 4G coverage comparison map CELTISS’s 4G coverage is outperforming MTN’s and MOOV’s

## Slide 24: Benchmarking – 4G coverage comparison MTN's 4G Radio coverage rate (99.28%) is very close MOOV's (99.96%) and CELTISS’s (99.54%)
Chart: RSRP Distribution (%)
| -85 to -5 | -90 to -85 | -105 to -90 | -120 to -105 | GOOD RSRP
MTN | 0.4749 | 0.2481 | 0.2698 | 0.0073 | 0.9928
MOOV | 0.6948 | 0.2386 | 0.0662 | 0.0003 | 0.9996
CELTISS | 0.8417 | 0.0904 | 0.0633 | 0.0045 | 0.9954

## Slide 25: Benchmarking – Voice quality comparison (MOS) map MOOV Voice Quality is much better & excellent compared to MTN’s and CELTISS

## Slide 26: Benchmarking – Voice quality comparison (MOS) CELTISS Voice Quality is much better & excellent compared to MTN’s and MOOV’S, MTN needs to improve its voice quality MOS.
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Exc+Good
MTN | 0.3525 | 0.535 | 0.0721 | 0.0405 | 0.8875
MOOV | 0.782 | 0.1652 | 0.0305 | 0.0223 | 0.9472
CELTISS | 0.6471 | 0.3411 | 0.0076 | 0.0042 | 0.9882

## Slide 27: Benchmarking – Voice quality MOS by technology Voice Quality MOS by technology
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Exc+Good
MTN | 0.3525 | 0.535 | 0.0721 | 0.0405 | 0.8875
MOOV | 0.782 | 0.1652 | 0.0305 | 0.0223 | 0.9472
CELTISS | 0.6471 | 0.3411 | 0.0076 | 0.0042 | 0.9882
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Exc+Good
MTN | 0.3525 | 0.535 | 0.0721 | 0.0405 | 0.8875
MOOV | 0.782 | 0.1652 | 0.0305 | 0.0223 | 0.9472
CELTISS | 0.6471 | 0.3411 | 0.0076 | 0.0042 | 0.9882

## Slide 28: Benchmarking – EC/NO comparison map 3G MOOV’s and CELTISS’s Quality is outperforming MTN’s. MTN network design needs to be optimized

## Slide 29: Benchmarking – EC/NO comparison 12,35% of drive test samples are showing a very low level of EcNo for 3G MTN network. A physical design optimization is needed
Chart: Ec/No Distribution (%)
| -8 to 0 | -12 to -8 | -16 to -8 | -34 to -16 | Good Ec/No
MTN | 0.1235 | 0.2046 | 0.5191 | 0.1528 | 0.3281
MOOV | 0.3576 | 0.3462 | 0.2594 | 0.0368 | 0.7038
CELTISS | 0.8306 | 0.1467 | 0.0189 | 0.0038 | 0.9773

## Slide 30: Benchmarking – SNIR comparison map 4G CELTISS Signal of quality is outperforming MTN’s and MOOV’s

## Slide 31: Benchmarking – SNIR comparison Drive tests are showing a low level of MTN Network SINR.
Chart: SINR Comparison
| (Min,-4) | (-4,0) | (0,7) | (7,15) | (15,20) | Good SINR
MTN | 0.0362 | 0.1531 | 0.4603 | 0.255 | 0.0735 | 0
MOOV | 0.0878 | 0.3154 | 0.3141 | 0.2102 | 0.0548 | 0
CELTISS | 0.0129 | 0.0459 | 0.2355 | 0.5299 | 0.1233 | 0

## Slide 32: Benchmarking – BLOCKED CALLS EVENTS map All operators MTN & MOOV & CELTISS are not satisfying ARCEP CSSR/CBR requirements

## Slide 33: Benchmarking – BLOCKED CALLS per Technology MTN has a high rate of blocked calls for 3G network
Chart: Call Setup Success Rate and Call Blocked Rate per Technology (%)
| 2G | 3G | 2G | 3G | 2G | MTN | MOOV | CELTISS
CSSR (%) | 0.9625 | 0.965 | 0.95 | 0.9727 | 0.9731
CBR (%) | 0.0375 | 0.035 | 0.05 | 0.0273 | 0.0269

## Slide 34: Benchmarking – 2G/3G CALL SETUP TIME MTN Call setup time is outperforming MOOV’s and CELTISS’s All operators MTN & MOOV & CELTISS’s have a high call setup time
Chart: Call Setup Time (s)
| Call Setup Time
MTN | 6.96
MOOV | 8.56
CELTISS | 8.27

## Slide 35: Benchmarking – HANDOVER FAILURE EVENTS map

## Slide 36: Benchmarking – HANDOVER FAILURE MTN’s and CELTISS’s Network Handover success rate are perfect compared to MOOV’s
Chart: Handover Success Rate (%)
| HSR (%)
MTN | 0.996
MOOV | 0.793
CELTISS | 0.995

## Slide 37: Benchmarking – DROPPED CALLS EVENTS map Voice Session Continuity of MTN and CELTISS network is outperforming MOOV’s

## Slide 38: Benchmarking – 2G/3G DROPPED CALLS MTN & CELTISS CDR are satisfying ARCEP threshold Compared to MOOV’s CDR network which is bad
Chart: Call Drop Rate (%)
| CDR (%)
MTN | 0.0046
MOOV | 0.0221
CELTISS | 0.0038

## Slide 39: Benchmarking – DROPPED CALLS per technology MTN & CELTISS network has an excellent drop rate compared to MOOV’s network that has a bad drop rate for 3G technology
Chart: Call Drop Rate per Technology (%)
| 2G | 3G | 2G | 3G | 2G | MTN | MOOV | CELTISS
CDR (%) | 0.0023 | 0.0023 | 0 | 0.0221 | 0.0018

## Slide 40: Benchmarking – SMS SENDING FAILURE EVENTS map CELTISS SMS SETUP/RESPONSE is much better than MTN’s & MOOV’s

## Slide 41: Benchmarking – SMS SENDING FAILURE CELTISS SMS SETUP/RESPONSE is outperforming MTN’s & MOOV’s. SMS service KPIs of the three operators are not compliant with the ARCEP requirements
MTN SMS sending/Receiving SR in MTN is excellent compared to MOOV’s
The Samples done in this DT not fulfils the ARCEP requirement for MTN.
Chart: SMS
| SMS Sending message success rate (%) | SMS Receving message success rate (%)
MTN | 0.9643 | 0.9687
MOOV | 0.962 | 0.963
CELTISS | 0.9633 | 0.9766

## Slide 42: Benchmarking – DATA 3G All operators have a good rate of successful Internet connection
Chart: PS Attach & PDP Contex Act(%)
| PS Attach success(%) | PS Attach fail (%) | PDP Context Act Success (%) | PDP Context Act fail (%)
MTN | 1 | 0 | 1 | 0
MOOV | 1 | 0 | 1 | 0
CELTISS | 1 | 0 | 0.9992 | 0.0008
Chart: Attach & PDP Activation Time (s)
| PS Attach Setup Time | PDP Context Act Time
MTN | 3.22 | 1.37
MOOV | 2.97 | 1.41
CELTISS | 3.34 | 1.46

## Slide 43: Benchmarking – DATA 3G All operators have very good web service success rate. MTN have high PS connection setup time
PS Connection setup is High in MTN compared to MOOV and CELTISS.
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 1
MOOV | 1
CELTISS | 1
Chart: PS Connection setup time
| PS Connection setup time
MTN | 0.0123
MOOV | 0.0065
CELTISS | 0.0028

## Slide 44: Benchmarking – DATA 3G All operators have good downlink and uplink FTP success rate
All operators MTN & MOOV & CELTISS satisfy ARCEP criteria of FTP success rate more than 80%.
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.996 | 0.9964
MOOV | 0.9983 | 0.9983
CELTISS | 1 | 0.9969

## Slide 45: Benchmarking – 3G FTP MEAN THROUGHPUT comparison map Excellent Throughput in MTN network and very close MOOV’s & CELTISS

## Slide 46: Benchmarking – 3G FTP MEAN THROUGHPUT comparison Excellent Throughput in MTN network compared to MOOV’s
MTN FTP DL AVERAGE Throughout is less than MOOV and CELTISS DL Throughout
DL Throughput mean for all operators satisfies ARCEP thresholds
MTN FTP UL AVERAGE Throughout is less than CELTISS UL Throughout
UL Throughput mean for all operators satisfy ARCEP thresholds
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 2200.6 | 1045.72 | 14352.9 | 15375.7
MOOV | 3337.54 | 1014.22 | 35717.8 | 11876.1
CELTISS | 4620.29 | 2151.61 | 18405.3 | 14601.4

## Slide 47: Benchmarking – 3G FTP THROUGHPUT comparison All operators MTN & MOOV & CELTISS satisfy ARCEP criteria reaching DL/UL Average throughputs target
Chart: FTP Throughput DL Mean Distribution (%)
| (Min,384) | (384,1000) | (1000,2000) | (2000,Max)
MTN | 0.003 | 0 | 0 | 0.997
MOOV | 0.0015 | 0 | 0 | 0.9985
CELTISS | 0 | 0 | 0 | 1
Chart: FTP Throughput UL Mean Distribution (%)
| (Min,144) | (144,512) | (512,1000) | (1000,Max)
MTN | 0.0011 | 0 | 0 | 0.9989
MOOV | 0 | 0 | 0 | 1
CELTISS | 0 | 0 | 0 | 1

## Slide 48: Benchmarking – 4G HTTP Browsing All operators have very good HTTP Browsing success rate
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 1
MOOV | 1
CELTISS | 1

## Slide 49: Benchmarking – 4G FTP THROUGHPUT comparison All operators have acceptable FTP success rate
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9967 | 0.9965
MOOV | 0.9984 | 1
CELTISS | 1 | 0.9984

## Slide 50: Benchmarking – 4G FTP THROUGHPUT comparison map MOOV’s average throughput DL rate is better than MTN’s & CELTISS’s

## Slide 51: Benchmarking – 4G FTP THROUGHPUT comparison MTN FTP DL AVERAGE Throughput is outperforming CELTISS’s. MTN FTP UL AVERAGE Throughput is outperforming MOOV’s & CELTISS
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 13142.8 | 15180.9 | 55606.77 | 36155.6
MOOV | 20806.2 | 9449.7 | 57707 | 28316.3
CELTISS | 11794.11 | 12408.7 | 14515.2 | 19711

## Slide 52: Benchmarking – BAND and TECHNOLOGY UTILISATION LTE MTN network uses mostly 2600 band MOOV’s uses both the 800 band and 2600 band CELTIS uses mostly 1800 band
Chart: 2G Band Distribution (%)
| GSM 900 | DSC 1800
MTN | 0.7519 | 0.2481
MOOV | 0.7443 | 0.2557
CELTISS | 0.2542 | 0.7458
Chart: 3G Band Distribution (%)
| 900 | 2100
MTN | 0.4803 | 0.5197
MOOV | 0.0444 | 0.9556
CELTISS | 0.0179 | 0.9821
Chart: 4G Band Distribution (%)
| LTE 800 | LTE 700 | LTE 1800 | LTE 2100 | LTE 2600
MTN | 0.0277 | 0.0286 | 0.0072 | 0.0306 | 0.9059
MOOV | 0.4948 | 0 | 0.0539 | 0.0004 | 0.4509
CELTISS | 0.0113 | 0 | 0.9887 | 0 | 0

## Slide 53
Next steps
07

## Slide 54: Next steps
Complete 2G & 3G drive tests: Remaining areas (north area of Benin)
Conduct deep analysis on drive tests results
Complete cross analysis on KPIs and OSS parameters with drive tests results and call traces
Issue final report and recommendations on February 10th, 2019

## Slide 55
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2019 Deloitte Bénin SARL. Société du réseau Deloitte