## Slide 1
Network QoS
Intermediate report
Octobre 30st, 2023

## Slide 2: Summary
Context & Report objectives | 03
Scope of Work | 05
Drive tests Activity, Current Status & Progress | 08
Executive Summary | 12
KPIs & Network settings Analysis | 18
Benchmarking on Cotonou area | 67
Next steps | 107

## Slide 3
Context & Report objectives
01

## Slide 4: Context & Report objectives
1
MTN Benin is a leading mobile operator in Benin with more than 60% market share.
2
It operates a network comprising of 675 2G, 3G and LTE sites across Benin.
3
MTN Benin wants an independent assessment and benchmarking of its radio network through drive tests
4
MTN Benin also wants to ascertain network assurance and capacities
Overview of the NW QoS assessment scope
A comprehensive drive testing exercise to determine customer perceived radio network quality of MTN Benin’s 2G, 3G and LTE network with that of the competition and the KPIs required by the regulator.
Formulate drive test methodology and coverage
Finalize reporting format and KPIs to be measured
Conduct drive tests for MTN Benin and competitor’s network
Validate results with MTN Benin’s radio planning team
Benchmark key KPIs between MTN, competition and regulator defined KPIs levels
Recommendations for network improvement
1
2
3
4
5
6
Detailed scope
Objectives of the assignment
2G/3G/4G MTN Networks KPIs audit based on OSS counters
Parameters settings audit of 2G/3G/4G MTN network
Capacity audit of 2G/3G/4G MTN network
Evaluate and benchmark Quality levels offered by MTN to MOOV mobiles networks and regulator defined KPIs levels based on Drive Test measurements results

## Slide 5
Scope of Work
02

## Slide 6: Scope of work (i/ii)
Conduct OSS Audit
  2G/3G/4G MTN Networks KPIs audit based on OSS counters
  Parameters settings audit of 2G/3G/4G MTN network
  Capacity audit of 2G/3G/4G MTN network
Hourly KPI review
HW / Alarms review
RAN Parameters
RAN Features
Neighbors
HW/licensing
Kick-off
Prerequisites
Data collection
Result analysis
Suggest Recommendations
audit report written
Presentation and actions
Close out report
Preparation
Early KPI
warning
Configuration Audit
Performance Analysis
Dimensioning
Reporting
Evaluate and benchmark Quality levels offered by MTN to MOOV mobiles networks and regulator’s defined KPIs levels based on Drive Test measurements results
  Voice service quality and SMS (one team with Drive test tool)
  3G Data FTP DL/UL and HTTP Browsing (one team with Drive test tool)
  4G Data FTP DL/UL and HTTP Browsing (one team with Drive test tool)
Drive Test execution
Post processing and report preparation
Kick-off
Prerequisites
Drive Test route preparation
Deep Analysis and
Recommendations
Presentation
Preparation
Network Data Collection
Post Processing
Events and layer 3 analysis
Reporting

## Slide 7: Scope of Work (ii/ii)
Cost
Cities to be covered
Cost
Drive Test KPI
Data KPIs (2G/3G/LTE)
HTTP IP-Service Access Success Ratio
HTTP Data Transfer Success Ratio
Session Setup time
HTTP mean data rate
FTP Session Success Rate
FTP UL/DL Throughput
Coverage rate (2G/3G/LTE)
Outoor Coverage rate
Indoor coverage rate
Incar coverage rate
Voice KPIs
Call blocking rate
Call drop rate
Call completetion success rate
Call completetion, with perfect quality, rate
Call completetion, with good quality, rate
Voice Quality (MOS)
SMS
MO SMS delivery success rate
MT SMS delivery success rate
19 indicators to analyze
18 thousand samples to analyze

## Slide 8
Drive tests Activity, Current Status & Progress
03

## Slide 9: Drive tests Activity, Current Status & Progress Drive test and Benchmark evaluation is on track according to initial plan
The Drive Test execution is ongoing as initially planned
We have processed more than 90% of Cotonou and SEME data

## Slide 10: Intermediate report
Scope of this report
1. A RAN network audit for MTN BENIN, aiming to identify weak points as well as suggests proposals to improve the network quality, and so the final user perception
  Current parameterization was analyzed and recommendations provided where appropriate, regarding RF environment, settings, design, etc.
  Analyzed cells which belong to:
    RNCs : HOERNC1 ,HOERNC2, BHERNC4 and DCERNC3
    BSCs : BHBSC05, BHEBSC6, DCBSC04, HOBSC02, HOBSC03.
  Network configuration and different performance measurements based on data from December 10th to 26th, 2018
  2. Network benchmarking results between MTN and MOOV on Cotonou area.

## Slide 11
Benchmarking Executive Summary
04

## Slide 12: Executive Summary – Benchmarking (2G)
2G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Coverage :
MTN coverage rate (99,97%) is closely comparable with its competitor's MOOV (99,99%) and CELTISS (99,97%)
All operators meets ARCEP 2G coverage obligation.
Voice service :
Accessibility: MTN is slightly lower than CELTISS and MOOV but meets ARCEP requirements,
All operators meets 2G ARCEP accessibility thresholds,
Retainability: MTN is slightly lower than MOOV and CELTISS.
All operators meets ARCEP 2G retainabilty requirements,
Integrity: MTN is slightly lower than MOOV and CELTISS,
MTN has the highest rate of 2G system utilization compared to competitors.
SMS service :
MTN is better than MOOV and lower than CELTISS.
All operators failed to meet ARCEP for SMS Send Success with End To End Delivery Time < 6 sec
For MTN Network it is recommended to reduce 2G system usage for voice service in order to improve voice quality,
It is recommended for MTN to reduce the GSM Half rate traffic,
MTN needs need to improve its SMS End To Delivery Time.

## Slide 13: Executive Summary - Benchmarking (3G) MTN network QoS is globally better than the MOOV’s. A design optimization can enable a better network QoS on all KPIs
3G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Coverage :
3G MTN coverage rate (99,55%) is comparable with its competitor's MOOV (99,21%) CELTISS (99,74%)
All operators meets ARCEP 3G coverage obligation.
Voice service :
Accessibility: MTN is better than MOOV and CELTISS.
All operators failed to meet ARCEP accessibility obligation
Retainability: : MTN is better than MOOV and slightly lower than CELTISS.
Only MTN and CELTISS meets ARCEP retainability obligation
Integrity: MTN is slightly lower than MOOV and CELTISS.
All operators meets ARCEP integrity obligation
SMS service :
MTN is better than MOOV and slightly lower than CELTISS.
All operators failed to meet ARCEP 3G coverage obligation.
Data service :
MTN throughput (DL:2,2M/UL:1,04M) is slightly lower than MOOV (DL:3,3M/UL:1,01M) and CELTISS (DL:4,6M/UL:4,1M) .
All operators meets ARCEP 3G throughput obligations.
RF optimization (Physical and logical) is needed to improve 3G MTN coverage.
Actions to improve accessibility are presented in the previous chapter

## Slide 14: Executive Summary - Benchmarking (4G) Ther 4G network coverage rate is comparable among all operators. MTN network mean throughput UL is better than MOOV’s and CELTISS’s. A Radio extension of the MTN network will enable outperforming competition’s 4G coverage and capacity
4G
TECHNOLOGY
KEY FINDINGS
KEY RECOMMENDATIONS
Coverage :
4G MTN coverage rate (99,28%) is comparable with MOOV’s (99,96%) and CELTISS’s (99,54)
All operators meets ARCEP 4G coverage obligation.
Data service :
MTN is ranked second in term of 4G DL throughput with 13.1Mbps, better than CELTISS 11.7Mbps and lower than MOOV 20.8Mbps,
MTN is ranked first in term of 4G UL throughput with 15.1Mbps against 9.4Mbps for MOOV and 12.4Mbps for CELTISS,
All operators meets ARCEP 4G End User Throughput obligation.
It is recommended to deploy more 4G sites in order to have a continuous 4G coverage; better than competitors,
By having the highest ratio of LTE 3CC utilization and Bandwidth and to outperform its competitors MTN needs to optimize 4G network.

## Slide 15: Benchmarking Key Results – Coverage MTN & MOOV & CELTISS have a close 2G /3G coverage but 4G coverage of MTN is lower than MOOV’s and CELTISS. 4G Network extension is needed in Cotonou to reach MOOV coverage
KPI |  | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
2G Coverage Rate | Incar | More than 70% with Incar: Rxlev >-87 dBm | 99,97% | OK | 99,99% | OK | 99,97% | OK | 2
 | Outdoor | More than 70% with Outdoor: Rxlev >-92 dBm | 99,70% | OK | 99,63% | OK | 99,74% | OK | 2
 | Indoor | More than 70% with Outdoor: Rxlev >-74 dBm |  |  |  |  |  |  | 
3G Coverage Rate | Incar | More than 90% with RSCP <-85 dBm | 96,00% | OK | 85,35% | NOK | 98,55% | OK | 2
 | Outdoor | More than 90% with RSCP <-85 dBm | 69,74% | OK | 70,00% | OK | 87,35% | OK | 3
 | Indoor | More than 90% with RSCP <-85 dBm |  |  |  |  |  |  | 
4G Coverage Rate | Incar | More than 60% with RSRP <-90 dBm* | 72,30% | OK | 93,34% | OK | 93,21% | OK | 3
 | Outdoor | More than 60% with RSRP <-95 dBm* | 72,86% | OK | 79,22% | OK | 85,92% | OK | 3
 | Indoor | More than 60% with RSRP <-78 dBm* |  |  |  |  |  |  | 

## Slide 16: Benchmarking Key Results – 2G/3G voice and SMS Summary MTN network in retainability CDR (%) meets ARCEP requirements, MTN is leading in accessibility but slightly exceeds ARCEP threshold, MTN needs to improve its Voice Quality MOS and SMS Send duration.
KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  | Value | Conformity | Value | Conformity | Value | Conformity | 
Accesibility: Blocking rate | <1% | 1,03% | NOK | 1,62% | NOK | 1,77 | NOK | 1
Retainability: Call drop rate | <1% | 0,46% | OK | 2,21% | NOK | 0,33% | OK | 2
Call Completetion Rate (%) | NA | 98,54% |  | 96,17% |  | 98,00% |  | 1
Integrity: Voice quality | Note requise> 2,8 | 3,66 | OK | 3,85 | OK | 3,94 | OK | 3
SMS sending success rate % (E2E delivery Time<6 sec) | >99% | 92,50% | NOK | 80,59% | NOK | 95,01% | NOK | 2
SMS receving success rate % | >99% | 96,87% | NOK | 96,30% | NOK | 97,66% | NOK | 2

## Slide 17: Benchmarking Key Results – 3G Data Summary MTN network in 3G DATA meets ARCEP requirements, MTN needs to improve its 3G Data THP compared to competitors.
Services | KPI | ARCEP Threshorlds | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
3G DATA | 3G Availabaility | >=95% | 99,21% | OK | 99,70% | OK | 99,12% | OK | 2
3G HTTP | Successful internet connexion rate | >90% | 100,00% | OK | 100,00% | OK | 100,00% | OK | 1
 | Connexion setup time | <=30sec | 1,23 | OK | 0,65 | OK | 0,28 | OK | 3
 | Web service failure rate | <10% | 0,00% | OK | 0,00% | OK | 0% | OK | 1
3G FTP | FTP failure rate UL/DL | <20 % | 0,40%/0,36% | OK | 0,17%/0,17% | OK | 0%/0,31% | OK | 3
 | FTP Data transmission average (DL) | >= 2Mbps | 2200,6 | OK | 3337,54 | OK | 4620,2 | OK | 3
 | FTP Data transmission average (UL) | >= 1Mbps | 1045,72 | OK | 1014,22 | OK | 2151,61 | OK | 2

## Slide 18: Benchmarking Key Results – 4G Data Summary MTN’s 4G DATA End User KPIs satisfy ARCEP requirements, MTN is ranked second in 4G DL THP after MOOV’s , MTN is outperforming MOOV’s & CELTISS in 4G UL THP.
Services | KPI | Threshorlds* | MTN |  | MOOV |  | CELTISS |  | MTN Ranking
 |  |  | Value | Conformity | Value | Conformity | Value | Conformity | 
4G HTTP Browsing | Web service failure rate (%) | <10% | 0,00% | OK | 0,00% | OK | 0,00% | OK | 1
 | Connexion setup time | <=10sec | 0,32 | OK | 0,37 | OK | 0,12 | OK | 2
4G FTP | FTP failure rate UL/DL | <10 % | 0,33%/0,35% | OK | 0,16%/0% | OK | 0%/0,16% | OK | 3
 | FTP Data transmission average (DL) | 4G >= 10 Mbps | 13142,8 | OK | 20806,2 | OK | 11794,11 | OK | 2
 | FTP Data transmission average (UL) | 4G: >= 4Mbps | 15180,9 | OK | 9449,7 | OK | 12408,7 | OK | 1

## Slide 19
Benchmarking 2G/3G/4G coverage
04

## Slide 20: Benchmarking: 2G coverage MTN, MOOV and CELTISS’s 2G coverage meets ARCEP RxLev thresholds,
Chart: RxLev Distribution (%)
| -74 to -10 | -87 to -74 | -92 to -87 | -110 to -92 | ACCEPTABLE COVREGE
MTN | 0.9458 | 0.0539 | 0.0003 | 0 | 0.9997
MOOV | 0.95 | 0.0499 | 0 | 0 | 0.9999
CELTISS | 0.9859 | 0.0138 | 0.0003 | 0 | 0.9997

## Slide 21: Benchmarking: 2G coverage - Maps MTN’s 2G coverage is very close to MOOV’s CELTISS’S 2G coverage outperforming MTN’s and MOOV’s

## Slide 22: Benchmarking: 3G coverage MTN’s 3G coverage meets ARCEP requirements and closely similar with competitors.
99.55% of DT 3G MTN Samples showing a good RSCP more than -86 which is satisfying ARCEP’s criteria
Chart: RSCP Distribution (%)
| -86 to -5 | -94 to -86 | -110 to -94 | ACCEPTABLE COVREGE
MTN | 0.9681 | 0.0274 | 0.0044 | 0.9955
MOOV | 0.8535 | 0.1386 | 0 | 0.9921
CELTISS | 0.9855 | 0.0119 | 0.0026 | 0.9974

## Slide 23: Benchmarking: 3G coverage-Maps MTN’s 3G coverage is outperforming MOOV’s 3G coverage MTN’s 3G coverage is very close to CELTISS’s

## Slide 24: Benchmarking: 4G coverage MTN's 4G Radio coverage rate (99.28%) is very close to MOOV's (99.96%) and CELTISS’s (99.54%) coverage,
Chart: RSRP Distribution (%)
| -85 to -5 | -90 to -85 | -105 to -90 | -120 to -105 | GOOD RSRP
MTN | 0.4749 | 0.2481 | 0.2698 | 0.0073 | 0.9928
MOOV | 0.6948 | 0.2386 | 0.0662 | 0.0003 | 0.9996
CELTISS | 0.8417 | 0.0904 | 0.0633 | 0.0045 | 0.9954

## Slide 25: Benchmarking – 4G coverage - Maps CELTISS’s 4G coverage is outperforming MTN’s and MOOV’s

## Slide 26
Benchmarking voice service
04

## Slide 27: Benchmarking: CS Accessibility 2G/3G BLOCKED CALLS MTN has the best accessibility to voice service compared to competitors, MTN exceeds slightly ARCEP requirements.
Chart: Call Setup SR(%) and Call Blocked Rate per Technology (%)
| 2G | 3G | 2G | 3G | 2G | 3G | MTN | MOOV | CELTISS
CSSR (%) | 0.9961 | 0.9936 | 0.9975 | 0.9863 | 1 | 0.9923
CBR (%) | 0.0039 | 0.0064 | 0.0025 | 0.0137 | 0 | 0.0177

## Slide 28: Benchmarking: CS Retainability 2G/3G DROPPED CALLS MTN and CELTISS satisfy ARCEP thresholds regarding Call Drop Rate.
Chart: Call Drop Rate (%)
| CDR (%)
MTN | 0.0046
MOOV | 0.0221
CELTISS | 0.0038
Chart: Call Drop Rate per Technology (%)
| 2G | 3G | 2G | 3G | 2G | MTN | MOOV | CELTISS
CDR (%) | 0.0023 | 0.0023 | 0 | 0.0221 | 0.0018

## Slide 29: Benchmarking: Voice service System Technology usage(%) MTN has 40% of voice calls carried by 2G, CELTISS and MOOV have more than 98% of voice calls carried by 3G, Recommended for MTN to reduce 2G utilization and increase 3G penetration for better audio quality.
Chart: Voice System Technology usage(%)
| GSM | UMTS
MTN | 0.4029 | 0.5971
MOOV | 0.0101 | 0.9899
CELTISS | 0 | 1

## Slide 30: Benchmarking Voice service Band usage(%) MTN's 2G band usage: 76,57% GSM 900 and 23,43% GSM 1800 Mhz, 3G band usage: MTN uses mainly UMTS2100, CELTISS uses mainly UMTS900 and MOOV has an equitable utilization for both bands U2100 and U900.
Chart: 2G band usage(%)
| GSM 900 | GSM 1800
MTN | 0.7657 | 0.2343
MOOV | 1 | 0
CELTISS | 0.0113 | 0
Chart: 3G band usage(%)
| UMTS 900 | UMTS 2100
MTN | 0.54 | 0.46
MOOV | 0.33 | 0.77
CELTISS | 0.802 | 0.198

## Slide 31: Benchmarking: CS Integrity Voice quality Mean Opinion Score CELTISS has the best ratio of excellent and good Voice Quality samples compared to MTN’s and MOOV’S,MTN needs to improve its voice quality MOS.
Chart: Voice Quality Distribution (%)
| Excellent | Good | Poor | Bad | Exc+Good
MTN | 0.3525 | 0.535 | 0.0721 | 0.0405 | 0.8875
MOOV | 0.782 | 0.1652 | 0.0305 | 0.0223 | 0.9472
CELTISS | 0.6471 | 0.3411 | 0.0076 | 0.0042 | 0.9882
Chart: 
| MTN | MOOV | CELTISS
Average MOS | 3.66 | 3.85 | 3.94

## Slide 32: Benchmarking – CS Integrity Voice quality maps (MOS) MTN has a high percentage of MOS samples lower than 2.2, High risk of mute calls and audio interruptions for MTN.

## Slide 33: Benchmarking – Voice quality MOS by System technology Voice Quality MOS by technology
Chart: 2G Voice Quality Distribution (%)
| (min;1,5) | (1,5;2,5) | (2,5;3,5) | (3,5;max)
MTN | 0.0325 | 0.1128 | 0.4971 | 0.3572
MOOV | 0.0272 | 0.0607 | 0.3333 | 0.5786
CELTISS | 0.0059 | 0.0202 | 0.3185 | 0.6553
Chart: 3G Voice Quality Distribution (%)
| (min;1,5) | (1,5;2,5) | (2,5;3,5) | (3,5;max)
MTN | 0.0325 | 0.1128 | 0.4971 | 0.3572
MOOV | 0.0272 | 0.0607 | 0.3333 | 0.5786
CELTISS | 0.0059 | 0.0202 | 0.3185 | 0.6553

## Slide 34: Benchmarking: Voice quality 2G Codec Rate distribution MTN has a high percentage of GSM Half rate usage(%), Several 2G codec rate was detected for MTN’s Network (WB, NB), MTN needs to define the default codec.
Chart: MTN 2G codec distribution(%)
| GSM HR NB 7.4 | GSM WB 12.65 | GSM FR NB 12.2 | GSM WB 6.6 | GSM FR NB 7.4 | GSM CCCH | GSM HR NB 5.9 | GSM WB 8.85 | GSM SDCCH | GSM HR NB 4.75 | GSM FR NB 5.9 | GSM FR NB 4.75 | GSM TCH EFR
Usage(%) | 0.21493 | 0.15415 | 0.11887 | 0.1037 | 0.098594 | 0.09019 | 0.077031 | 0.056781 | 0.038486 | 0.01987 | 0.013043 | 0.0088119 | 0.0055439
Chart: MOOV 2G codec distribution(%)
| GSM CCCH | GSM TCH EFR | GSM SDCCH | GSM | GSM FRNB 12.2 | GSM FRNB 7.4 | GSM HR NB 7.4 | GSM FRNB 5.9 | GSM FRNB 4.75 | GSM HR NB 4.75 | GSM HR NB 5.9
codec usage (%) | 0.33779 | 0.18694 | 0.16613 | 0.1539 | 0.087837 | 0.020432 | 0.019477 | 0.012221 | 0.0078289 | 0.0055375 | 0.0019095
Chart: CELTISS 2G codec usage(%)
| GSM FR NB 12.2 | GSM FR NB 5.9 | GSM CCCH | GSM SDCCH | GSM | GSM FR NB 7.4 | GSM FR NB 4.75
codec usage(%) | 0.38056 | 0.25796 | 0.14413 | 0.10122 | 0.064913 | 0.0473 | 0.0039225

## Slide 35: Benchmarking: Voice quality 3G Codec Rate distribution AMR WB HD-voice is activated in MTN’s and CELTISS’s Network, AMR WB 12,65 is the maily used codec for MTN, MTN needs to define AMR-WB 12,65 as default codec.
Chart: MTN 3G codec distibution (%)
| UMTS FDD NB 12.2 | UMTS FDD WB 12.65 | UMTS FDD WB 6.6 | UMTS FDD WB 8.85
Usage(%) | 0.079108 | 0.62391 | 0.11823 | 0.17876
Chart: MOOV 3G codec distribution (%)
| UMTS FDD NB 10.2 | UMTS FDD NB 12.2 | UMTS FDD NB 4.75 | UMTS FDD NB 5.15 | UMTS FDD NB 5.9 | UMTS FDD NB 6.7 | UMTS FDD NB 7.4 | UMTS FDD NB 7.95
Usage(%) | 0.006552 | 0.96396 | 0.005733 | 0.007371 | 0.003276 | 0.003276 | 0.004914 | 0.004914
Chart: CELTISS 3G codec usage (%)
| UMTS FDD NB 12.2 | UMTS FDD WB 12.65
codec usage(%) | 0.74594 | 0.25406

## Slide 36: Benchmarking Voice quality 3G MOS by Codec Rate AMR WB HD-voice is activated in MTN’s and CELTISS’s Network, MTN needs to define AMR-WB 12,65 as principal codec.
Chart: MTN 3G MOS By codec Rate
| UMTS FDD NB 12.2 | UMTS FDD WB 12.65 | UMTS FDD WB 6.6 | UMTS FDD WB 8.85
codec rate | 3.867 | 3.9 | 3.318 | 3.553
Chart: MOOV 2G MOS By codec Rate
| UMTS FDD NB 12.2
3G Average MOS By codec rate | 3.974
Chart: CELTISS 2G MOS By codec Rate
| UMTS FDD NB 12.2 | UMTS FDD WB 12.65
Average | 3.936 | 4.184

## Slide 37: Benchmarking – Voice quality 2G MOS by Codec Rate
Chart: MTN 2G MOS By codec Rate
| GSM AHS NB 7.4 | GSM AHS WB 12.65 | GSM TCH EFR | GSM TCH EFR NB 7.4 | GSM WFS | GSM WFS WB 12.65 | GSM WFS WB 6.6 | GSM WFS WB 8.85
2G MOS | 3.423 | 3.084 | 4.078 | 3.657 | 2.348 | 3.208 | 3.05 | 2.913
Chart: MOOV 2G MOS By codec Rate
| GSM AFS NB 12.2 | GSM AFS NB 7.4 | GSM AHS NB 7.4 | GSM TCH EFR
2G Average MOS By codec rate | 3.807 | 3.432 | 3.19 | 3.689
Chart: CELTISS 2G MOS By codec Rate
| GSM AFS | GSM AFS NB 12.2 | GSM AFS NB 4.75 | GSM AFS NB 5.9 | GSM AFS NB 7.4 | GSM AHS NB 7.4
Average | 3.984 | 3.869 | 3.32 | 3.27 | 3.885 | 3.597
MTN: 2G main used codec rate: GSM AHS NB 7.4 and GSM TCH EFR,
MTN needs to reduce 2G technology usage in order to improve voice quality MOS.

## Slide 38: Benchmarking: Radio parameters EC/NO comparison 12,35% of drive test samples are showing a very low level of EcNo for 3G MTN network. A physical design optimization is needed to improve Ec/No.
Chart: Ec/No Distribution (%)
| -8 to 0 | -12 to -8 | -16 to -8 | -34 to -16 | Good Ec/No
MTN | 0.1235 | 0.2046 | 0.5191 | 0.1528 | 0.3281
MOOV | 0.3576 | 0.3462 | 0.2594 | 0.0368 | 0.7038
CELTISS | 0.8306 | 0.1467 | 0.0189 | 0.0038 | 0.9773

## Slide 39: Benchmarking: Radio parameters EC/NO 3G MOOV’s and CELTISS’s Quality is outperforming MTN’s. MTN network design needs to be optimized and improve Ec/No.

## Slide 40: Benchmarking – SNIR comparison map 4G CELTISS Signal of quality is outperforming MTN’s and MOOV’s

## Slide 41: Benchmarking – SNIR comparison Drive tests are showing a low level of MTN Network SINR.
Chart: SINR Comparison
| (Min,-4) | (-4,0) | (0,7) | (7,15) | (15,20) | Good SINR
MTN | 0.0362 | 0.1531 | 0.4603 | 0.255 | 0.0735 | 0
MOOV | 0.0878 | 0.3154 | 0.3141 | 0.2102 | 0.0548 | 0
CELTISS | 0.0129 | 0.0459 | 0.2355 | 0.5299 | 0.1233 | 0

## Slide 42: Benchmarking – BLOCKED CALLS EVENTS map All operators MTN & MOOV & CELTISS are not satisfying ARCEP CSSR/CBR requirements

## Slide 43: Benchmarking – CALL SETUP TIME/Call Mode MTN has the best 4G CSBF Call setup Time, MTN needs to reduce 2G technology usage.
Chart: CS Call Setup Time By Technology (s)
| 4G CSFB CST | 3G CST | 2G CST
MTN | 6.834 | 6.538 | 7.147
MOOV | 8.568 | 10.28 | 6.67
CELTISS | 8.271 | 6.991
Chart: Call mode distribution (%)
| MTN | MOOV | CELTISS
4G CSFB | 0.62354 | 0.98792 | 0.99617
3G | 0.003881 | 0.009396 | 0.0038265
2G | 0.37257 | 0.0026846 | 0

## Slide 44: Benchmarking – HANDOVER FAILURE EVENTS map

## Slide 45: Benchmarking – Mobility -HANDOVER SR(%) MTN has the best performance in term of mobility,
Chart: Handover Success Rate (%)
| HSR (%)
MTN | 0.996
MOOV | 0.793
CELTISS | 0.995

## Slide 46: Benchmarking – DROPPED CALLS EVENTS map Voice Session Continuity of MTN and CELTISS network is outperforming MOOV’s

## Slide 47: Benchmarking – SMS SENDING FAILURE EVENTS map CELTISS SMS SETUP/RESPONSE is much better than MTN’s & MOOV’s

## Slide 48: Benchmarking – SMS SENDING FAILURE CELTISS SMS SETUP/RESPONSE is outperforming MTN’s & MOOV’s. SMS service KPIs of the three operators are not compliant with the ARCEP requirements
Chart: SMS SR(%)
| SMS Sending message success rate (%) | SMS Receving message success rate (%)
MTN | 0.925 | 0.9687
MOOV | 0.8059 | 0.963
CELTISS | 0.9501 | 0.9766
Chart: MTN SMS Send Time Distribution (%)
| (0,3) | (3,6) | >6
MTN | 0.2916 | 0.6334 | 0.075

## Slide 49
Benchmarking Data service
04

## Slide 50: Benchmarking – DATA 3G All operators have a good rate of successful Internet connection
Chart: PS Attach & PDP Contex Act(%)
| PS Attach success(%) | PS Attach fail (%) | PDP Context Act Success (%) | PDP Context Act fail (%)
MTN | 1 | 0 | 1 | 0
MOOV | 1 | 0 | 1 | 0
CELTISS | 1 | 0 | 0.9992 | 0.0008
Chart: Attach & PDP Activation Time (s)
| PS Attach Setup Time | PDP Context Act Time
MTN | 3.22 | 1.37
MOOV | 2.97 | 1.41
CELTISS | 3.34 | 1.46

## Slide 51: Benchmarking – DATA 3G All operators have very good web service success rate. MTN have high PS connection setup time
PS Connection setup is High in MTN compared to MOOV and CELTISS.
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 1
MOOV | 1
CELTISS | 1
Chart: PS Connection setup time
| PS Connection setup time
MTN | 0.0123
MOOV | 0.0065
CELTISS | 0.0028

## Slide 52: Benchmarking – DATA 3G All operators have good downlink and uplink FTP success rate
All operators MTN & MOOV & CELTISS satisfy ARCEP criteria of FTP success rate more than 80%.
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.996 | 0.9964
MOOV | 0.9983 | 0.9983
CELTISS | 1 | 0.9969

## Slide 53: Benchmarking – 3G FTP MEAN THROUGHPUT Excellent Throughput in MTN network compared to MOOV’s
MTN FTP DL AVERAGE Throughout is less than MOOV and CELTISS DL Throughout
DL Throughput mean for all operators satisfies ARCEP thresholds
MTN FTP UL AVERAGE Throughout is less than CELTISS UL Throughout
UL Throughput mean for all operators satisfy ARCEP thresholds
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 2200.6 | 1045.72 | 14352.9 | 15375.7
MOOV | 3337.54 | 1014.22 | 35717.8 | 11876.1
CELTISS | 4620.29 | 2151.61 | 18405.3 | 14601.4

## Slide 54: Benchmarking – 3G FTP MEAN THROUGHPUT comparison map Excellent Throughput in MTN network and very close MOOV’s & CELTISS

## Slide 55: Benchmarking – 3G FTP THROUGHPUT comparison All operators MTN & MOOV & CELTISS satisfy ARCEP criteria reaching DL/UL Average throughputs target
Chart: FTP Throughput DL Mean Distribution (%)
| (Min,384) | (384,1000) | (1000,2000) | (2000,Max)
MTN | 0.003 | 0 | 0 | 0.997
MOOV | 0.0015 | 0 | 0 | 0.9985
CELTISS | 0 | 0 | 0 | 1
Chart: FTP Throughput UL Mean Distribution (%)
| (Min,144) | (144,512) | (512,1000) | (1000,Max)
MTN | 0.0011 | 0 | 0 | 0.9989
MOOV | 0 | 0 | 0 | 1
CELTISS | 0 | 0 | 0 | 1

## Slide 56: Benchmarking – 4G HTTP Browsing All operators have very good HTTP Browsing success rate
Chart: HTTP Browsing Success Rate (%)
| HTTP Browsing Success rate (%)
MTN | 1
MOOV | 1
CELTISS | 1

## Slide 57: Benchmarking – 4G FTP THROUGHPUT comparison All operators have acceptable FTP success rate
Chart: FTP Success Rate (%)
| FTP Success DL (%) | FTP Success UL (%)
MTN | 0.9967 | 0.9965
MOOV | 0.9984 | 1
CELTISS | 1 | 0.9984

## Slide 58: Benchmarking – 4G FTP THROUGHPUT comparison MTN FTP DL AVERAGE Throughput is outperforming CELTISS’s. MTN FTP UL AVERAGE Throughput is outperforming MOOV’s & CELTISS
Chart: FTP Throughput (Kbps)
| App_Throughpout_DL | App_Throughpout_UL | Max_App_Throughpout_DL | Max_App_Throughpout_UL
MTN | 13142.8 | 15180.9 | 55606.77 | 36155.6
MOOV | 20806.2 | 9449.7 | 57707 | 28316.3
CELTISS | 11794.11 | 12408.7 | 14515.2 | 19711

## Slide 59: Benchmarking – 4G FTP THROUGHPUT comparison map MOOV’s average throughput DL rate is better than MTN’s & CELTISS’s

## Slide 60: Benchmarking – BAND and TECHNOLOGY UTILISATION LTE MTN network uses mostly 2600 band MOOV’s uses both the 800 band and 2600 band CELTIS uses mostly 1800 band
Chart: 3G Band Distribution (%)
| 900 | 2100
MTN | 0.4803 | 0.5197
MOOV | 0.0444 | 0.9556
CELTISS | 0.0179 | 0.9821
Chart: 4G Band Distribution (%)
| LTE 800 | LTE 700 | LTE 1800 | LTE 2100 | LTE 2600
MTN | 0.0277 | 0.0286 | 0.0072 | 0.0306 | 0.9059
MOOV | 0.4948 | 0 | 0.0539 | 0.0004 | 0.4509
CELTISS | 0.0113 | 0 | 0.9887 | 0 | 0

## Slide 61: Benchmarking – Data TECHNOLOGY Usage(%) MTN has the highest LTE CA Carrier Aggregation usage, HSDPA-DC not used for MTN, To improve 3G Throughput MTN needs to increase DC-HSPA utilization.
Chart: 3G Packet Technology Usage(%)
| DC-HSPA | HSDPA | UMTS | HSPA
MTN | 0 | 0.0041123 | 0.60442 | 0.39309
MOOV | 0.52078 | 0.0073002 | 0.060573 | 0.41134
CELTISS | 0.49491 | 0.02656 | 0.026924 | 0.45161
Chart: 4G Packet Technology Usage (%)
| LTE CA | LTE FDD
MTN | 0.78334 | 0.21666
MOOV | 0.58263 | 0.41737
CELTISS | 0.50199 | 0.49801

## Slide 62: Benchmarking – Data 4G Carrier Aggregation Usage(%) MTN has the highest LTE CA Carrier Aggregation 3CC usage 70.5% against 23.59% for MOOV and 0% for CELTISS, MTN needs to optimize 4G Network to get the first position in term of DL THP, CELTISS’s Network, LTE CA 3CC not activated.
Chart: MTN - Carrier aggregation usage (%)
| 3CC | 2CC | LTE
 | 0.705 | 0.1034 | 0.1915
Chart: MOOV - Carrier aggregation usage (%)
| 3CC | 2CC | LTE
 | 0.2359 | 0.6294 | 0.1347
Chart: CELTISS - Carrier aggregation usage (%)
| 2CC | LTE
 | 0.6294 | 0.1347

## Slide 63: Benchmarking – Data 4G Bandwidth Usage(%) MTN has the highest LTE Bandwidth, LTE BW: 50 MHz for MTN against 30 MHz for MOOV and 30MHz for CELTISS.
Chart: MTN-LTE Bandwidth (MHz )
| Bandwidh
LTE 800 | 10
LTE 1800 | 10
LTE 2100 | 10
LTE 2600 | 20
Chart: CELTISS-LTE Bandwidh (MHz)
| Bandwidh
LTE 800 | 10
LTE 1800 | 20
Chart: MOOV-LTE Bandwidth (MHz)
| Bandwidh
LTE 800 | 10
LTE 1800 | 10
LTE 2600 | 20

## Slide 64
Next steps
07

## Slide 65: Next steps
Complete 2G & 3G drive tests: Remaining areas (north area of Benin)
Conduct deep analysis on drive tests results
Complete cross analysis on KPIs and OSS parameters with drive tests results and call traces
Issue final report and recommendations on February 10th, 2019

## Slide 66
Deloitte fait référence à un ou plusieurs cabinets membres de Deloitte Touche Tohmatsu Limited, société de droit anglais (« private company limited by guarantee »), et à son réseau de cabinets membres constitués en entités indépendantes et juridiquement distinctes. Pour en savoir plus sur la structure légale de Deloitte Touche Tohmatsu Limited et de ses cabinets membres, consulter www.deloitte.com/about.
Fort d’un réseau de firmes membres dans plus de 150 pays, Deloitte allie des compétences de niveau international à des expertises locales pointues, afin d’accompagner ses clients dans leur développement partout où ils opèrent. Nos 264 000 professionnels sont animés par un objectif commun, faire de Deloitte la référence en matière d’excellence de service.
Au Bénin, Deloitte mobilise un ensemble de compétences diversifiées pour répondre aux enjeux de ses clients, de toutes tailles et de tous secteurs – des grandes entreprises multinationales aux microentreprises locales, en passant par les entreprises moyennes.
Le présent document et ses annexes sont confidentiels et réservés à l’usage interne exclusif du destinataire. Toute reproduction ou toute divulgation partielle ou totale à des tiers en est interdite, sauf accord écrit préalable de Deloitte Bénin.
© 2019 Deloitte Bénin SARL. Société du réseau Deloitte